## Slide 1
The Fast Fourier Transform (FFT)
and MATLAB Examples

## Slide 2
Learning Objectives
Discrete Fourier transforms (DFTs) and their relationship
to the Fourier transforms
Implementation issues with the DFT via the FFT
sampling issues (Nyquist criterion)
resolution in the frequency domain (zero padding)
neglect of negative frequency components

## Slide 3
These Fourier integral pairs normally are performed
numerically by sampling the time and frequency
domain functions at discrete values of time and
frequency and then using the discrete Fourier transforms
to relate the sampled values

## Slide 4
Fast Fourier Transform
Discrete Fourier Transform
… time window sampled with N points
… sampling time interval

## Slide 5
As with the Fourier transforms, there are different choices
made for the Discrete Fourier transform pairs. In general, we
could write:
as long as
The indexing could also go from
1 to N instead of 0 to N-1
Fast Fourier Transform

## Slide 6
These discrete Fourier Transforms can be implemented
rapidly with the Fast Fourier Transform (FFT) algorithm
Fast Fourier Transform
FFTs are most efficient if the number of samples, N, is
a power of 2. Some FFT software implementations require this.
N | (N-1)2 | (N/2)log2N
256 | 65,025 | 1,024
1,024 | 1,046,529 | 5,120
4,096 | 16,769,025 | 24,576

## Slide 7
Mathematica
Fourier[{a1,a2,…,aN}]
InverseFourier[{b1,b2,…,bN}]
lists
Maple
FFT(N, xre, xim)
N = 2n
iFFT(N,Xre,Xim)
MATLAB
arrays
fft(x)
ifft(X)
arrays
Fast Fourier Transform

## Slide 8
FFT function
Fast Fourier Transform
function y = FourierT(x, dt)
% FourierT(x,dt) computes forward FFT of x with sampling time interval dt
% FourierT approximates the Fourier transform where the integrand of the
% transform is x*exp(2*pi*i*f*t)
% For NDE applications the frequency components are normally in MHz,
% dt in microseconds
[nr, nc] = size(x);
if nr == 1
N = nc;
else
N = nr;
end
y = N*dt*ifft(x);

## Slide 9
inverse FFT function
Fast Fourier Transform
function y = IFourierT(x, dt)
% IFourierT(x,dt) computes the inverse FFT of x, for a sampling time interval dt
% IFourierT assumes the integrand of the inverse transform is given by
% x*exp(-2*pi*i*f*t)
% The first half of the sampled values of x are the spectral components for
% positive frequencies ranging from 0 to the Nyquist frequency 1/(2*dt)
% The second half of the sampled values are the spectral components for
% the corresponding negative frequencies. If these negative frequency
% values are set equal to zero then to recover the inverse FFT of x we must
% replace x(1) by x(1)/2 and then compute 2*real(IFourierT(x,dt))
[nr,nc] = size(x);
if nr == 1
N = nc;
else
N = nr;
end
y =(1/(N*dt))*fft(x);

## Slide 10
if
Nyquist
criterion
T
-T
tmax
fs
-fs
fmax
vp(t)
| Vp(f) |
N samples
N samples
Fast Fourier Transform
vp and Vp in the discrete Fourier transforms are periodic functions.
How do we guarantee these represent non-periodic pulses?

## Slide 11
The use of linspace and s_space functions for FFTs
and inverse FFTs
T =1.0
In the example above N = 8, T = 1.0 so
>> t = linspace(0,1, 8);
>> dt = t(2) -t(1)
dt = 0.1429

## Slide 12
To get the proper sampled values and the correct t we can use the alternate function s_space (it’s on the ftp site)
>> t = s_space(0,1, 8);
>> dt = t(2)-t(1)
dt = 0.1250
>> t = linspace(0,1, 512);
>> dt = t(2) - t(1)
dt = 0.0020
>> t = s_space(0,1, 512);
>> dt = t(2) - t(1)
dt = 0.0020

## Slide 13
When you are using many points the difference is not large if we use either linspace or s_space but the difference is still there
>> format long
>> t = linspace(0, 1, 500);
>> dt = t(2) -t(1)
dt = 0.00200400801603
>> t = s_space(0, 1, 500);
>> dt = t(2) -t(1)
dt = 0.00200000000000

## Slide 14
T
v (t)
N samples
2T
v (t)
2N samples
fs = 1/t
| V (f) |
N samples
f
f =1/T
t
fs = 1/t
| V (f) |
2N samples
t
f =1/2T
f
zero “padding”
Fast Fourier Transform

## Slide 15
>> t =s_space(0, 4, 16);
>> v = t.*(t < 0.5) + (1-t).*(t >= 0.5 & t<=1.0);
>> h = plot(t, v, 'ko');
>> set(h, 'MarkerFaceColor', 'k')
>> axis([ 0 4 0 0.6])
>> dt = t(2) - t(1)
dt = 0.2500
0
0.5
1
1.5
2
2.5
3
3.5
4
0
0.1
0.2
0.3
0.4
0.5
Zero padding example

## Slide 16
>> f =s_space(0, 1/dt, 16);
>> vf = FourierT(v, dt);
>> h = plot(f, abs(vf), 'ko');
>>axis([ 0 4 0 0.3])
>> set(h, 'MarkerFaceColor', 'k')
>> df = f(2) - f(1)
df = 0.2500
0
0.5
1
1.5
2
2.5
3
3.5
4
0
0.05
0.1
0.15
0.2
0.25

## Slide 17
>> vt2 =[v, zeros(1,16)];
>> vf2 = FourierT(vt2, dt);
>> h = plot(f, abs(vf2), 'ko');
??? Error using ==> plot
Vectors must be the same lengths.
>> f =s_space(0, 1/dt, 32);
>> h = plot(f, abs(vf2), 'ko');
>> set(h, 'MarkerFaceColor', 'k')
>>axis([ 0 4 0 0.3])
could also use
vt2 = padarray(v,[0, 16], 0, ‘post’);
>> df=f(2) - f(1)
df = 0.1250
half the former df
same sampling frequency
Now, pad the original signal with zeros
0
0.5
1
1.5
2
2.5
3
3.5
4
0
0.05
0.1
0.15
0.2
0.25

## Slide 18
>> t =s_space(0, 4, 512);
>> v = t.*(t < 0.5) + (1-t).*(t >= 0.5 & t<=1.0);
>> dt = t(2) -t(1)
dt = 0.0078
>> fs =1/dt
fs = 128
>> f =s_space(0, fs, 512);
>> vf =FourierT(v, dt);
>> plot(f, abs(vf))
Now, use a much higher sampling frequency
0
20
40
60
80
100
120
140
0
0.05
0.1
0.15
0.2
0.25

## Slide 19
>> h = plot(f(1:20), abs(vf(1:20)), 'ko');
>> set(h, 'MarkerFaceColor', 'k')
To see the frequency spectrum on a finer scale
0
1
2
3
4
5
0
0.05
0.1
0.15
0.2
0.25
Note: we had some aliasing before

## Slide 20
>> vt =IFourierT(vf, dt);
>> plot(t, real(vt))
If we do the inverse FFT we do again recover the time function
0
0.5
1
1.5
2
2.5
3
3.5
4
-0.1
0
0.1
0.2
0.3
0.4
0.5
0.6

## Slide 21
We can do multiple FFTs or IFFTs
all at once if we place the data in columns
>> t =s_space(0, 4, 16);
>> v = t.*(t < 0.5) + (1-t).*(t >= 0.5 & t<=1.0);
>> dt = t(2) - t(1);
>> mv= [ v' v' v'];
>> mvf = FourierT(mv, dt);
>> vf1 = mvf(:,1);
>> f = s_space(0, 1/dt, 16);
>> h = plot(f, abs(vf1)', 'ko')
>> set(h, 'MarkerFaceColor', 'k')
0
0.5
1
1.5
2
2.5
3
3.5
4
0
0.05
0.1
0.15
0.2
0.25

## Slide 22
Note that even though there is aliasing here if we do the inverse FFT of these samples we do recover the original time samples:
>> v1 =IFourierT(vf1,dt);
>> h=plot(t, real(v1), 'ko');
>> set(h, 'MarkerFaceColor', 'k')
0
0.5
1
1.5
2
2.5
3
3.5
4
-0.1
0
0.1
0.2
0.3
0.4
0.5
0.6

## Slide 23
Fast Fourier Transform
FFT Examples using the function:
function y = pulse_ref(A,F,N, t)
y = A*(1 -cos(2*pi*F*t./N)).*cos(2*pi*F*t).*(t >= 0 & t <= N/F);
A … controls the amplitude
F … controls the dominant frequency in the pulse
N … controls the number of cycles (amount of "ringing")
in the pulse and hence the bandwidth
MATLAB function:

## Slide 24
>> t = s_space(0,5,512);
>> dt = t(2)- t(1)
dt = 0.0098
>> y=pulse_ref(1,5,3,t);
>> plot(t, y)
>> yf1=FourierT(y,dt);
>> f=s_space(0, 1/dt, 512);
>> f(end)
ans = 102.2000
>> plot(f, abs(yf1))
Frequency spectrum for relatively wideband pulse
if t is in sec
f is in MHz
sampling
frequency
Nyquist frequency
= ½ sampling
frequency
0
1
2
3
4
5
-2
-1
0
1
2
0
20
40
60
80
100
120
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35

## Slide 25
>> plot(f(1:100), abs(yf1(1:100)))
Expanded view
0 – 20 MHz
0
2
4
6
8
10
12
14
16
18
20
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35
0
0.5
1
1.5
2
2.5
3
3.5
4
4.5
5
-2
-1.5
-1
-0.5
0
0.5
1
1.5
2

## Slide 26
>> y = pulse_ref(1,5,5,t);
>> yf2 = FourierT(y, dt);
>> plot(f(1:100), abs(yf2(1:100)))
Somewhat more
narrow band pulse
(only 0 - 20 MHz
shown)
0
0.5
1
1.5
2
2.5
3
3.5
4
4.5
5
-2
-1.5
-1
-0.5
0
0.5
1
1.5
2
0
2
4
6
8
10
12
14
16
18
20
0
0.1
0.2
0.3
0.4
0.5

## Slide 27
>> y = pulse_ref(1,5,10,t);
>> yf3 = FourierT(y, dt);
>> plot(f(1:100), abs(yf3(1:100)))
Decrease bandwidth
even more
(only 0 - 20 MHz
shown)
0
1
2
3
4
5
-2
-1
0
1
2
0
2
4
6
8
10
12
14
16
18
20
0
0.2
0.4
0.6
0.8
1

## Slide 28
f is not quite adequate here
f =1/T = 1/5 MHz
>> plot(f(1:50), abs(yf3(1:50)))
Show plot in more detail
0
1
2
3
4
5
6
7
8
9
10
0
0.2
0.4
0.6
0.8
1
we can improve these results with zero padding of our signal

## Slide 29
zero padding
now, have 1024 points over 10
microseconds, so dt is same but
T = Ndt is twice as large
0
1
2
3
4
5
6
7
8
9
10
-2
-1
0
1
2
>> t=s_space(0, 10, 1024);
>> y=pulse_ref(1, 5,10, t);
>> plot(t,y)
>> dt = t(2) -t(1)
dt = 0.0098
recall, originally, we had
t = s_space(0,5, 512);
we could also zero pad via
t = [t, zeros(1, 512)];

## Slide 30
>> yf4 = FourierT(y, dt);
>> f = s_space(0, 1/dt, 1024);
>> plot(f(1:100), abs(yf4(1:100)))
Improved representation of the
spectrum f = 1/T = 1/10 MHz
0
1
2
3
4
5
6
7
8
9
10
0
0.2
0.4
0.6
0.8
1
1.2
1.4

## Slide 31
>> y = IFourierT(yf3, dt);
>> plot(t , real(y));
Example inverse FFT (of yf3)
real part is taken here to eliminate any small
imaginary components due to numerical round off
errors
0
0.5
1
1.5
2
2.5
3
3.5
4
4.5
5
-2
-1
0
1
2

## Slide 32
fs
fmax
| Vp(f) |
N samples
positive frequency
components
negative frequency
components
fs
fmax
| Vp(f) |
N samples
positive frequency
components
?
in time domain
if v(t) is real
Fast Fourier Transform

## Slide 33
Hilbert transform of v(t)
so
Fast Fourier Transform

## Slide 34
>> t = s_space(0,5, 512);
>> y = pulse_ref(1,5,10,t);
>> plot(t, y)
>> yf= FourierT(y, dt);
>> yf5 = yf .*(f < 50);
>> plot(f, abs(yf5))
zero negative
frequency components
Throwing out negative frequency components
now, do the inverse FFT
on just these positive
frequency components
0
1
2
3
4
5
-2
-1
0
1
2
0
20
40
60
80
100
120
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1

## Slide 35
>> yf5(1) = yf5(1)/2;
>> y = 2*real(IFourierT(yf5, dt));
>> plot(t, y)
when throwing out negative frequency
components, need to divide dc value
by half also (not needed if dc value is zero or
already very small)
0
1
2
3
4
5
-2
-1
0
1
2

## Slide 36
References
Walker, J.S., Fast Fourier Transforms, CRC Press, 1996
Burrus, C.S. and T.W. Parks, DFT/FFT and Convolution
Algorithms, John Wiley and Sons, New York, 1985.
Fast Fourier Transform