## Slide 1
Ultrasonic System Measurement Model - II

## Slide 2
Learning Objectives
Definition of a Measurement Model
Three Types of Measurement Models
Auld Model
Thompson-Gray
Model for 2D scatterers
Verifying the Modeling Assumptions
and Measurements Needed

## Slide 3
Sf
n
What is an Ultrasonic Measurement Model? A model that expresses the output voltage, vR(t) ,received from a flaw in a ultrasonic testing configuration in a form that explicitly states the modeling or measurement parameters needed to obtain that voltage (immersion shown only as a specific example)
Pulser
Receiver
surface of the flaw which has an outward normal, n
All the measurement models discussed use VR(), the frequency components of vR(t)
component being inspected
Ultrasonic Measurement Models
A
B

## Slide 4
Ultrasonic Measurement Models
Electroacoustic Measurement Model - 2002
Dang, C. J., Schmerr, L.W., and A. Sedov," Modeling and measuring all the elements of an ultrasonic nondestructive
evaluation system. I: Modeling Foundations," Research in Nondestructive Evaluation, 14, 141- 176, 2002.
Sf
n
pulser
cabling
sending
transducer
receiving
transducer
cabling
receiver
propagation,
flaw scattering
output voltage
driving voltage
= ?

## Slide 5
Auld Electromechanical Reciprocity Relation
Auld (1979) , using reciprocity relations and the solutions to two specific problems, developed an explicit relation that has been widely used
problem (1)
problem (2)
Sf
n
transducer A firing,
flaw present
transducer B firing,
flaw absent
The two problems:
Ultrasonic Measurement Models
B. A. Auld, Wave Motion,, Vol. 1, (1979), pp. 3-10.
A
A
B
B

## Slide 6
Sf
n
Auld Electromechanical Reciprocity Relation
… change in cable transmission coefficient due to the presence of the flaw
P… power delivered by the transducer
stress vector and velocity for problem (1) : A firing and flaw present
stress vector and velocity for problem (2): B firing and flaw absent
Ultrasonic Measurement Models
A
B

## Slide 7
Sf
n
Auld Electromechanical Reciprocity Relation
Auld's assumptions:
1) linear, reciprocal electromechanical system (harmonic disturbances)
2) fundamental TEM mode propagating in the cable
Since we expect
Auld's relation "essentially" is
an ultrasonic measurement model
Ultrasonic Measurement Models
A
B

## Slide 8
An Alternative Reciprocity Relation
In 1998, Dang, Schmerr, and Sedov obtained a completely explicit model relationship using a purely mechanical reciprocity relationship plus several other relatively weak assumptions
problem (1)
problem (2)
vA
(1)
Sf
vB
(2)
n
Ultrasonic Measurement Models
A
A
B
B

## Slide 9
… system function (pulser, cabling, receiver)
… average velocity over the face of transducer A in problem (1)
… average velocity over the face of transducer B in problem (2)
… radiation impedance of transducer A in problem (1)
Ultrasonic Measurement Models

## Slide 10
assumptions used to obtain this explicit model
1) linear, reciprocal acoustic and elastic media (harmonic disturbances)
Ultrasonic Measurement Models

## Slide 11
average velocity
2) we also assumed the output velocity for the transducers can be written in a separable form. For transducer A, for example
Here, the "forces" are defined in terms of weighted pressure integrals over the transducer face, using the same functions used to describe the velocity. For example, for transducer A
density, wave speed of the fluid
For a piston transducer
Ultrasonic Measurement Models
A

## Slide 12
flaw
Ft
FB
Transmitted
force
Blocked
force
A
B
These two assumptions lead to an explicit expression for the acoustic/elastic transfer function:

## Slide 13
3) we also assume that the pulser, receiver, transducers and cabling can be replaced by equivalent linear, time-shift invariant (LTI) systems, i.e.
Then, we can write the reciprocity relationship in the form
or, finally
Ultrasonic Measurement Models

## Slide 14
assumptions
1) linear, reciprocal acoustic and elastic media (harmonic disturbances)
2) the output velocity for the transducers can be written in a separable form
3) the pulser, receiver, transducers and cabling can be replaced by equivalent linear, time-shift invariant (LTI) systems.
A General Ultrasonic Measurement Model
Ultrasonic Measurement Models

## Slide 15
4) if we also assume that the transducers behave as piston radiators at high frequency then
and our explicit model becomes, finally
Ultrasonic Measurement Models

## Slide 16
5) now, assume the incident waves are quasi-plane waves in the vicinity of the flaw, e.g.
and also define normalized amplitudes of these quasi-plane waves as
Ultrasonic Measurement Models

## Slide 17
Then the form of the measurement model becomes
Ultrasonic Measurement Models
velocity fields
in problems (1),(2)
due to unit average velocities on the transducer faces
scattered wave fields
from the flaw

## Slide 18
the normalized fields are defined as velocity and stress in
problem (1) due to an incident wave of unit displacement amplitude
The flaw scattering term is rather complex:
stresses and velocity components in problem (1)
components of the incident wave direction and polarization
in problem (2)
components of the unit outward normal to the flaw surface
elastic constants tensor

## Slide 19
rs
n
flaw
U0
U0 … displacement
amplitude for wave
of type  ( = P,S) in
problem (1)
Scattered wave of
type  ( = P,S)
3-D scattering amplitude
incident wave with polarization
d in problem (2)
scattered displacement
from a flaw
P-wave
S-wave
Ultrasonic Measurement Models

## Slide 20
However, it can be shown that
3-D scattering amplitude
vector scattering amplitude of waves in problem (1)
polarization vector of incident
waves in problem (2)
Ultrasonic Measurement Models

## Slide 21
Measurement Model - Quasi-Plane Waves
Ultrasonic Measurement Models
The beam modeling terms and flaw scattering terms appear separately in this model but they still must be combined before the voltage can be obtained

## Slide 22
6) Now, assume a small 3-D flaw, i.e. where the incident waves do not vary significantly in amplitude over the surface of the flaw
O
Then
and, recall

## Slide 23
Measurement Model (Thompson-Gray form)
beam models
plane wave far field
scattering amplitude
component
Ultrasonic Measurement Models
R. B. Thompson and T. A. Gray, J. Acoust. Soc. Am., Vol. 74, (1983), pp. 140-146.

## Slide 24
Measurement Model (Thompson-Gray form)
1) linear, reciprocal acoustic and elastic media (harmonic disturbances)
2) the output velocity for the transducer(s) can be written in a separable form
3) the pulser, receiver, transducers and cabling can be replaced by equivalent linear, time-shift invariant (LTI) systems.
4) the transducers are assumed to behave as piston radiators operating at high frequency
5) the incident waves are quasi-plane waves in the vicinity of the flaw
6) the scatterer is a small 3-D flaw where the incident waves do not vary significantly in amplitude over the surface of the flaw
Ultrasonic Measurement Models

## Slide 25
6a) If instead, the scatterer is a small cylindrical flaw (e.g. side-drilled hole), with incident and scattered wave directions in the plane of the cross-section then we can assume
only
In this case
O
Ultrasonic Measurement Models

## Slide 26
3-D scattering amplitude component of a 2-D, cylindrical geometry (end effects neglected) is just
so that the measurement model can be expressed, finally, as
Ultrasonic Measurement Models
Schmerr, L.W., and A. Sedov, "Modeling ultrasonic problems for the 2002 benchmark session,"
Review of Progress in Quantitative Nondestructive Evaluation, D.O. Thompson and D.E. Chimenti, Eds.,
American Institute of Physics, Melville, N.Y. , 22B,1776-1783, 2003.

## Slide 27
Relationship between 2-D and 3-D scattering amplitudes
which gives the alternate form
Ultrasonic Measurement Models

## Slide 28
1) linear, reciprocal acoustic and elastic media (harmonic disturbances)
2) the output velocity for the transducer(s) can be written in a separable form
3) the pulser, receiver, transducers and cabling can be replaced by equivalent linear, time-shift invariant (LTI) systems.
4) the transducers are assumed to behave as piston radiators operating at high frequency
5) the incident waves are quasi-plane waves in the vicinity of the flaw
6) the scatterer is cylindrical flaw with incident and scattered wave directions in the plane of the cross-section, where the incident waves do not vary significantly in amplitude over the small cross-section of the flaw
Measurement Model for 2-D scatterers

## Slide 29
2-D small flaw (Schmerr-Sedov form)
3-D small flaw (Thompson-Gray form)
General Measurement Model (Auld form)
Ultrasonic Measurement Models

## Slide 30
Is the system linear and reciprocal?
Electrical linearity checks of pulser/receiver
A
A
A
For a transducer
Using Measurement Models
Ultrasonic Measurement Models

## Slide 31
Is the transducer acting as a piston?
Compare responses with theoretical predictions in a reference experiment, e.g.
Is a quasi-plane wave assumption valid?
Compare
with
as computed with a non-paraxial beam model
Ultrasonic Measurement Models

## Slide 32
Is a small flaw assumption valid?
Compare
with
(3-D case)
or
(cylindrical case)
Ultrasonic Measurement Models

## Slide 33
What supporting measurements are needed?
System factor
Obtain in separate experiment
Velocity, Attenuation
Obtain in separate experiments
Transducer effective radius, focal length
Ultrasonic Measurement Models

## Slide 34
Summary
A measurement model form is available suitable for simulating most NDE inspections
To make these models useful one needs to have
ultrasonic beam models
flaw scattering models
experimental determination of essential parameters
Once all these elements are available one has a very powerful tool for designing tests, optimizing components, and replacing expensive experimental procedures.
Ultrasonic Measurement Models