## Slide 1
Batch Process Research Corporation
BPRC
8001 Lingay Drive
Allison Park, PA 15101
USA
Toll Free: 800-684-BPRC
Fax: (412)635-0521
bprc@bprc.com
Products and Services
MultiBatchDS Professional
MultiBatchDS Educational
Custom consulting sevices in Computer aided Batch and Continuous Process Design , Optimization, and Control.
Annual seminars and in-house workshops on batch distillation & batch process designs
In-house seminars at the client’s facility
Research and Development
Books and other educational activities

## Slide 2
Batch Distillation: Design, Optimization, and Optimal Control
Urmila Diwekar
Carnegie Mellon University
Pittsburgh, PA 15213
Email: urmila@cmu.edu

## Slide 3
Batch vs. Continuous
The factors that favor batch operation are
Production rate
  Sometimes batch if less than 107 lbs/year
  Usually batch if less than 106 lbs/year
  Multiproduct plants
Market forces
  Seasonal production
  Short production life
Scale up problems
  Very long reaction times
  Handling slurries at low flowrates
  Rapidly fouling materials

## Slide 4
Batch Process Design & Operations
Batch Reactors
Batch Distillation
Batch Crystallization
Drying & Filtration
Chromatographic Separation
Sedimentation & Thickeners
Numerical Integration
Optimization & Optimal Control
Scheduling & Planning
Flexibility & Uncertainty Analysis

## Slide 5
Why Batch Distillation?

## Slide 6
Continuous Distillation
Batch Distillation
Unsteady State Nature of Batch Distillation

## Slide 7
Flexibility
Benzene - 1
Toluene - 98
Xylene - 1
Benzene - 99
Toluene - 1
Toluene - 1
Xylene - 69
FEED
Benzene - 100
Toluene - 100
Xylene - 70
1
2
Benzene - 99
Toluene - 1
Benzene - 1
Toluene - 98
Xylene - 1
Toluene - 1
Xylene - 69

## Slide 8
Operating Modes
1.2
1.0
0.8
0.6
0.4
0.2
0.0
2
3
4
5
6
7
8
0.5
0.4
0.3
0.2
0.1
0.0
0
10
20
30
40
50
Optimal Control
Optimal Control
Variable Reflux
Constant Reflux
Variable Reflux
Constant Reflux
x
B
(1)
T, hr
R

## Slide 9
2
3
1
2
3
1
(a)
(b)
(c)
(e)
(d)
Different column configurations including emerging designs
Conventional column
a rectifier
Multifraction
operation
Recycle waste cut
Inverted column
a stripper
Column with
a middle vessel

## Slide 10
Review of Batch Distillation
1902 - 1997

## Slide 11
Simple Distillation Analysis
Lord Rayleigh, 1902 - Rayleigh Equation
d (ln B/F) = d xB/(xD - xB)
xB
B
xD
xD
xB
single theoretical stage

## Slide 12
xD
xB
single theoretical stage
y
x
xD
x
y
x
y
x
x
xB
multiple theoretical stages
Batch Distillation

## Slide 13
Operating Modes (linear representation)
R
T
xD
T
Variable reflux
Optimal reflux
Variable reflux
Constant reflux
Constant reflux

## Slide 14
Relation between xD and xB
McCabe-Thiele, 1925
Variable Reflux, Bogart 1937
Constant Reflux, Smoker & Rose, 1940
xD2
xB2
xD1
xD
xB1
xB1
xB2

## Slide 15
Rigorous Models
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
Huckaba & Danly, 1960
Distefano,1969
Boston et al., 1983
(BATCHFRAC)
Diwekar, 1988
(Batch-Dist, MultiBatchDS)

## Slide 16
Numerical Integration
0
0.2
0.4
0.6
0.8
1
0
0.2
0.4
0.6
0.8
1
Distillate Composition
Batch Time, hrs
(a)
0
0.2
0.4
0.6
0.8
1
0
0.2
0.4
0.6
0.8
1
Batch Time, hrs
(b)
Stiff Integrator
Non-Stiff Integrator
18 % Holdup on plates

## Slide 17
Numerical Integration (contd.)
0
0.2
0.4
0.6
0.8
1
0
0.2
0.4
0.6
0.8
1
Distillate Composition
Batch Time, hrs
(a)
-1000
-800
-600
-400
-200
0
200
400
600
0
0.2
0.4
0.6
0.8
1
Batch Time, hrs
(b)
10 % Holdup on plates
Stiff Integrator
Non-Stiff Integrator

## Slide 18
Numerical Integration (contd.)
0
0.2
0.4
0.6
0.8
1
0
0.2
0.4
0.6
0.8
1
Distillate Composition
Batch Time, hrs
0
0.2
0.4
0.6
0.8
1
0
0.2
0.4
0.6
0.8
1
Batch Time, hrs
1 % Holdup on plates
Stiff Integrator
Model Change

## Slide 19
Semi-rigorous Models
MB, EB, VLE
MB, EB, VLE
MB, EB, VLE
DMB, DEB, VLE
MB, EB, VLE
MB, EB, VLE
MB, EB, VLE
Diwekar, 1988
(Batch-Dist, MultiBatchDS)
Doherty &
co-workers, 1990-93

## Slide 20
Shortcut Model
DMB, DEB, VLE
Diwekar, 1988
Diwekar, 1991 Binary
Azeotropic Systems
Kalagnanam & Diwekar,
1993,Ternary Azeotropic
Systems
Batch distillation can be
considered as continuous
distillation with changing
feed, Diwekar 1988

## Slide 21
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
F
U
G
Eqn
DMB
HG
Rigorous Model
Shortcut Model

## Slide 22
Features of Shortcut Method
Fast and reasonably accurate
Easy identification of feasibility
Quick screening of alternatives
CPU time independent of number of plates
Solution of non-integer algebraic equations
Useful for design, optimization, and synthesis….

## Slide 23
Optimization
History of Optimization
  1000 BC Queen Dido - Isoperimetric Problem
  First Systematic theory of Optimization - Variational Calculus, June 4, 1694 by John Bernoulli
  Numerical Optimization - 1947 -94
Batch Distillation Optimization
  Mostly Optimal Control Problems - 1963-94
  Design Optimization (Nonlinear Programming)
    Luyben 1971
    Diwekar et al. 1989

## Slide 24
Optimal Control Problems
Maximum Distillate Problem - where the amount of distillate of a specified concentration for a specified time is maximized (Converse and Gross, 1963; Keith and Brunet, 1971; Murty et al., 1980; Diwekar et al., 1987; Logsdon et al., 1990; Farhat et al., 1990)
Minimum Time Problem - where the batch time needed to produce a prescribed amount of distillate of a specified concentration is minimized (Coward, 1967a, b; Hansen and Jorgensen, 1986; Mujtaba and Macchietto, 1988)
Maximum Profit Problem - where a profit function for a specified concentration of distillate is maximized (Kerkhof and Vissers, 1978; Logsdon et al., 1990)

## Slide 25
Optimal Control Solution Methods
Calculus of Variation
Dynamic Programming
Pontryagin’s Maximum Principle
  1963 -1994
Nonlinear Programming Optimization (NLP)
  Collocation for Discretization : Logsdon et al, 1990, 93
  Polynomial Approximation: Mujtaba & Machiatto, 1988; Farhat et al. 1990
Combined Maximum Principle & NLP Optimization
  Diwekar et al., 1992

## Slide 26
Limitations of the Shortcut Method
can handle nearly ideal and ideal azeotropic systems
heat effects not considered
not applicable to reactive distillation

## Slide 27
Reduced Order Model
DMB, DEB, VLE
DMB, DEB, VLE
Continuous Distillation
Joseph & Coworkers
1983-87
Stewart et al, 1985
Westerberg & Coworkers
1994
Batch Distillation
Diwekar, 1988
(Batch-Dist, MultiBatchDS)
DMB, DEB, VLE
*
*
DMB, DEB, VLE

## Slide 28
Reduced Order Model
Collocation based model
Unlike continuous distillation, no problem
for LLK or HHK
Useful for packed columns, non-equilibrium
models, reactive distillation
Wajge et al., 1997 - packed column

## Slide 29
Start
Rapid
analysis of column
/ Feasibility Info.
Reqd.?
Is
system nearly
ideal and holdup
effect negligible
?
Is
holdup effect
negligible or
system
highly
stiff?
Modified Short-cut
Short-cut
Semi-rigorous
Rigorous
Reduced-order
Is
column large
/packed, or
rate-based
simulation
desired?
Yes
No
Yes
No
No
Yes
No
Yes
Guidelines for the Use of Models

## Slide 30
Complex Systems
Analysis of azeotropic systems
Concept of residue curve maps
Acetone
Methanol
Chloroform
54.5
65.1
54.2
56.8
58.1
61.7
64.5
Doherty and Coworkers, 1981-95
Safrit et al., 1996-97

## Slide 31
Complex Columns
Inverted Columns
  Sorensen & Skogestad, 1996
  Lotter & Diwekar, 1997
Middle Vessel Column
  Devidyan et al., 1982-1994
  Diwekar & Coworkers 1994-97
  Barlo et al., 1996
Multi-vessel column
  Hasebe et al., 1992
  Skogestad et al., 1997

## Slide 32
Conventional Batch Column

## Slide 34
An Inverted Batch Column

## Slide 35
Distillate
Feed
Feed
Botpro

## Slide 36
Prod 1
Prod 2
Prod 3
Middle Vessel Column Multivessel Batch Column
Feed/Prod3
Prod1
Prod2
Feed/Prod4
Feed
Feed
Feed

## Slide 37
Industrial Case Study
Feed
Comp-1 24.4 %
Comp-2 26.8 %
Comp-3 48.8 %
1
2
Comp-1 11.5 %
Comp-2 88.5 %
Comp-3 Neg.
Comp-2 2.5 %
Comp-3 97.5 %
Comp2 and 3 are close boiling

## Slide 38
1
3
The Inverted Column Product Distribution
Comp-1 11.5 %
Comp-2 88.5 %
Comp-3 Neg.
Comp-2 2.5 %
Comp-3 97.5 %
Feed
Comp-1 24.4 %
Comp-2 26.8 %
Comp-3 48.8 %

## Slide 39
N=20
N=70
N = 20
N = 70

## Slide 40
Industrial Case Study: Feasibility
Conventional column with nearly infinite plates (N=70)
and high reflux ratio (R > 20)
Stripper with reasonable number of plates (N < 25)
Various middle vessel configurations

## Slide 41
Batch Distillation Column Software Requirements
Features
Windows
Databank
Operations
Constant Reflux
Variable Reflux
Fixed Eqn. Optimal
Optimal Reflux
Models
Shortcut
Semirigorous
Reduced Order
Rigorous
Options
Design Feasibility
Optimization
Reactive Distillation
3 phase Distillation
Uncertainty Analysis
Configurations
Semi-batch
Recycle waste cut
Rectifier
Stripper
Middle Vessel
Why
User friendly state of the art input/output interface
Ability to generate data from structural information
Yield improvement due to operational flexibility and
systematic optimization/optimal control methods
Hierarchy of models for numerical stability, design feasibility, and advanced system designs.
Advanced features
Emerging designs provide promising directions for cost effective designs to obtain purer products

## Slide 42
Visual Highlights
A user-friendly graphical input interface based on Windows 95 and NT. Also supports keyword input structures.
Flexible and easy-to-use menus and sub-menus.
Powerful, interactive plotting with multiple options for abscissa and ordinate.
Graphical as well as textual output results.
On-line help screens and tutorials.
On-line monitoring and control of the program execution.
MultibatchDS : Professional Batch Distillation Systems for multiple column configurations, multiple operating modes, multiple fractions, and multiple products---with multiple levels of models

## Slide 43
Batch Distillation Column Software Requirements
Features
Windows
Databank
Operations
Constant Reflux
Variable Reflux
Fixed Eqn. Optimal
Optimal Reflux
Models
Shortcut
Semirigorous
Reduced Order
Rigorous
Options
Design Feasibility
Optimization
Reactive Distillation
3 phase Distillation
Uncertainty Analysis
Configurations
Semi-batch
Recycle waste cut
Rectifier
Stripper
Middle Vessel
Why
User friendly state of the art input/output interface
Ability to generate data from structural information
Yield improvement due to operational flexibility and
systematic optimization/optimal control methods
Hierarchy of models for numerical stability, design feasibility, and advanced system designs.
Advanced features
Emerging designs provide promising directions for cost effective designs to obtain purer products

## Slide 44
Molecular Designs
Simulating distillation with no data? No problem

## Slide 45
Batch Distillation Column Software Requirements
Features
Windows
Databank
Operations
Constant Reflux
Variable Reflux
Fixed Eqn. Optimal
Optimal Reflux
Models
Shortcut
Semirigorous
Reduced Order
Rigorous
Options
Design Feasibility
Optimization
Reactive Distillation
3 phase Distillation
Uncertainty Analysis
Configurations
Semi-batch
Recycle waste cut
Rectifier
Stripper
Middle Vessel
Why
User friendly state of the art input/output interface
Ability to generate data from structural information
Yield improvement due to operational flexibility and
systematic optimization/optimal control methods
Hierarchy of models for numerical stability, design feasibility, and advanced system designs.
Advanced features
Emerging designs provide promising directions for cost effective designs to obtain purer products

## Slide 46
Modeling Issues
Unsteady state nature
Flexibility

## Slide 47
Rigorous Models
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
Huckaba & Danly, 1960
Distefano,1969
Boston et al., 1983
(BATCHFRAC)
Diwekar, 1988
(Batch-Dist, MultiBatchDS)

## Slide 48
Semi-rigorous Models
MB, EB, VLE
MB, EB, VLE
MB, EB, VLE
DMB, DEB, VLE
MB, EB, VLE
MB, EB, VLE
MB, EB, VLE
Diwekar, 1995
(MultiBatchDS)

## Slide 49
Shortcut Model
DMB, DEB, VLE
Diwekar, 1988
Diwekar, 1991 Binary
Azeotropic Systems
Kalagnanam & Diwekar,
1993,Ternary Azeotropic
Systems
Batch distillation can be
considered as continuous
distillation with changing
feed, Diwekar 1988

## Slide 50
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
DMB, DEB, VLE
F
U
G
Eqn
DMB
HG
Rigorous Model
Shortcut Model

## Slide 51
Reduced Order Model
DMB, DEB, VLE
DMB, DEB, VLE
Continuous Distillation
Joseph & Coworkers
1983-87
Stewart et al, 1985
Westerberg & Coworkers
1994
Batch Distillation
Diwekar, 1988
(Batch-Dist, MultiBatchDS)
DMB, DEB, VLE
*
*
DMB, DEB, VLE

## Slide 52
Start
Rapid
analysis of column
/ Feasibility Info.
Reqd.?
Is
system nearly
ideal and holdup
effect negligible
?
Is
holdup effect
negligible or
system
highly
stiff?
Modified Short-cut
Short-cut
Semi-rigorous
Rigorous
Reduced-order
Is
column large
/packed, or
rate-based
simulation
desired?
Yes
No
Yes
No
No
Yes
No
Yes
Guidelines for the Use of Models

## Slide 53
Modeling Issues
Unsteady state nature
Flexibility

## Slide 54
Operating Modes (linear representation)
R
T
xD
T
Variable reflux
Optimal reflux
Variable reflux
Constant reflux
Constant reflux

## Slide 55
Batch Distillation Column Software Requirements
Features
Windows
Databank
Operations
Constant Reflux
Variable Reflux
Fixed Eqn. Optimal
Optimal Reflux
Models
Shortcut
Semirigorous
Reduced Order
Rigorous
Options
Design Feasibility
Optimization
Reactive Distillation
3 phase Distillation
Uncertainty Analysis
Configurations
Semi-batch
Recycle waste cut
Rectifier
Stripper
Middle Vessel
Why
User friendly state of the art input/output interface
Ability to generate data from structural information
Yield improvement due to operational flexibility and
systematic optimization/optimal control methods
Hierarchy of models for numerical stability, design feasibility, and advanced system designs.
Advanced features
Emerging designs provide promising directions for cost effective designs to obtain purer products

## Slide 56
Conventional Batch Column

## Slide 57
An Inverted Batch Column

## Slide 58
Prod 1
Prod 2
Prod 3
Middle Vessel Column Multivessel Batch Column
Feed/Prod3
Prod1
Prod2
Feed/Prod4
Feed
Feed
Feed

## Slide 59
2
3
1
2
3
1
(a)
(b)
(c)
(e)
(d)
Different column configurations including emerging designs
Conventional column
a rectifier
Multifraction
operation
Recycle waste cut
Inverted column
a stripper
Column with
a middle vessel

## Slide 60
Industrial Case Study
Feed
a Moles
A 3.0 28
B 1.1 29
C 1.0 71
1
2
A - neg.
B - 0.83 mole frac.
C - 0.17 mole frac.
A - neg.
B - 0.08 mole frac.
C - 0.92 mole frac.
Pure A
Number of Theoretical Plates > 100

## Slide 61
Feed
Botpro
Product C
&
Product B
Waste Product A
Number of Theoretical Plates < 25
Heuristic Rule: “ To obtain a given purity in a minimum
amount of time, the inverted column is better than
regular column for separations where light component is
present in a small amount”
- Sorensen & Skogestad (1996)
If the relative volatilities of the components are changed then the above heuristic fails

## Slide 62
An alternative approach is to use a quantitative measure
based on shortcut procedures
- Malone et al., 1985
F
U
G
Eqn
DMB
HG
F
U
G
Eqn
DMB
HG
Shortcut Method for Rectifier
-(Diwekar & Madhavan, 1991)
Shortcut Method for Stripper
-(Lotter & Diwkear, 1997)
Minimum Number of Plates for Rectifier = 42
Minimum Number of Plates for Stripper = 16

## Slide 63
Batch Distillation Column Software Requirements
Features
Windows
Databank
Operations
Constant Reflux
Variable Reflux
Fixed Eqn. Optimal
Optimal Reflux
Models
Shortcut
Semirigorous
Reduced Order
Rigorous
Options
Design Feasibility
Optimization
Reactive Distillation
3 phase Distillation
Uncertainty Analysis
Configurations
Semi-batch
Recycle waste cut
Rectifier
Stripper
Middle Vessel
Why
User friendly state of the art input/output interface
Ability to generate data from structural information
Yield improvement due to operational flexibility and
systematic optimization/optimal control methods
Hierarchy of models for numerical stability, design feasibility, and advanced system designs.
Advanced features
Emerging designs provide promising directions for cost effective designs to obtain purer products

## Slide 64
Batch Distillation Column Software Comparison
Features
Windows
Databank
Operations
Constant Reflux
Variable Reflux
Fixed Eqn. Optimal
Optimal Reflux
Models
Shortcut
Semirigorous
Reduced Order
Rigorous
Options
Design Feasibility
Optimization
Reactive Distillation
3 phase Distillation
Uncertainty Analysis
Configurations
Semi-batch
Recycle waste cut
Rectifier
Stripper
Middle Vessel
BATCHSIM
Yes
SIMSCI
Yes
Yes (limited)
No
No
No
No
No
Yes
No
No
No
No
No
No
No
Yes
No
No
MultiBatchDS
Yes
Cranium/ Multiple data banks
Yes
Yes
Yes
Yes
Yes
Yes
Yes
Yes
Yes
Yes
Yes (limited)
Yes
Yes
Yes
Yes
Yes
Yes
Yes
BATCHFRAC
No
ASPEN Plus
Yes
Yes (limited)
No
No
No
No
No
Yes
No
No
Yes (limited)
No
No
No
No
Yes
No
No

## Slide 65
MultiBatchDS- Add-ons
MultiBatchDS/Datalink
MultiBatchDS can be easily linked to commercially available databanks and thermodynamic models from other software companies like ASPEN or SIMSCI, or to your in-house databank.

## Slide 66
MultiBatchDS- Add-ons
MultiBatchDS/Continuous
A Batch column or a continuous column?
MultiBatchDS provides an add-on for simulating a continuous column on the same platform to resolve this problem.

## Slide 67
MultiBatchDS- Add-ons
MultiBatchDS/Probabilistic
A fully integrated add-on for uncertainty analysis based on probabilistic techniques and Monte Carlo simulations contains a library of distribution functions and various sampling technique including a new sampling technique which can be 100 times faster than any existing techniques.

## Slide 68
MultiBatchDS- Add-ons
MultiBatchDS/Packed columns
The collocation based reduced-order model can be easily adapted for packed columns or for non-equilibrium distillation columns with this add-on. Mass transfer relations for specific packings can be readily input using this add-on for packed column simulation.

## Slide 69
MultiBatchDS- Add-ons
MultiBatchDS/RT
A customized data-acquisition and control add-on that provides a real-time interface to in-house control systems. You can modify thermodynamic parameters using the simulation and plant data with built-in optimization based parameter estimation techniques.

## Slide 70
Future Work
New Column Configurations
Reactive Batch Distillation
Batch Distillation Synthesis
Batch Distillation Control
Uncertainty & Flexibility Analysis
Fugitive Emission Modeling

## Slide 71
FUTURE PLANS
Batch Reactors
Batch Distillation
Batch Crystallization
Drying & Filtration
Chromatographic Separation
Sedimentation & Thickeners
Numerical Integration
Optimization & Optimal Control
Scheduling & Planning
Flexibility & Uncertainty Analysis