## Slide 1
CH1. What is what
CH2. A simple SPF
CH3. EDA
CH4. Curve fitting
CH5. A first SPF
CH6: Which fit is fitter
CH7: Choosing the objective function
CH8: Theoretical stuff
Ch9: Adding variables
CH10. Choosing a model equation
2. A Simple SPF
We defined ‘Safety’, ‘Unit’, ‘Traits’, ‘Population’, and SPF as a tool to get estimates of E{μ} and σ{μ}.
In this session:
I will make all this tangible with a simple SPF for a real population.

## Slide 2
When originally conceived (1995) SPF gave expected crashes as function of only exposure
Since then broadening in two ways:
Not only estimate of E{m} but also of σ{m}
Not only function of exposure but also of other traits
Function =
Function can be table, graph, algorithm, ...
I will develop first a simple SPF in form of table & graph because in this case populations are real.

## Slide 3
Used in all illustrations.
Two-lane, rural roads, Colorado
5323 segments, 6029 miles, 13 years, 21,718 Fatal & Injury accidents
Segment | Length [miles] | AADT |  |  |  |  | 
 |  | 1986 | 1987 | 1988 | ... | 1997 | 1998
... |  | ... | ... | ... | ... | ... | ...
2232 | 0.40 | 1350 | 1350 | 700 | ... | 1062 | 1108
2233 | 0.53 | 1200 | 1200 |  | ... | 934 | 974
... |  |  |  |  | ... |  | 
The Data

## Slide 4
Continued...
Segment | Length [miles] |  | Total accidents |  |  |  |  |  | Terrain
 |  |  | 1986 | 1987 | 1988 | ... | 1997 | 1998 | 
... |  | … | ... | ... | ... | ... | ... | ... | 
2232 | 0.40 | … | 0 | 1 | 1 | ... | 2 | 0 | Rolling
2233 | 0.53 | … | 0 | 1 | 2 | ... | 1 | 0 | Rolling
... |  | … |  |  |  | ... |  |  | 
Segment |  | Injury and Fatal accidents |  |  |  |  | 
 |  | 1986 | 1987 | 1988 | ... | 1997 | 1998
... | ... | ... | ... | ... | ... | ... | ...
2232 | ... | 0 | 0 | 0 |  | 1 | 0
2233 | ... | 0 | 0 | 1 |  | 1 | 0
... | ... |  |  |  | ... |  | 

## Slide 5
Period:1994-1998; Segment Length: 0.5 to 1.0 miles; N=2228 segments.
AADT Bins | No. of I&F accidents | No. of 0.5-1.5 mile segments | 
0-1,000 | 376 | 975 | 0.39
1,000-2,000 | 445 | 466 | 0.95
... | ... | ... | ...
9,000-10,000 | 102 | 19 | 5.37
10,000-11,000 | 81 | 18 | 4.50
... | ... |  | 
Data
An average segment in this bin had 102/19=5.37 I&F crashes in 5 years.
Bins and Computations
The first element of simple SPF, the

## Slide 6
AADT Bins | 
0-1,000 | 0.39
1,000-2,000 | 0.95
... | ...
9,000-10,000 | 5.37
10,000-11,000 | 4.50
Ordinate, , is estimate of average number of crashes/ segment in bin

## Slide 7
Moral: SPFs are about populations
AADT Bins | 
0-1,000 | 0.39
1,000-2,000 | 0.95
... | ...
9,000-10,000 | 5.37
10,000-11,000 | 4.50
Here there are 20 different populations.
Each population defined by five traits:
(1) State: Colorado,
(2) Road Type: two-lane,
(3) Setting: rural,
(4) Segment Length: 0.5 to 1.5 miles
(5)Traffic: AADT bin.
Each estimate in a row, each point on the graph, is a guess at the mean of the μ’s in a population.

## Slide 8
How close are E{m} and ?

## Slide 9
the accuracy of
Data |  |  | Estimates | 
AADT Bins | I&F accidents | 0.5-1.5 mile segments |  | ±
0-1,000 | 376 | 975 | 0.39 | 0.02
1,000-2,000 | 445 | 466 | 0.95 | 0.05
... | ... | ... | ... | 
9,000-10,000 | 102 | 19 | 5.37 | 0.53
10,000-11,000 | 81 | 18 | 4.50 | 0.50
... | ... |  |  | 
√102/19=±0.53

## Slide 10
5.37+0.53
5.37-0.53
The first element of (simple) SPF
Note the widening of ±σ limits. Why?

## Slide 11
Is this real?
If yes, what could explain it?

## Slide 12
And now to the second element of the SPF, the s{m}
Recall
Only this!
Nothing to do with this

## Slide 13
How to estimate the s{m}
One way
AADT Bins | I&F acc. | Segments |  |  | S2 | 
... | ... | ... | ... | ... |  | 
9K-10K | 102 | 19 | 5.37 | ... | 35.18 | ±5.46
... | ... |  |  | ... |  | 

## Slide 14
5.46
If we estimate the m of a road segment with the same traits as the population to be 5.37 then

## Slide 15
Now both elements of the (simple) SFP are in hand

## Slide 16
A Simple SPF - Summary
As SPF gives estimates of E{m} and of s{m} as a function of traits;
A function is not only an equation. We used a table to highlight the concept of ‘population’;
Using Colorado data we built a simple SPF and showed how both its elements are estimated;
Two groups of reasons for our interest in E{m} were given. The second group (estimation of specific μ’s) requires knowledge of s{m}.

## Slide 17
2. A Simple SPF – Summary continued
5. A third reason for interest in E{m} is of the cause-effect kind. I am skeptical; you keep an open mind.
6. I showed how s{m} can be estimated and how it is used.
7. The simple SPF has broad bins, few traits, and is of no practical use. To be of use, more traits have to be added and some variables have to be made continuous.