## Slide 1
CH1. What is what
CH2. A simple SPF
CH3. EDA
CH4. Curve fitting
CH5. A first SPF
CH6: Which fit is fitter
CH7: Choosing the objective function
CH8: Theoretical stuff
Ch9: Adding variables
CH10. Choosing a model equation
3. Exploratory Data Analysis
Using Colorado data we built a simple SPF and showed how E{μ} and σ{μ} are estimated.
In this session:
The modeling process. Our data. What an EDA is used for. How to use a Pivot Table. Some obvious observations. How crashes depend on segment length and AADT.

## Slide 2
The Data
The SPF
How to make an SFP out of data
The Modeller

## Slide 3
The Data
The Modeller
What does the data say?
Initial EDA
Decisions, decisions:
Which traits to use? Equation or not? If not equation how to smooth? If smooth, what form? How to estimate parameters? Does it fit? Add a variable? ...

## Slide 4
What questions can an EDA answer?
Is there an orderly relationship between a variable and E{m}?
2. If yes, what function can represent it?
The same questions will be asked whenever a new variable is to be added. IEDA and VIEDA
EDA is not a collection of tools, it is a quest to understand the data in order to make good modeling decisions

## Slide 5
This data will be used throughout.
How many segments?
How many miles?
How many I&F crashes?
Average AADT?
Go to ‘Spreadsheets to accompany Power Points.’
Open #2. Initial EDA on ‘1. Original Data’ workbook
5323 segments, 6029 miles,
21,718 I&F, 52,317 total
2,151 Avg AADT, max 20,000

## Slide 6
Zero or no data?
What information?

## Slide 7
Holes were plugged, errors corrected but outliers may exist.
To get an idea how crashes vary with ‘Segment Length & ‘AADT’ I computed five year average AADT (1994-1998) and sum of I&F crashes for 1994-1998.
See ‘2. Condensed Data’ workbook

## Slide 8
The ‘Pivot Table’ spreadsheet tool makes tabulations easy.
Move to ‘3.Data & Pivot’ workbook
To answer: Create a table with ‘AADT’ bins on the side, ‘Segment Length’ across the top, and various stats in cells.
Is there an orderly relationship linking E{μ} to Segment Length and AADT? If yes, what does it look like?
1
2

## Slide 9
Must include headings row
Select: Existing Worksheet,
Choose location,
Click OK

## Slide 10
This is what you now see:

## Slide 11
Drag this
To here
Now this column opens

## Slide 12
Right click on any number in the ‘Row Labels’ column to open the ‘menu’.
Click on ‘Group’.
This will open
Change to 0
Change to 20,000
Click OK

## Slide 13
Now the Row Labels turn to:
(If the field list disappeared, click on Row Labels)
Now drag ‘Miles’ into the ‘Column Labels’ area

## Slide 14
Now the columns have to be ‘grouped’
As before, right-click on any column label and select ‘Group’ in menu.
Click OK
Choose:
0.5 and 20

## Slide 15
Now that the rows and columns are ready
Drag
this
to here

## Slide 16
Number of crashes in each bin
Where we have a fair number of crashes

## Slide 17
To get a different summary, right-click anywhere within the table to open:
2. Choose: ‘Count’
1. Click

## Slide 18
This gets us the count of segments in each bin.
No information
Good information

## Slide 19
To get the estimate of E{m} for a bin divide the number of crashes in previous table by number of segments from this table.
The Pivot makes it easy:
Right-click again within the table and choose ‘Average’.

## Slide 20
(After changing the number format):
Estimates of E{m}

## Slide 21
If all we know about a certain two-lane rural Colorado road segment is that it is 3.0 miles long, what is our estimate of its μ?
Answer: 4.74 accidents in five years
Why?
Because this is the estimate of the E{μ} of the population of units with the same known traits.
Pause EDA
Reflections and morals

## Slide 22
If we also know about that segment that its AADT=2500, what is now our estimate of its μ?
Answer: 6.80 F&I accidents in five years

## Slide 23
Noticing the obvious:
O.O. #1. Populations defined by different traits have different E{μ}‘s.
Traits | 
Length=3 miles | 4.74
Length=3 miles & AADT=2500 | 6.80
O.O. #2. For the of a population to be an unbiased estimate of the μ of a specific unit, the traits of that unit must be the same as the traits that define the population

## Slide 24
Not so obvious conclusions:
SPFs serve various uses:
Screening, comparing E{μ}s, estimating μ’s etc.
If, e.g., ‘Pavement Friction’ is not in the data for screening but is known for estimation of μ then we need two SPFs,
one SPF without ‘Pavement Friction’ and one with.
No SPF fits all uses
New footing.
How does one usually decide about whether to use a trait?
How must one decide?
How does one usually report results?
How must one report?

## Slide 25
O.O. #3. The more traits define a population the fewer are the segments from which E{μ} is estimated and the larger is its standard error
Traits |  | 
S.L.=3 miles | 1224/258=4.74 | √1224/258=±0.14
S.L.=3 miles & AADT=3000 | 238/35=6.80 | √238/35=±0.44
Another not-so-obvious conclusion:
Adding a trait to the SPF will diminish bias but reduce the accuracy of .
The right course of action?

## Slide 26
Return to EDA
Recall that SPFs provide estimates of E{μ} and σ{μ}
We use these
To estimate these

## Slide 27
One way to estimate σ{μ} is:
So, this is what we need now
This is an estimate of this.

## Slide 28
Sample Variances of crash counts:
To get crash count variances, right-click in table, go to ‘Summarize data by’ and then ‘more options’. From the options choose ‘VARp’.
Use again ‘3. Data and Pivot’ worksheet

## Slide 29
What is the effect of Terrain? (Flat, rolling, mountainous)

## Slide 30
How to capture ‘Terrain’?
Length | AADT | Mountainous | Rolling | M/R
<0.5 miles | 0-1000 | 0.20 | 0.22 | 0.90
0.5-1.5 miles | 1000-2000 | 1.65 | 1.06 | 1.56
Increasing with
Segment Length & AADT?
Implication for modeling?

## Slide 31
We asked two questions of the (initial) EDA?
Is there an orderly relationship?
(If not, do not add trait to SPF)
2. If yes, what function can represent it?
Visualization. 3D vs. 2D

## Slide 32
Orderly? Yes.
E{μ} increases with AADT.
What function? Not clear.
Visualization for AADT
(holding Segment Length constant)

## Slide 33
Why so much fluctuation?
Randomness of crash counts;
In many cells have few segments;
Differences in unaccounted-for traits.
Moral: What we are looking at may not be what we are looking for.
Mountainous, curves, steep grades
Flat, mild curves, no grade

## Slide 34
Orderly? Yes.
Increasing? Yes.
What function? Not clear
Visualization for Segment Length
(holding AADT constant)

## Slide 35
Summary for section 3.
Ingredients for SFP:
Data, Experience, Computation, Judgment
Unlike in baking, SPF development is not predefined sequence of steps;
It is a gradual progress towards a satisfactory result consisting of steps and missteps.
EDA provides guidance. It is not something you do once, before computing begins; you use it all the time. More about this later.

## Slide 36
Data come with holes and error; fix these early;
The Pivot Table is a useful tool of EDA (as is graphing).
Two obvious but important observations:
a. When a trait is added E{μ} changes;
b. This has implications for model building & reporting
c. Adding a trait diminishes the accuracy with which
E{μ} is estimated.
Segment Length, AADT and Terrain are ‘safety-related’, what functions is not clear.
EDA helps to answer two core questions:
Is the trait ‘safety-related’;
If yes, what function can represent that relationship.