## Slide 1
CH1. What is what
CH2. A simple SPF
CH3. EDA
CH4. Curve fitting
CH5. A first SPF
CH6: Which fit is fitter
CH7: Choosing the objective function
CH8: Theoretical stuff
Ch9: Adding variables
CH10. Choosing a model equation
4. Curve Fitting: Tools and First Steps
EDA : Is the trait ‘safety-related’ and, If yes, what function might represent it.
Obvious observations
In this session:
Why is Curve-Fitting necessary. The costs of C-F. How to do non-parametric C-F. The ‘Solver’. How to use it for parametric C-F.

## Slide 2
The Data
The Curve-Fitting Machine
The SPF
The Modeller
C-F Elements

## Slide 3
Why is C-F necessary?
Data are sparse
Few observations → bad estimates
→bad decisions →poor use of money

## Slide 4
Even with rich data there are many cells where data is insufficient
The safety of units depends on many traits
The addition of every trait further decimates the number of observations in a cell.
The “sparse-data problem”.
Where can Curve Fitting help?

## Slide 5
The goal of curve-fitting is:
...to the create an SPF that provides good
E{m} and s{m} = f(Traits, parameters)
Applications centered perspective
Here the question is: “How to do modeling to get good estimates of E{m} and s{m}?
Recall:

## Slide 6
Many think that he goal of C-F to produce good CMFs
Is such a goal is achievable? Chapter 5
E{m} and s{m} = f(Traits, parameters)
Cause and effect centered perspective
Here the question is:” How to do modeling to get the right ‘f’ and parameters so that I can compute the change in E{m} caused by a change in a trait.
Recall:

## Slide 7
Under the data cloud there is an ‘orderly’ relationships
A loose definition:
  Relationship is orderly if fitting some curve to data points seems sensible
The belief on which all C-F is founded:

## Slide 8
If ‘orderly’ then what is observed in one cell contains information about the neighbouring cell.
Therefore, estimate for one cell =f(Data in other cells)
What can we do if ‘orderly’?
1 | 2 | 3 | 4
AADT | No. of Segments | Accidents/ segment | SPF ordinate Five-point running average
… |  |  | 
2000-3000 | 35 | 6.80 | 7.26
3000-4000 | 15 | 8.80 | 9.70
4000-5000 | 11 | 16.36 | 11.20
5000-6000 | 7 | 13.43 | 12.34
6000-7000 | 5 | 10.60 | 14.58
… |  |  | 
11.20=(6.80+8.80+… +10.60)/5.

## Slide 9
Two Kinds of C-F
Non-parametric
Parametric
Specify rule how to compute local estimate from nearby data.
Product: Table & graph
Specify variables, parameters, & function. Estimate parameters.
Product: Model Equation
Example of rule:
Compute the running average of 9 observed values
Example of model equation:

## Slide 10
No free lunch (the price)
There is something different about this bin but 1’ ignores it
Same here
This kink in the curve is due to 1
Judging by the bars the squares are accurate. Is the curve really better?
Non-parametric
5 point moving average
Parametric:
All the above +

## Slide 11
Open Spreadsheet #3. ‘N-W non-parametric C-F’ on the ‘N-W Smoothing’ worksheet
The data
Click on Command button,
Play.
Is there a curve under the cloud?

## Slide 12
Non-parametric C-F
Can bring out order even where non is discernible.

## Slide 13
Overfitting in a nutshell
The 500 curve fits the data better than the 1000 one. Which curve is better?
The smaller the bandwidth the better will be ‘goodness-of-fit’ statistics.
Conclusion: Better GOF statistic is not necessarily a better fit!

## Slide 14
But, sparse data problem persist!
When Segment Length is added
Conclusion: Can be of use in EDA or with 1-2 traits; not more.

## Slide 15
Since the safety of units depends on more than one or two traits one cannot avoid making assumptions
One has to flesh out a ‘model equation’:
What traits (variables) should be in the model equation;
How these should combine into an equation;
  Variables & equation make the skeleton.
What should be the values of the parameters;
  Parameters stretch the skeleton to fit the data.
  This always requires minimization or maximization
Next
Going the next step

## Slide 16
Preparing the optimization tool for parametric C-F: The ‘Excel Solver’
Before first use ‘reference’ it.
Go to ‘Developer’. On ‘Code’ tab go to ‘Visual Basic’. Click on ‘Tools’, select ‘References’, check ‘Solver’ box. OK

## Slide 17
Using ‘Solver’ to find peaks and valleys: Illustration
Prepare spreadsheet for finding max or min:
Put an initial guess in A2,
Place formula in B2
Open spreadsheet #4: How to use the ‘Solver’

## Slide 18
1. Click on ‘Data’
2. Click on ‘Solver’
3. Window opens

## Slide 19
1. ‘y’ in B2 is to be minimized or maximized.
2. You want to find Max or Min?
3. You want to find it by changing the ‘x’ in A2
4. Click

## Slide 20
How the ‘Solver’ works:
It begins the search from the initial guess (0.3 in A2);
If ‘min’ it computes the largest downhill slope;
It selects a step size and takes it;
It repeats 1, 2 and 3 till the ‘largest slope’ is close to 0.

## Slide 21
Solver’s main limitation:
If the initial guess is at ‘1’ it can find ‘Max’ at ‘3’ and ‘Min’ at ‘2’ but it cannot find the ‘Min’ at ‘4’!
Conclusion: It finds ‘local’, not ‘global’ extrema.
Now, with same initial guess, find maximum.
(Result: x=0.070, y=0.343)
Now try to find the other valley. Choose initial guess to the left of the peak, say 0.05. (Min & Solve)

## Slide 22
What went wrong?
Solver decided to take a step downhill all the way to x=-1.55. But here value cannot be calculated.
This kind of problem arises when one tries to divide by 0, take a log of a negative number, etc.
To guard against it: Use constraints. Click ‘Add’

## Slide 23
If you now click on ‘Solve’
OK
Another possible snag:
Solver is asked to find values that differ by factors of 1000 or more
More later

## Slide 24
Finding global optima for non-convex functions is difficult.
This is why some software packages restrict you in the choice of the objective function (e.g. to Generalized Linear Models).
There is no such restriction in the spreadsheet C-F. However, one has to be careful in choosing the initial guess.

## Slide 25
How to use the solver for curve-fitting (C-F).
When doing the simple SPF based on bins we had:
Chart: 
| 500 | 1500 | 2500 | 3500 | 4500 | 5500 | 6500 | 7500 | 8500 | 9500 | 10500 | 11500
 | 0.38297 | 0.6403 | 1.1548 | 1.526 | 2.4686 | 1.9594 | 1.929 | 3.1391 | 2.9747 | 5.46 | 2.3034 | 3.448
Task: Fit a curve to these points by weighted least squares
Open spreadsheet #5: Fitting a curve to s{m} on ‘Data’ workpage.

## Slide 26
Go to the ‘Initial guess’ worksheet
Initial
guesses
Play with the initial guesses to fit the curve to data

## Slide 27
376/2729=0.138
E4*(C4-D4)^2
To be minimized
Play with the initial guesses to minimize weighted sum of SD
Go to the ‘Use Solver’ worksheet

## Slide 28
Now use ‘Solver’

## Slide 29
The fitted curve

## Slide 30
Choose the function to be fitted. (Here it was α(AADT) β)
Input into a range of cells that can be later conveniently (contiguously) selected some good initial guesses for the parameters.
Input the formula that computes the fitted values.
Decide on the criterion by which to judge the goodness of a fit. (Here it was the sum of weighted squared differences).
Use the ‘Solver’ to find the parameters which make for the best fit.
We now have the tool needed for parametric C-F
The main steps:

## Slide 31
Parametric Curve Fitting - overview
Which variables should be in the model equation;
In what manner should they combine;
What should be the value of the parameters.

## Slide 32
The difficulties:
What surface (function)? The regularity is difficult to visualize, confounding is a problem;
No theory, few features known by logic. All else is possible;
We know that important variables are missing from the model equation making the variables in the model into proxies;
Variables in the model are inaccurate and averaged.
Smoothing always distorts;
Parametric smoothing is a straightjacket

## Slide 33
Summary for section 4.
The goal of C-F is to ensure good fit to data.
There are two types of C-F, (a) non-parametric and (b) parametric.
For (a) we need a computation rule, for (b) a model equation & estimated parameters. Both rely on existence of ‘orderly relationship’.
The belief in orderly relationship allows us to use data from one bin for estimation in a different bin and thereby solves the ‘sparse data problem’.
But there s no free lunch.

## Slide 34
Non-parametric fits work well with one or two traits.
The Excel solver was introduced and its uses illustrated.
Valdimir Kush: Arrow of time