## Slide 1: Chapter 10: Reliable Transmission Protocol for Underwater Acoustic Networks
Xiujuan Du, Meiju Li, and Keqin Li

## Slide 2
Underwater Acoustic Networks (UANs) use acoustic communication and are characterized by limited bandwidth capacity, high energy consumption, long propagation delay, which cause the traditional protocols designed for radio channels to be either inapplicable or to be inefficient for UANs. The chapter introduces a three-layer protocol architecture for UANs which is Micro-ANP. Based on Micro-ANP architecture and Recursive LT (RLT) code, a handshake-free reliable transmission mechanism is presented in detail.
Abstract

## Slide 3
The energy, computation and storage resources of UANs are seriously constrained; consequently, the protocol stack running on UANs nodes should not be complicated. However, most research on UANs so far has followed the traditional five-layered architecture in network design, and in tough condition such as dynamic topology, seriously impaired channel and scarce resources, network efficiency was obtained by cross-layer designs, which cause numerous complicated issues that are difficult to overcome. UANs need a simple and efficient protocol architecture.
Background

## Slide 4: Micro ANP Architecture
Fig 2.1. Micro-ANP Architecture

## Slide 5: Introduction of Micro-ANP
The network transport layer in Micro-ANP is primarily responsible for reliable hop-by-hop transmission, routing, and channel access control. In Micro-ANP, broadcasting, Level-Based Adaptive Geo-Routing (LB-AGR) and a secure anonymous routing are the three major routing protocols that are applicable to dynamic underwater topology. A secure anonymous routing protocol can achieve anonymous communication between intermediate nodes as well as two-way authentication between source and destination nodes without any real-time online Public Key Generator (PKG), thus decreases the network delay while improving network scalability. In Micro-ANP, slotted Floor Acquisition Multiple Access (slotted FAMA) and a RLT Code based Handshake-Free (RCHF) reliable MAC protocol are the two-channel access control mechanism.

## Slide 6: The head fields of Micro ANP
Bits: 8 | 8 | 8 | 2 | 6 | 1 | 1 | 24 | 8
level of sender | sender ID | receiver ID | type 00: Data 01: Ack 10: Control | frame sequence number | immediately ack 1: yes 0: no | If block 1: Yes 0: No | IDs of original Packets | block ID
Bits:6 | 1 | 2 | 1 | 48 | 4 | 8 | variable | 16
block size | direction 0: down 1: up | Sink ID | (source¦ destination) 0: position 1: node ID | (source¦destination) position or ID Full “1” for broadcast | application priority (application type) | load length | data | FCS
Table 2.1 Head Fields of Micro-ANP

## Slide 7: Advantages of Micro ANP
Micro-ANP is a three-layered architecture that allows intermediate nodes to perform Application Dependent Data Aggregation (ADDA) at the application layer. Without requiring a cross-layer design, Micro-ANP can make efficient use of scarce resources. Moreover, Micro-ANP eliminates inapplicable layers and excessive repeated fields such as address, ID, length, Frame Check Sequence (FCS), and so on, thus reducing superfluous overhead and energy consumption.

## Slide 8: Advantages of Micro ANP
From Table 2.1, we can see that the common head-length of Micro-ANP is less than 20 bytes. In comparison, the total head-length of well-known five-layer models is more than 50 bytes. Therefore, Micro-ANP protocol greatly improves data transmission efficiency.

## Slide 9: Reliable Transmission Protocol for UANs
The inapplicability of conventional reliable transport mechanisms in UANs is analyzed.
Digital fountain codes are rate-less , the amount of redundancy is not fixed prior to transmission and can be determined on the fly as the error recovery algorithm evolves, and they allow for lightweight encoder and decoder implementations.
Based on digital fountain code, a Recursive LT (RLT) code with a small degree distribution is proposed.

## Slide 10: RLT Encoding Graph
Fig. 4.1. Encoding graph of RLT code

## Slide 11: Encoding

## Slide 12: Decoding

## Slide 13: Degree Distribution

## Slide 14: Table 4.1. Decoding complexity comparison

## Slide 15: RLT Code based Handshake-Free Reliable Transmission Protocol
In the RCHF MAC solution, a source node first groups input packets into blocks of size k (i.e., there are input packets in a block). Then, the source node encodes the k packets, and sends the encoded packets to the next hop. When k is equal to 50, the minimum time interval for transmitting a block between two neighbor nodes is approximately 60 s, which is in compliance with the requirements of the limited transmission time between two neighbor nodes in dynamic UANs. By setting the block size k appropriately, RCHF can control the transmission time, allowing the receiver to be able to receive sufficient encoded packets to reconstruct the original block even when the nodes are moving. Application data are transferred from a source node to a sink node block by block and each block is forwarded via RLT coding hop-by-hop.

## Slide 16: Two Transmission Constraints

## Slide 17: RLT Code based Handshake-Free Reliable Transmission Protocol

## Slide 18: RLT Code based Handshake-Free Reliable Transmission Protocol

## Slide 19: State-Based Handshake-Free Media Access Control
Each node maintains one dynamic neighbor table that includes a state field containing the real-time state of neighbor nodes as shown in Table 4.2
Value | State
0 | sending state
1 | receiving frame from other nodes
2 | unknown state
3 | transmission-avoidance
Table 4.2. The state table of neighbor nodes

## Slide 20
When a node has packets to send, it searches the neighbor table for the state field of the intended receiver. If the state is “0” or “1”, it will delay delivery until the state is greater than one; otherwise, the node becomes a sender, switches into the transmission phase and starts to deliver frames. The pseudocode for sending packets is omitted.
State-Based Handshake-Free Media Access Control

## Slide 21: Simulation Scene
All simulations are performed using Network Simulator 2 (NS2) with an underwater sensor network simulation package extension (Aqua-Sim). Our simulation scenario is similar to reality; one hundred nodes are distributed randomly in an area of 7000 m×7000 m×2000 m

## Slide 22: Simulation Parameters
Parameter | Value
Block Size | 50
Packet Length | 160 bytes
Bandwidth | 10 kbps
Routing protocol | static
Traffic | CBR
Transmission Range | 1500 m
MAC Protocol | 802.11
Table 4.4. Simulation parameters

## Slide 23: Simulation Result
Fig. 4.2. Performance vs. hop count

## Slide 24: Simulation Result
Fig. 4.3. Throughput vs. packet interval(s)

## Slide 25: Conclusion
In this chapter, a three-layer Micro-ANP protocol architecture for UANs is introduced. Furtherly, a kind of digital fountain code which is called as RLT is presented. RLT is characterized by small degree distribution and recursive encoding, so RLT reduces the complexity of encoding and decoding. Based on the Micro-ANP architecture and RLT code, a handshake-free reliable transmission mechanism-RCHF is presented. In RCHF protocol, frames are forwarded according to the state of the receiver which can avoid the sending-receiving collisions and overhearing collisions. Simulations show that RCHF protocol can provide higher delivery ratio, throughput and lower end-to-end delay.

## Slide 26: Conclusion
under the precondition of less resource consumption, guaranteed channel utilization and network throughput, combining the technologies of channel coding, cognitive underwater acoustic communication, data compression and post quantum public key cryptography, studying on secure and reliable data transmission is another future work.