## Slide 1: Chapter 18: Biometric Systems for User Authentication
Natarajan Meghanathan
Jackson State University, Jackson, MS, USA

## Slide 2
Biometrics: Comprises of methods for uniquely recognizing humans based upon one or more intrinsic physical or behavioral traits or identifiers.
  Used to authenticate users and grant or deny access control rights to data and system resources
Biometric identifiers can be divided into two main classes:
  Physiological: related to the body – often unique and can be used for identification as well as verification
    Examples: Fingerprint, Face recognition, DNA, Palm print, Iris recognition and etc.
  Behavioral: related to the behavior of a person – may not be unique for each person and can be used mainly for verification
    Examples: Typing rhythm, body mechanics (gait), voice, etc
Introduction to Biometrics

## Slide 3
Biometric identifiers are difficult to be lost or forgotten, difficult to be copied/shared, and require the person to be authenticated to be present at the time and point of authentication (a user cannot claim his password was stolen and misused!!)
Instead of passwords, biometric systems could be used to protect the strong cryptographic keys.
For a given biometric identifier, all users have a relatively equal security level – One user’s biometrics is no easier to break than another’s.
  There cannot be many users who have “easy to guess” biometrics that can be used to mount an attack against them.
Strength of Biometrics

## Slide 4
Verification: “Is this person truly Natarajan Meghanathan?”
  Applications: Computer network login, ATMs, Credit-card purchases, Physical access control, distance learning. In all these applications, the user identity is primarily evaluated through another mechanism. Biometrics is used to verify the claimed identity.
Identification: “Is this person in the database?”
  Determine if the input biometric sample is associated with any of a large number of enrolled identities
  Applications: Driver’s license, Voter ID cards, Missing children identification, Welfare-disbursement.
Screening: “Is this a wanted person?”
  To determine whether a person belongs to a watchlist of a moderate number of identities
  Examples: Airport security, Mass surveillance
  Screening applications don’t have a well-defined enrollment phase and have little control over their subjects and imaging conditions.
  Note: Screening can be accomplished only using Biometrics (not through Token-based or Knowledge-based identification).
Biometric Systems: Functionalities

## Slide 5
Verification Mode: “one-to-one comparison” with a stored template to verify that the individual is who he claims to be.
Identification Mode: “one-to-many comparison” against a biometric database to identify an unknown individual and establish the identity of the person as someone enrolled in the system.
  The comparison is considered successful if the biometric sample collected falls within threshold values for the characteristic.
Verification Mode – Enrollment vs. Subsequent Uses:
  The first time an individual uses a biometric system, it is referred to as enrollment. During the enrollment phase, biometric information from the individual is collected and securely stored in a database.
  During subsequent attempts, biometric information collected from the individual is compared with the information stored at enrollment time.
Examples of Biometric systems for user identification: Recognition systems based on fingerprint, iris, retinal scans
Examples of Biometric systems for user verification: Recognition systems based on face, speech, hand-geometry and signature
Two Modes of a Biometric System

## Slide 6
Basic Block Diagram of a Biometric System

## Slide 7
First Block (Sensor): An interface between the real world and the system; Used to acquire all the necessary data, depending on the characteristic.
Second Block (Pre-processing): Needed to enhance the input (i.e., remove all the background noise and unnecessary artifacts during data collection) and also to use some kind of normalization, if needed.
Third Block (Feature Extractor): Responsible to extract the necessary features from the pre-processed input in the correct and in the optimal way.
Fourth Block (Template Generator): The template is typically a vector of numbers or an image with particular properties, and is generally a synthesis of the relevant characteristics extracted from the source.
For enrollment, the template is typically stored in a central database (or sometimes within the biometric reader device itself or on a smartcard).
For matching, the obtained template is passed to a matcher that compares it with other relevant templates in the database and estimates the distance between them using any specific algorithm (e.g., the Hamming Distance metric) and returns the result of the evaluation to the application device, which will then decide how to handle the user being evaluated.
Description of the Block Diagram

## Slide 8
False Accept Rate (FAR, a.k.a. False Match Rate): It is a measure of the percent of invalid inputs that are incorrectly accepted.
  It is the probability that the system incorrectly matches the input pattern to a non-matching template in the database.
False Reject Rate (FRR, a.k.a. False Non-match Rate): It is a measure of the percent of valid inputs that are incorrectly rejected.
  It is the probability the system fails to detect a match between the input pattern and a matching template in the database.
Relative Operating Characteristic: It is a curve drawn between the False Accept Rate vs. the False Reject Rate.
  The shape of the curve depends on the threshold value set for acceptance. If the threshold value (for the difference or the distance between the templates – tolerance to input variations and noise) is too small, the FAR would be low, but the FRR would also be high. If the threshold value is too high, the FAR would be high, but the FRR would be low.
Performance Metrics

## Slide 9
Crossover Error Rate (CER): The rate at which both the accept and reject errors are equal.
  A lower CER value is desired for a biometric system in order to be considered more accurate and convenient for its users.
Failure to Enroll Rate (FER): The rate at which attempts to create a template from an input is not successful.
  This is most commonly caused by low quality inputs that are insufficiently distinctive biometric samples or from a system that makes it difficult to provide consistent biometric data.
  Retinal scans require high precision – so people with diabetes, blood pressure cannot be considered for such systems.
Tradeoff: Larger the FER, lower the FAR and FRR; and vice-versa.
Failure to Capture Rate (FCR): The probability that the system fails to detect a biometric input when presented correctly.
Template Capacity: The number of unique users that can be represented by its contents.
Performance Metrics

## Slide 10
Fingerprint Recognition (Authentication) is an automated method of verifying a match between two human fingerprints to identify an individual and verify their identity.
Fingerprint analysis requires comparison of several features of the print pattern and minutia points.
Print patterns represent aggregate characteristics of ridges, while minutia points represent unique features found within the patterns.
The three basic patterns of fingerprint ridges are the arch, loop and whorl.
The major minutia features of fingerprint ridges are: ridge ending, bifurcation and short ridge (dot).
Minutia and patterns are very important in the analysis of fingerprints since no two fingerprints (even for the same person) have been proven to be identical.
Fingerprint Recognition

## Slide 11
Fingerprint Ridge Patterns
Fingerprint Minutia Features
Arch
Loop
Whorl
Ridge Ending
Bifurcation
Short Ridges (Dots)
(adapted from
Jain et al., 2006;
Cao and Jain, 2015)

## Slide 12
The method involves capturing the detail-rich, intricate structures of the iris using near infra-red illumination (NIR, 750 nm wavelength) that would reduce the reflection (would be very noisy if visible light was used) from the cornea.
The images captured through the infra-red camera are converted to digital templates to provide mathematical representations of the iris that yield unique positive identification of an individual.
Iris (Plural: Irides) is a thin, circular structure in the eye, responsible for controlling the diameter and size of the pupil (the black hole) and the amount of light reaching the pupil.
Iris Recognition

## Slide 13
Although, NIR-based Iris images are less noisy and are of good quality, NIR is insensitive to the melanin pigment (the color pigment) in the Iris.
On the other hand, visible wavelength (VW) imaging could also capture melanin, which would additionally provide rich sources of information mainly coded as shape patterns in Iris.
With effective noise-filtering techniques and feature extraction methods, images captured from both NIR and VW spectrum could be fused to obtain templates that could provide high accuracies of recognition in large databanks.
Iris Image: Visible Wavelength vs. NIR
VW-Iris Image
NIR-Iris Image
(adapted from Chandra Murty et al., 2009; Jain et al., 2006)

## Slide 14
Iris is an internal organ that is well protected against damage and war by a highly transparent and sensitive membrane (the cornea). This distinguishes it from fingerprints, which can be difficult to recognize after years of certain types of manual labor.
The Iris is mostly flat and its geometric configuration is only controlled by two complementary muscles that control the diameter of the pupil. Hence, the shape of Iris is more predictable than other structures.
The Iris texture (like fingerprints) is formed randomly during embryonic gestation (8th month); even genetically identical twins (similar DNA print) will have completely independent Iris textures.
Unlike fingerprinting or retinal scanning (wherein the eye has to be brought very close to a microscopic lens), the image of the iris can be captured from about 10 cm to a few meters away and there is no need for the person to be identified to touch any equipment.
Iris recognition systems are considered one of the swiftest biometric technologies for one-to-many identification with a very low false acceptance rate as well as a low false rejection rate.
The Iris texture can be remarkably stable for more than 30 years, barring very few medical and surgical procedures or trauma.
Advantages of Iris Recognition

## Slide 15
Live-tissue Verification Problem: Iris recognition systems are vulnerable to the problem of live-tissue verification.
  Any biometric identification system has to ensure that the signal acquired and compared has actually been recorded from a live body part of the person to be identified and is not a manufactured template.
  Many commercially available Iris-recognition systems are easily fooled by presenting a high-quality photograph of a face instead of a real face. This makes Iris-recognition systems unsuitable for unsupervised applications like door access-control systems.
The problem of live-tissue verification is of less concern in supervised applications (like immigration control), where a human operator supervises the process of taking the picture.
Security Considerations

## Slide 16
Retina is a light-sensitive tissue lining the inner surface of the eye.
The network of blood vessels (capillaries) that supply blood to the retina is so complex and is unique for every person, including genetically identical twins.
Like Iris texture, the retina remains largely unchanged from birth until death and hence a retinal scan image is considered to be very precise and reliable metric with an error rate of one in a million.
A retinal scan is performed by casting an unperceived beam of low-energy infrared light into a person’s eye as they look through the scanner’s eyepiece.
  Capturing a retinal scan is the most difficult among the biometric technologies as retina is small, internal; the user has to be perfectly still.
The retinal blood vessels are more absorbent of the infra-red light than the rest of the eye and the reflection patterns of the light is captured as a computer code and stored in a database.
Retinal patterns are likely to be altered in cases of diabetes, glaucoma, cataracts or severe astigmatism.
Retinal Scan

## Slide 17
A facial recognition system is used to automatically identify or verify a person from a digital image or a video frame from a video source.
  One way to do this is to compare selected facial features (that are not easily altered – upper outlines of the eye sockets, the areas around the cheekbones, and the sides of the mouth) with those in the database.
Key Advantage: It does not require consent from the rest subject.
  Properly designed systems installed in airports, multiplexes, and other public places can identify individuals (though the correctness is often questionable!!) among the crowd.
  Other biometric systems like fingerprints, iris scans, retinal scans cannot be used for in mass identification (surveillance).
Weaknesses:
  Sensitive to facial expressions and the frontal orientation at which the photo is taken.
  Privacy concerns
Face Recognition Systems

## Slide 18
Speaker recognition systems discriminates between speakers by making use of the combination of physiological differences in the shape of vocal tracts and learned speaking habits.
Speaker recognition systems are mostly passphrase-dependent so that it can provide an added security feature (rather than being text-independent – such systems are also available).
During the enrollment phase, a user is required to speak a particular passphrase (like a name, birth date, birth city, favorite color, a sequence of numbers, etc) over a microphone for a certain number of times.
This phrase is converted from analog to digital format, and the distinctive vocal characteristics such as pitch, cadence, and tone, are extracted, and a speaker model is established. A template is then generated and stored for future comparisons.
Speaker recognition is often used where voice is the only available biometric identifier, such as telephone and call centers.
Speaker Recognition Systems

## Slide 19
Unlike fingerprints, human hand is not unique. However, hand geometry-based biometrics is not as intrusive as a fingerprint recognition system and hence may be sufficient enough to be used for verification; but, not for identification.
Feature extraction involves computing the widths and lengths of the fingers at various locations using the captured image. These metrics define the feature vector of the user’s hand.
Hand Geometry may not be invariant during the growth period.
The presence of Jewelry (e.g., rings) or limitations in dexterity (e.g., arthritis) may pose challenges in extracting the correct hand geometry information.
The physical size of hand geometry systems is large and it cannot be embedded in certain devices such as laptops.
Environmental factors like dry weather or individual anomalies such as dry skin, do not appear to have any negative effects on the authentication accuracy of hand geometry-based systems.
Hand Geometry Based Biometrics

## Slide 20
Signature recognition refers to authenticating the identity of a user by measuring handwritten signatures.
In a signature recognition system, a person signs his or her name on a digitized graphics tablet or a PDA.
The signature is treated as a series of movements that contain unique biometric data, such as personal rhythm, acceleration, stroke order, stroke count and pressure flow.
The signature dynamics information is encrypted and compressed into a template.
Signature recognition systems (for hand signatures) measure how a signature is signed and are different from electronic signatures, which treat a signature as a graphic image.
Signature Recognition Systems
Source: http://www.gao.gov/new.items/d031137t.pdf

## Slide 21
Universality – each person should have the characteristic
Uniqueness – how well the biometric separates one individual from another
Permanence – how well the biometric resists aging and other variations over time
Collectability – ease of acquisition for measurement
Performance – accuracy, speed and robustness of technology used.
Acceptability – degree of approval of a technology by the public/ users of the biometric
Circumvention – ease of use of a substitute
Parameters considered for Selecting a Human Characteristic

## Slide 22
Technologies vs. Parameters
Biometric Identifier | Parameters/ Factors to Choose a Biometric Technology |  |  |  |  |  | 
 | Universality | Distinctiveness | Permanence | Collectable | Performance | Acceptability | No Circumvention
Face | Best | Best | Avg | Best | Poor | Best | Poor
Fingerprint | Avg | Best | Best | Avg | Best | Avg | Avg
Hand Geometry | Avg | Avg | Avg | Best | Avg | Avg | Avg
Iris | Best | Best | Best | Avg | Best | Poor | Best
Signature | Poor | Poor | Poor | Best | Poor | Best | Poor
Voice | Avg | Poor | Poor | Avg | Poor | Best | Poor

## Slide 23
Attacks on biometric systems could be categorized into two types:
  Zero-effort Attacks: The biometric identifiers of an opportunistic intruder may be sufficiently similar to a legitimately enrolled individual, resulting in a False Accept.
    This is equivalent to the problem of finding the probability that the biometric data originating from two different individuals will be sufficiently similar.
Adversary Attacks: A determined impostor masquerades as an enrolled user by using a physical or a digital artifact of a legitimately enrolled user. Under these attacks, an individual may also deliberately manipulate his/her biometric identifier in order to avoid detection by an automated biometric system.
Attacks on a Biometric System
Source: A. K. Jain, A. Ross and S. Pankanti, “Biometrics: A Tool for Information
Security,” IEEE Transactions on Information Forensics and Security, vol. 1, no. 2,
pp. 125 – 143, June 2006.

## Slide 24
Circumvention: An intruder gains access to the system by using data pertaining to a legitimately enrolled user.
Repudiation: A legitimate user may access the facilities offered by an application and claim that an intruder had circumvented.
Collusion: An individual with super-user privileges (such as an administrator) may deliberately modify biometric system parameters to permit incursions by a collaborating intruder.
Coercion: An impostor may force a legitimate user (e.g., at gunpoint) to grant him access to the system.
Denial of Service (DoS): An attacker may overwhelm the system resources to the point that legitimate users will be refused service.
  Example: An attacker may bombard a server processing access requests, with a large number of bogus requests, thereby overloading its computational resources and preventing valid requests from being processed.
Subcategories of Adversary Attacks
Source: A. K. Jain, A. Ross and S. Pankanti, “Biometrics: A Tool for Information Security,” IEEE Transactions on Information Forensics and Security, vol. 1, no. 2, pp. 125–143, 2006.

## Slide 25
Motivation: Intraclass variations and Interclass similarities
Non-universality – While every user is expected to possess the biometric identifier being acquired, in reality, it is possible for a subset of the users to be not able to provide a particular biometric.
Spoof attacks – An impostor may attempt to spoof the biometric identifier of a legitimate enrolled user in order to circumvent the system.
Advantages – A Multi-biometric system could
  Address the problem of non-universality, since multiple biometric identifiers would ensure sufficient population coverage.
  Provide anti-spoofing measures by making it difficult for an intruder to simultaneously spoof the multiple biometric identifiers of a legitimate user.
  Ensure a “live” user is present at the point of data acquisition by asking the user to present a random subset of the multiple biometric identifiers (for example: right index and left middle finger, left hand and so on).
Overall, multi-biometric systems could facilitate a challenge-response kind of authentication.
Multi-Biometric Systems

## Slide 26
Serial Mode – The output of the matching operation on one biometric identifier could be used to narrow down the records to be searched for to validate the sample corresponding to the other biometric identifier.
  With the serial mode, there is no need to simultaneously collect the biometric samples corresponding to all the biometric identifiers.
Parallel Mode – The sample for each biometric identifier is simultaneously processed to decide on the final recognition. When operated in the parallel mode, we need to simultaneously collect the biometric samples corresponding to all the multiple identifiers beforehand.
Multi-Biometric Systems: Modes of Operation

## Slide 27
Sensor-Level Fusion: The raw data obtained from multiple sensors (one for each biometric identifier) can be processed and integrated to generate new data from which features can be extracted.
Feature-Level Fusion: The feature sets extracted from each biometric identifier sources can be fused to create a new feature set to repesent the individual.
  Example: The geometric features of the hand and the Eigen-coefficients of the face may be fused to obtain a new high-dimension feature vector
Match Score-Level Fusion: The match scores obtained from each biometric classifier are normalized and the normalized scores are summed to obtain a new match score – used to make the final decision.
Decision-Level Fusion: The decisions (Accept/ Reject) made at each biometric system based on the individual scores are then combined (usually a majority voting approach) to arrive at a final decision.
Levels of Fusion: Parallel Mode Multi-Biometric Systems

## Slide 28
Tightly-coupled fusion: The sensor-level and feature-level fusion techniques are considered to be tightly-coupled as the raw data and the feature vectors convey the richest information about different identifiers.
  However, it is more difficult to perform a combination at the feature level because the relationship between the feature spaces of different biometric systems may not be known and the feature representations may not be compatible.
  Also, if the individual biometric systems are developed by different commercial vendors, different feature values may not be accessible and comparable. In such scenarios, loosely-coupled fusion systems (at the score or decision level) have to be chosen.
Loosely-coupled fusion: There is little or no interaction among the biometric inputs and the fusion occurs at the output of relatively autonomous biometric authentication systems that independently assesses the input from their own perspective.
Tightly Coupled vs. Loosely Coupled Multi-Biometric Systems
Source: A. K. Jain, A. Ross and S. Pankanti, “Biometrics: A Tool for Information Security,” IEEE Transactions on Information Forensics and Security, vol. 1, no. 2, pp. 125 – 143, June 2006.

## Slide 29
Feature-Level Fusion in Multi-Biometric Systems
Adapted from: A. K. Jain, A. Ross and S. Pankanti, “Biometrics: A Tool for Information Security,” IEEE Transactions on Information Forensics and Security, vol. 1, no. 2, pp. 125 – 143, June 2006.

## Slide 30
Score-Level Fusion in Multi-Biometric Systems
Adapted from: A. K. Jain, A. Ross and S. Pankanti, “Biometrics: A Tool for Information Security,” IEEE Transactions on Information Forensics and Security, vol. 1, no. 2, pp. 125 – 143, June 2006.

## Slide 31
Decision-Level Fusion in Multi-Biometric Systems
Adapted from: A. K. Jain, A. Ross and S. Pankanti, “Biometrics: A Tool for Information Security,” IEEE Transactions on Information Forensics and Security, vol. 1, no. 2, pp. 125 – 143, June 2006.