## Slide 1: Chapter 22: Experimental Digital Forensics of Subscriber Identification Module (SIM) Card
Mohamed T. Abdelazim, Nashwa Abdelbaki, and Ahmed F. Shosha

## Slide 2
SIM Cards Overview
Developing Environment
SIM Communication Protocols
SIM File System
Data Acquisition
SIM Card Forensic Methodology
SMS Forensic
Experimental Results
Conclusion
References
Agenda

## Slide 3: SIM Cards Overview
Properties
  Subset of smart cards
  Stand alone embedded system
  Consists of EEPROM, Processor, FLASH
SIM Usage
  GPS devices
  Identifying the user over cellular network

## Slide 4: SIM Cards Overview
Literature survey
  No public research related to SIM cards
  Available forensic tools
    Outdated and unsupported
    Not an open-source
    Customized to a specific hardware

## Slide 5: Development Environment
90% of used smart cards including SIM cards use JAVA card.
Java card is based on four main components
  Java virtual machine: used for application installation and defining the features and services.
  Java runtime: which handles context switching between applications.
  Java API: which is a set of classes and interfaces to allow the application to use card services.
  Java Card Programming Language: Java cards inherit its security measures from Java programming. This environment allows multi application to be installed and run, which allow developing application or even malwares.

## Slide 6: SIM Communication Protocols
SIM cards relay on two major protocols
  Application Protocol Data Unit (APDU)
  Attention (AT)
Communication consist of a series of commands
  Request Command
  Response Command

## Slide 7: SIM Communication Protocols
Application Protocol Data Unit (APDU)
  By constructing the command byte
  Based on PC/SC standrd
  APDU Request Command

## Slide 8: SIM Communication Protocols
Application Protocol Data Unit (APDU)
  APDU Response Command

## Slide 9: SIM Communication Protocols
Application Protocol Data Unit (APDU)
  Example:-
    If we want to update one record at the address “6F42” then we have to follow the following set of instructions.

## Slide 10: SIM Communication Protocols
Application Protocol Data Unit (APDU)
  Example Cont.:-
    APDU for select 3F00 using the command “A0A40000023F00” where 3F00 is the address for the root directory.
    APDU for select 7F10 under 3F00 using the command “A0A40000027F10” where 7F10 is the directory holding the requested files.
    APDU to select 6F42 under 7F10 using the command “A0A40000026F42” where 6F42 is the requested file under the directory.
    APDU to update record 1 of 6F42 to “534D532043454E545245FFFFE1FFF...”

## Slide 11: SIM Communication Protocols
Attention (AT)
  Well defined API from GSM standard
  These APIs have two types
    API for specific information on SIM
      Ex: AT+CCID
    General purpose API which relate to memory address
      Ex: AT+CRSM=176,12258,0,0,10

## Slide 12: SIM Communication Protocols
Attention (AT)
  AT Request Command
    AT+CRSM=<command>[,<filed>[,<P1>,<P2>[,<data>]]]

## Slide 13: SIM Communication Protocols
Attention (AT)
  AT Response Command
    +<command>: <SW1>, <SW2>[, <response>]
    <command>: Note for executed command.
    <SW1, SW2>: Represent the response status which could indicate correct execution or error with the execution. Using both SW1 and SW2 we can identify the error from non-supported commands, incorrect parameters, or denied permission. The size for both SW1 and SW2 is two bytes length. Table 4 summarizes the possible different response values for SW1, SW2.
    <response>: This field hold the data extracted from the SIM card as a result of command execution.

## Slide 14: SIM Communication Protocols
Command Execution State
  After each command execution included in command response.
  The command state represented by two values, SW1, SW2
  Both values indicate the execution state

## Slide 15: SIM Communication Protocols
AT vs APDU Commands
  APDU command can only be used if the SIM reader supports PC/SC specifications, however AT commands can be used with standard communication protocols like serial communication.
  APDU and AT commands have the same structure with different implementation, however APDU commands have more functionality over AT commands.
  AT commands are an abstraction layer for APDU commands where they have limited functionality mapping.
  Using APDU commands will require knowing the SIM behavior, structure and command sequence in order to extract the needed information which can be achieved with executing multiple commands; however using AT commands will allow data retrieval with a single command.
  Installing/uninstalling new software “applet” requires the use of APDU commands where there is no AT commands for installing or un-installing applets from SIM card.

## Slide 16: SIM File System
SIM cards file system consists of three types identifiers
  Main Files (MF): reside at memory address 0x3F00. MF are considered the root directory for SIM file system
  Dedicated Files (DF): represent the application level for each service provided by SIM such as directories.
  Elementary Files (EF): hold the actual information which needs to be extracted for digital forensics.

## Slide 17: SIM File System
Each file can have one of five permissions
  Always: the file is valid without any permissions and always accessible.
  Card Holder Verification 1(CHV1): the file is protected by user’s PIN code.
  CHV2: the file is protected by user’s PIN2 code.
  Admin (ADM): the file can only be accessed after having the appropriate administrative authority.
  NEVER: the file cannot be accessed.

## Slide 18: SIM File System
Each Elementary File can has one of three data structure
  Transparent EF: An EF with a transparent structure consists of a sequence of bytes. When reading or updating, the sequence of bytes to be acted upon is referenced by a relative address (offset), and the number of bytes to be read or updated. The total data length of the EF’s body indicated in the EF’s header.
  Linear fixed EF: An EF with a linear fixed structure consists of a sequence of records that have the same (fixed) length.
  Cyclic EF: Cyclic files are used for storing records in chronological order. When all records are used for storage, then the next storage of data shall overwrite the oldest information.

## Slide 19: SIM File System
Each file identifier has file header which specify the file properties.
  There are two forms of file header based on SIM type
    SIM/USIM: which is 15 byte header
    UICC: which is variable header length

## Slide 20: Data Acquisition
Using general purpose AT commands
Brute Force the memory addresses range
Extracting the file identifiers header
Reading file data based one file type

## Slide 21: Forensic Methodology

## Slide 22: SMS Forensic
Commonly used 40 location for SMS on SIM card each record of size 176 byte
SMS file identifier is cyclic
Each record has two parts
  Frist byte is the status for identifying the SMS type
  The remaining 175 for payload
If the first byte is “00” then its and empty record and the payload will be set initially to “FF”
In case of SMS deletion the record will be reinitialized to its original values

## Slide 23: Experimental Results
Case 1: Old/Fresh SIM Forensic
  Extracted SIM CCID, IMSI, SMS, Phonebook, PIN status, and others

## Slide 24: Experimental Results
Case 2: Blank SIM Forensic
  After adding some random data we tried to extract it again.

## Slide 25: Experimental Results
Case 3: PIN Key Enabled/Disabled Forensic
  When PIN key is enabled all the data are protected
  When PIN key is disabled we can retrieve the information form the SIM

## Slide 26: Experimental Results
Case 4: Timeline and Event Reconstruction
  In this experiment we sent, received and removed some SMSs to build Timeline for the saved SMSs
Empty Location
Received SMS

## Slide 27: Experimental Results
Case 5: SIM/USIM Header Extraction
  Extracted two different file types
    Elementary file
    List of records

## Slide 28: Conclusion
  Data can be extracted as long as PIN key is not active
  SMS can be recovered as long as it has not been deleted or overwritten
  AT commands are easy to use but has limited functionality however it has no dependency on hardware so USB modem can be used as SIM reader
  PIN key has only 3 attempts after that the SIM is locked and can only be unlocked using PK which has also 3 attempts and then the SIM is destroyed.

## Slide 29: References
  AbdelAzim, M., 2016. Simanalyzer Tool. https://github.com/Tabaz/SIMAnalyzer. Accessed 30 January 2017
  Casadei, F., Savoldi, A. and Gubian, P., 2006. Forensics and SIM cards: an Overview. International Journal of Digital Evidence, 5(1), pp.1-21.
  ETSI, T., 100 977 v8.14.0, 2007. Digital cellular telecommunications system (Phase 2+); Specification of the Subscriber Identity Module-Mobile Equipment (SIM-ME) Interface. ETSI Standards,European Telecommunications Standards Institute, Technical Specification.
  ETSI, T., 131 102 V4.15.0, 2005. Universal Mobile Telecommunications System (UMTS); Characteristics of the USIM application, European Telecommunications Standards Institutee.
  ETSI, T., 100 916 V7.8.0, 2003. Digital cellular telecommunications system; AT command set for GSM Mobile Equipment (ME), European Telecommunications Standards Institute.
  ETSI, T., 143 019 V5.6.0, 2003. Digital cellular telecommunications system (Phase 2+); Subscriber Identity Module Application Programming Interface (SIM API) for Java Card; ETSI Standards, European Telecommunications Standards Institute, Technical Specification.
  ETSI, T., 100 901 V7.5.0, 2001. Digital cellular telecommunications systems (Phase 2+), technical realization of the short message service (SMS) point-to-point (PP), European Telecommunications Standards Institute, Technical Specification.
  Guo, H., Smart cards and their operating systems.
  Ibrahim, N., Al Naqbi, N., Iqbal, F. and AlFandi, O., 2016. SIM Card Forensics: Digital Evidence.
  I. Oracle, Java card technology, http://www.oracle.com/technetwork/java/embedded/javacard/overview/getstarted-1970079.html. Accessed 30 January 2017
  I. Sun Microsystems, 1998. Java Card Applet Developers Guide.
  Jansen, W.A. and Delaitre, A., 2007, October. Reference material for assessing forensic SIM tools. Security Technology, 2007 41st Annual IEEE International Carnahan Conference on Security Technology (pp. 227-234). IEEE.
  Jansen, W. and Ayers, R., 2006, January. Forensic software tools for cell phone subscriber identity modules.In Proceedings of the Conference on Digital Forensics, Security and Law (p. 93). Association of Digital Forensics, Security and Law.
  Osmocom, Osmocom simtrace, http://bb.osmocom.org/trac/wiki/SIMtrace. Accessed 30 January 2017
  Rankl, W. and Effing, W., 2004. Smart card handbook. John Wiley & Sons.
  Thakur, R., Chourasia, K. and Singh, B., 2012. Cellular Phone Forensics. International Journal of Scientific and Research Publications, 2(8).