## Slide 1: Chapter 23: A Dynamic Area-Efficient Technique to Enhance ROPUFs Security against Modeling Attacks

## Slide 2
Ring Oscillator (RO) PUFs are one of the most appropriate techniques for the security of silicon chips [14] since it is a proven technique to provide high performance in terms of reliability and uniqueness of its generated response.
However, compared to other silicon PUFs (SPUFs), ROPUF can only offer a limited number of challenge-response pairs (CRPs) for generation of secure binary responses. For this reason, ROPUF is categorized as weak SPUF which can be more vulnerable to modeling attacks [1].
Introduction

## Slide 3
Number of CRPs in ROPUF design is related linearly to the number of components that are used to construct a ROPUF design whose behavior depends on the random manufacturing process variations. Due to these limitations, an adversary may try all challenges and know the corresponding responses that is linear to number of applied challenges, within a certain time [1].
In this regard, a dynamic technique namely d-ROPUF that offers multiple CRPs behaviors to increase ROPUF unpredictability, which in turn enhances its unclonablity against modeling attacks, is proposed.

## Slide 4
The proposed technique is an area-efficient ROPUF design that utilizes the dedicated FPGA logic (dedicated multiplexers, LUTs, fixed routings) to accommodate four multi-stage structures in a single CLB using Programmable XOR gates (PXORs) that control the individual RO frequencies. In addition, a reconfiguration mechanism is appropriately designed to automatically alter the behavior of CRPs and reconfigure the design into new structures with different stages (invertors). Hence, the design can generate updated secret keys and consequently becomes highly unpredictable and secure against modeling attacks.

## Slide 5: Basic and Configurable Silicon PUFs
Arbiter PUFs (APUFs) [7] and Ring Oscillators PUFs (ROPUFs) [8] are silicon based PUFs that take into consideration the process variations of Integrated Circuits (ICs) in order to produce random responses.

## Slide 6
In 2004, Lee et al [8] used a switch box structure to create a race between two delay paths with an arbiter at the end. The basic circuit of APUF is presented in Fig. 1 Two identical delay paths are formed to produce a response bit based on the fastest path. The arbiter is placed at the end of the circuit (D-latch) to decide the winning signal that reaches first.
Fig. 2 shows the original ROPUF design for extracting unique signatures. These signatures are produced using challenge response mechanism and are difficult to clone or predict [7]. As shown in Fig. 2, ROPUF circuit compares the two frequencies fi and fj, in order to produce 0 or 1 output based on frequency that is higher. The measured process variations should be unique for each RO [7].

## Slide 7
In 2007, a 1-out-of-k technique was also proposed by Devadas to improve the reliability factor of RO PUFs [7]. This technique was named the redundancy approach which selects 1-RO pair among k-RO pairs that has the maximum frequency difference. The major disadvantage of this technique lies in its area inefficiency since k times more area is wasted when it is implemented on FPGAs.
In 2009, Maiti [6] introduced the notion of configurable ROPUFs (c-ROPUF) for better reliability. As shown in Fig. 3, he overcame the 1-out-of-k scheme drawback by offering a configurable design which occupies the same amount of area with more number of ROs.
However, Maiti did not propose his method for stronger secret key production.

## Slide 8
An improved version of the configurable ROPUF by Maiti [5] that can generate stronger response bits while using the same amount of area is proposed by Xin [2], and Amsaad in Fig. 4 [9].

## Slide 9: Implementations of the Proposed Technique on real hardware

## Slide 10
As shown in Fig. 6, for area efficiency the proposed design is mapped inside one CLB taking advantage of the identical nature of internal routings that connect LUTs to two levels of dedicated MUXs (F5, F6) with fixed routing delays [9]. Internal routings guarantees identical RO loops in different CLBs and eliminates the local noise caused by dynamic routings [9].A RO loop in a d-ROPUF structure is a circuit composed of odd number of inverters that are serially connected.
Single CLB in Spartan-3E FPGAs contains four slices and eight LUTs (2 LUTs per slice). Each of these eight LUTs can be configured as an inverter or a buffer. In order to have odd number of inverters (1, 3, 5, and 7), seven LUTs are configured as inverters and one LUT as a buffer using PXOR gates.

## Slide 11
These LUTs are connected with the help of internal CLB routings and four different structures are built inside a single CLB. As seen in Fig. 6, the red lines connect the enable signal (VDD) to activate the selected CLB and also configure LUTs as controlled inverters (PXORs).
There is only one LUT that is configured as a buffer (connected to ground signal) which adds extra delay to keep the generated frequency for one-stage inventor RO structure less than 300 MHz, that is the maximum operational value of Spartan 3E FPGA frequency.
Likewise, different LUTs are shown in different colors and connected using different colored lines to show how four ROPUF structures are mapped using internal CLB routings.

## Slide 12
Fig. 7 shows the
proposed technique for an FPGA area. A 0.1 ms delay is provided prior to the activation of each counter, so that the signal is stabilized before the actual RO frequency
measurement starts [9, 13].

## Slide 13
To implement the design on the entire area of FPGA, we divided each chip into top and bottom area (120 CLBs). To avoid self-heating noise of the neighboring ROs, each RO in our design is activated for a shorter time 0.1 ms (activation period) with a step size of 5,000 clock cycles [13].
A deactivation period of 0.1 ms is also allowed before activating the next RO. The timing controller shown in Fig. 7 controls the activation, and deactivation periods of the individual ROs, the challenge generator, 120 decoder and encoder, the main and reference counters using T1 and T2 signals.
Once the T1 signal is received by the challenge generator, input challenge is send to the decoder and encoder, hence a single RO is activated for 0.1 ms.

## Slide 14
At the end of this period, the main counters receive T2 from the timing controller and starts counting the number of clock cycles that is generated by the activated RO. At the same time, the reference counter receives the T2 signal and counts for 0.1 ms (5,000 clock cycles) before it stops the main counter by sending RC signal.
At the end of the second 0.1 ms period, the main reference and main counters will be deactivated and a control RC signal is sent by the reference counter to the main counter.
Once the main counter receives RC signal, it stops counting and forwards the counted number of clock cycles through a 16-bit data bus to an Agilent logic analyzer. A third 0.1 ms is given before the main counter sends T1 signal to activate another RO.

## Slide 15: Experimental Results
Table 1 shows that, the value of Mean and Median of all structures are very close to each other which indicates that RO sample frequencies are more likely normally distributed.
A distribution is considered normal (symmetric) when the right and left sides of the graph are approximately mirror images of each other.
The normality of RO sample frequencies

## Slide 16
For a symmetric distribution, the Skewness and Kurtosis values are equal to zero. As seen in Table 2, one stage structure is skewed to the right since it has a positive Skewness value. Furthermore, one and seven stage structures are closest to the symmetric distribution because its Skewness is closest to zero. On the other hand, three and five stage structures appear to have the highest Skewness to the left.
As far as Kurtosis is concerned, since three and five stages are closer to zero, they tend to have more readings near the center and are closer to normality.

## Slide 17
Fig. 8 show the distribution of average sample frequencies of each structure for all 30 FPGAs.
To accurately determine the normality of RO frequencies for each structure, we perform two different statistical tests using IBM-SPSS software namely: Kolmogorov-Smirnova and (K-S) Shapiro- Wilk (S-W) for each r-ROPUF structure.

## Slide 18
From Table 3 it is observed that, the five and seven stages d-ROPUF structures are at the lower bound of the significance value which is 0.200. However, the one and three stages reconfigurations are closer to zero (0.003 and 0.29) which indicates that their RO frequencies are more random.

## Slide 19: Loop parameters of ROPUF Model
Diverseness of RO is sum of average diverseness, process variation diverseness and diverseness due to noise [2]. Average diverseness and variability represents the standard deviation and variance of RO frequencies. Variability is simply the square of diverseness whereas the diverseness of ROs is calculated as follows:

## Slide 20
As seen in Table 4, average diverseness and variability of the individual RO frequencies decrease with increase in the number of stages. This in turn indicates that lesser the number of stages, more reliable is the ROPUF response [4, 12].
dAVG is fixed for ROs which represent the average frequency of the identically instantiated RO loops. However, the percentage of intra-die process variation dPV varies from one RO loop to other which is shown in Table 5.

## Slide 21
As shown in Fig. 9, average process variation (dPV) is in the range 0.8% - 1.18%, with an average of 0.92% and a standard deviation of 0.18%. A higher process variation implies a higher d-ROPUF performance [3, 8, 12]. From the same figure we notice that, a d-ROPUF structure with less number of stages has higher static process variation compared to the one with more number of stages. This indicates that, a d-ROPUF structure with less number of stages is more reliable to authenticate chips.

## Slide 22: Correlation between d-ROPUF structures and their Performances
Pearsons correlation coefficient is used to study the relationship between each d-ROPUF structure and its performance. Pearsons correlation coefficient r describes the type of relationship between a dependent variable V (variability) and an independent variable S (number of stages of each d-ROPUF) as follows:

## Slide 23
In statistics, variability is always a positive value that is used to estimate how far apart a set of numbers is spread from the mean value. Low variability means that data points are very close to the mean, while a high variance value indicates that data points are quite far off from the mean value.
Table 6, shows that there is a strong negative linear relationship between d-ROPUF structures and its performance factors in terms of average diverseness and average variability

## Slide 24
Fig.10 (a) and (b) shows the average frequencies of 22 CLBs. 1-stage and 3-stages RO structures have a greater frequency variation compared to 5-stage and 7-stages RO structures. While ROs with 5 and 7 stages vary only by (variability) 0.56 and 0.61 MHz respectively, 1 and 3 stages RO structures have been shown to vary by 4.4 and 9.1 MHz respectively.
A low variability indicates that the RO structures are more vulnerable to bit flip occurrence.

## Slide 25: Quality Metrics of d-ROPUF structures
Uniqueness factor shows how unique is the generated output for different chips. Average inter-die Hamming Distances (HDs) is used to evaluate the uniqueness between two chips, u and v with n-bit responses, Ru and Rv respectively, at normal operating conditions as shown:
The uniformity metric shows how well distributed are the percentage of 0’s and 1’s in the generated response bits of a certain chip.

## Slide 26
where, rs;i is the ith response bit among n response bits. Ideal uniformity of PUF responses is 50% which means that RO responses are well distributed between 0’s
and 1’s in a certain chip.
Bit-aliasing also measures how distributed is the percentage of 0’s and 1’s in the responses across multiple chips. Ideal bit-aliasing of PUF responses is 50%
Uniformity is calculated using intra-die Hamming Weights (HWs) as follows:

## Slide 27
Reliability measures how efficient are a PUF structure in reproducing the same response bits using the same RO pair when the operating condition changes. For a certain challenge, reliability can be evaluated by calculating Hamming distance between rs, rt the tth response bit from a chip at room temperature (normal operating condition), and rs,rt the tth response bit from the same chip at varying operating condition.
ROPUF reliability and bit flips percentage are calculated as follows:

## Slide 28
Table 7 shows the obtained result for the top and bottom values of uniqueness, uniformity and bit aliasing.
For the bottom area of FPGA, the uniqueness of 1-stage ROs have the highest value whereas the 5-stage ROs have the lowest. However, all the values are above 45% which indicates a good uniqueness value.
The average uniformity and bit aliasing results for all stages taken into account can be considered good since the values are close to 50%.

## Slide 29
Fig. 11 shows the average total number of bits flipped due to temperature and voltage variations. We notice that the environmental variations have fairly uniform effects on the reliability of d-ROPUF. In addition, voltage variations negatively impact the reliability of d-ROPUF and cause more bit flips in the d-ROPUF response when compared to temperature variations.
As the temperature or voltage deviates from the normal value, the number of bit flips increases which in turn affects the ROPUF reliability.

## Slide 30
While at 25C the average reliability is found to be 97.3% with 6.3 bits flips out of 238 bits which represents the highest reliability with the lowest bit flip percentage.
In terms of voltage variations, at 1.4V the average reliability is found to be 92.1% with 19 bits flips out of 238 bits which represents the lowest reliability with the highest bit flip percentage.
As seen in Table 8, at 75 C temperature variation, the average reliability is found to be 93.9% with 14.4 bits flips out of 238 bits which represents the lowest reliability with the highest bit flip percentage.

## Slide 31: Conclusions
A dynamic ROPUF structure (d-ROPUF) with different challenge response behavior is proposed to enhance ROPUF security against hardware vulnerabilities and attacks.
The design is implemented and evaluated on 30 Spartan 3E FPGA chips.
It is shown that the obtained RO frequencies are normally distributed. Using a newly proposed parameter, RO variability, we determine that the performance of d-ROPUF structures can be increased by having less number of stages and vice versa.

## Slide 32
Our results show that the d-ROPUF exhibits fairly good performance in terms uniqueness, uniformity, and bit-aliasing at the normal operating conditions.
We observe that varying environmental conditions in terms of supply voltage variations have a higher effect on the reliability of d-ROPUF response which causes more bit flips compared to temperature variations.
Although the reliability is slightly affected by the environmental variations, a high ratio of static to dynamic variation ensures that the generated d-ROPUF response bits exhibit high reliability in terms of intra-chip Hamming Distance.

## Slide 33: References
Herder C, Yu M, Koushanfar F, Devadas S (2014) Physical Unclonable Functions and Applications: A Tutorial. Proceedings of the IEEE 102:1126-1141.
Xin X, Kaps J, and Gaj K (2011). A Configurable Ring-Oscillator-Based PUF for Xilinx FPGAs. 14th EUROMICRO Conference on Digital System Design DSD11 651657.
Kursawe K, Sadeghi A, Schellekens D, Skoric B, and Tuyls P (2009). Reconfigurable Physical Unclonable Functions : enabling technology for tamper-resistant storage.Proceedings IEEE International Conference on Hardware-Oriented Security and Trust 22-29
Mustapa M, Niamat M, Alam M and Killian T (2013) Frequency uniqueness in ring oscillator Physical Unclonable Functions on FPGAs. 56th International Midwest Symposium on Circuits and Systems (MWSCAS) 465-468.
Maiti A and Schaumont P (2009) Improving the quality of a Physical Unclonable Function using configurable Ring Oscillators. International Conference on Field Programmable Logic and Applications, Prague 703-707.
Krishnan V .Statistics for the Behavioral Sciences ISBN-13: 978-1-111-83099-1, 9th Edition.
Suh G and Devadas S (2007). Physical unclonable functions for device authentication and secret key generation ACM Press 914.

## Slide 34
Lim D, Lee J, Gassend B, et al (2005) Extracting secret keys from integrated circuits. IEEE Transactions on Very Large Scale Integration (VLSI) Systems 13:12001205.
Amsaad F, Hoque T, Niamat M (2015). Analyzing the performance of a configurable ROPUF design controlled by programmable XOR gates. IEEE 58th International Midwest Symposium on Circuits and Systems (MWSCAS) 1-4.
Lim D (2004) .Extracting Secret Keys from Integrated Circuits. Masters thesis, MIT.
Majzoobi M, Koushanfar F, Potkonjak M (2009) Techniques for Design and Implementation of Secure Reconfigurable PUFs. ACM Transactions on Reconfigurable Technology and Systems 2:133.
Maiti A, Casarona J, McHale L and Schaumont P (2010). A large scale characterization of RO-PUF. IEEE International Symposium on Hardware-Oriented Security and Trust (HOST) 94-99.
Sedcole P and Cheung P (2006). Within-die delay variability in 90nmFPGAs and beyond, IEEE FPT Proceedings 97-104.
Sklavos S (2013). Securing Communication Devices via Physical Unclonable Functions (PUFs), Information Security Solutions, Springer 13:253-261.