## Slide 1: Chapter 24: Physical Unclonable Functions (PUFs) Design Technologies: Advantages and Trade Offs
Ioannis Papakonstantinou, and
Nicolas Sklavos

## Slide 2
Fundamental Terms and Metrics
Basic Categories of PUFs
Intrinsic and Non-intrinsic
Electronic and Non-electronic
Designs of Silicon PUFs
delay-based PUFs
memory-based PUFs
mixed signal PUF
MAIN SECTIONS OF PRESENTATION

## Slide 3: Physical Unclonable Function
What this is
hardware security
specific architectures that behave differently each time
Inherit their unique characteristics during their manufacture process
key factor : uncontrolled parameters
unique and unclonable
PUFs can be considered as the equivalent of fingerprint ID for (electronic) devices

## Slide 4: Physical Unclonable Function
When
Pappu [8] proposed an optic-based
Gassend et al. [2] introduced the notion of PUF and described a fully integrated PUF
Emerged in computer systems in the recent years, Sklavos [14]

## Slide 5: Physical Unclonable Function
Why
Advantages in various parameters (cost, area, run-time, security and specific implementation designs)
Can be used as a secret key instead of a key stored in a non-violate memory
Can be used as cryptographic functions
Multiple security protocols can be implemented in hardware
Can be used as a source of randomness
Are an attractive solution for smartcard design

## Slide 6: Fundamental Terms and Metrics
Challenge :
input from the verifier
stimulates the device
Response :
output to the verifier
generated after the Challenge
Intra-chip variation :
Hamming Distance between the responses of a PUF for the same given challenge
as less as possible to achieve high robustness

## Slide 7: Fundamental Terms and Metrics
Inter-chip variation :
Hamming Distance between the responses of different PUFs for the same given challenge
best possible value 50% to achieve high uniqueness
False Acceptance Ratio (FAR) :
percentage of PUF responses that are wrongfully considered valid
high FAR in a PUF increases robustness and decreases security
False Rejection Ratio (FRR) :
percentage of PUF responses that are wrongfully rejected by the verifier
high FRR increases security and decreases robustness

## Slide 8: Basic Categories of PUFs
Intrinsic
Non-Intrinsic
Electronic
Non-Electronic

## Slide 9: Intrinsic or not
A PUF to be intrinsic must :
Inherit its unique characteristics during its manufacturing process due to uncontrolled and random process variations. The manufacturer must not be involved in order to be identified
Must internally evaluate itself from an embedded measurement equipment. Responses must be able to be used directly as an answer to the verifier and no intermediary transformation is needed so its answer can be considered usable
Pros
Fewer external limitations and more security
Better accuracy with less influence from environmental parameters

## Slide 10: Electronic or not
Non-electronic PUFs are those whose basic behavior is based on non-electronic technologies. Secondary functions of it can occur by the use of electronic subsystems
Electronic PUFs are those which use electronic components for their basic operation. They are easier in processing and to interconnect with other components
Major categories of silicon PUFs :
delay-based PUFs
memory-based PUFs
mixed signal PUF

## Slide 11: Designs of Silicon PUFs
Delay PUFs
Arbitrary
Ring Oscillator (RO)
Memory PUFs
SRAM
Bistable Ring (BR)
Mix Signal PUFs
MECCA
SHIC

## Slide 12: Delay
Delay variations in manufacturing process
Delay differences in silicon
Measurement of the difference to decide the response
Simplicity
Easy designing
Arbiter PUF
Ring Oscillator PUF
Glitch PUF

## Slide 13: Arbiter
Identical paths
Propagating transitions
Sets up race condition
Arbiter at the end of the paths
Selecting paths as a Challenge
Arbiter output as Response
Feed-forward
XOR
Reconfigurable
Lightweight
Mixing all the above

## Slide 14: Arbiter
Example of arbiter PUF

## Slide 15: Arbiter
Inter and intra-chip variation for different PUF structures [5]
Designs | Inter-chip Variation |  | Intra-chip Variation | 
 | Max | Min | Max | Avg
Non feed forward | 59 | 22 | 13 | 5.8
Feed forward overlap | 66 | 27 | 15 | 8.7
Feed forward cascade | 64 | 25 | 20 | 10.7
Feed forward separate | 65 | 26 | 17 | 9.9
Reconfigurable Feed forward | 65 | 25 | 19 | 10.3
Mux and demux | 57 | 23 | 16 | 7.1

## Slide 16: Arbiter
Pros
Simplicity
Easy implementation
Lots of variations
Reconfigurability
Cons
Requirement for identical paths
Sensitive to environmental changes
Not friendly for FPGAs
Prone to reverse engineering and emulation attacks (at their basic layout)

## Slide 17: Ring Oscillator
Multiple oscillating circuits
Different Frequencies
Frequency counter modules
Comparator module
Selecting pair of rings as Challenge
Comparison of frequencies between rings to extract the response

## Slide 18: Ring Oscillator
Basic layout of RO PUF

## Slide 19: Ring Oscillator
Pros
Low cost
Easy implementation
Easy evaluation
Good reliability
Suitable for ASICs and FPGAs
Lots of variations
Cons
Slow responses
Large area
Prone to modeling attacks
Exhibit linearity
Consume more power

## Slide 20: Glitch
Composed of combinatorial logic circuits
Transitional effects
Value changes before output reach its steady value
Random influenced output used as Response

## Slide 21: Memory
Memory cells
Use existing memory of the device
Response from stored value
Unspecified value at start-up
SRAM PUF
Bistable Ring PUF (BR-PUF)

## Slide 22: SRAM
Use of SRAM memory
Memory cells from cross-coupled invertors
Different Static Noise Margin (SNR) for each memory cell
SNM determines the logical value of each cell at start-up
Repetitive behavior

## Slide 23: SRAM
Pros
Use of already existing memory of the device
No area overhead
Easy implementation to the majority of digital devices
Suitable for FPGAs
Cons
Not very stable under environmental varietions

## Slide 24: SRAM
Inter and intra-chip variation for different SRAM PUFs [12]
SRAM | Technology (nm) | Intra-chip var(%) |  |  |  | Inter-chip var(%) | 
 |  | 20 ºC avg | ±60 ºC worst | normal vdd avg | 90%-110% vdd worst | 20 ºC avg | ±60 ºC worst
Cypress CY7C15632KV18 | 65 | 3.8 | 12.2 | 3.8 | 4.5 | 49.7 | 48.6
Virage HP ASAP SP ULP 32-bit | 90 | 2.9 | 19.6 | 5.5 | 6.2 | 49.3 | 46.8
Virage HP ASAP SP ULP 64-bit | 90 | 3.5 | 17.6 | 5.5 | 6.3 | 49.2 | 48.0
Faraday SHGD130-1760X8X1BM1 | 130 | 4.5 | 13.7 | 4.6 | 5.4 | 53.5 | 65.2
Virage asdsrsnfs1p1750x8cm16sw0 | 130 | 4.8 | 20.5 | 5.5 | 6.4 | 50.1 | 48.7
Cypress CY7C1041CV33-20ZSX | 150 | 3.5 | 9.2 | 3.5 | 3.9 | 50.1 | 48.1
IDT 71V416S15PHI | 180 | 2.8 | 9.3 | 1.7 | 2.2 | 40.5 | 40.4

## Slide 25: Bistable Ring
Chen et al. [1]
Combination of memory and delay based PUF
Rings instead of memory cells
Even number of inverters at each ring
Two possible states for each ring
Different time to stabilize
Observation of the ring until stabilization …
… or setting a common upper evaluation time

## Slide 26: Bistable ring
Basic idea of bistable rings.
Possible states for a six inverter ring:
010101
101010

## Slide 27: Bistable ring
Max and average settling time various stages of
rings [16]
Stages | 32 | 64 | 128
Max Settling Time (μs) | 8.44 | 22.25 | 37.20
Average Settling Time (μs) | 5.26 | 10.78 | 23.09

## Slide 28: Bistable ring
Pros
Easy implementation
Reduced complexity (common evaluation time)
Suitable for FPGAs
Does not require symmetry
Exponential CRPs
Cons
Large area
Trade-off between reliability and uniqueness

## Slide 29: Mix Signal
Analog and digital components
Analog behavior
Analog-to-digital conversion (wherever needed)
expensive manufacture
Trivial implementation
MECCA PUF
SHIC PUF

## Slide 30: MECCA
MECCA – Memory Cell Chip Authentication
Krishna et al. [4]
SRAM array
Failure mechanism (write failure)
Different failure limit for each memory cell
Changing signal duration to induce failures

## Slide 31: MECCA
Pros
Excellent uniqueness (avg. inter-chip var. 49%)
Excellent reproducibility (avg. intra-chip var. 0,85%)
Little area overhead
Memory-based PUF
Resistant to modeling attacks (due to analog nature)
Cons
Complex design
Includes analog modules

## Slide 32: SHIC
SHIC – Super High Information Content
Rührmair et al. [9]
Special fabricated diodes
Each diode independent from others
High density of information – Large amount of information stored in standard area
Limited read-out speed
Very big number of extracted CPRs to compromise security
Huge amount of time to achieve a good ratio of read-out bits / overall stored bits

## Slide 33: SHIC
Pros
Suitable for many security applications
Cheap
Require very small area
Good temperature stability
Resistant to machine learning attacks
Secure even if an adversary gain access for limited time
Cons
Specialized fabrication method

## Slide 34: References
1. Chen, Q., Csaba, G., Lugli, P., Schlichtmann, U., & Ruhrmair, U. (2011). The bistable ring
PUF: A new architecture for strong physical unclonable functions. In IEEE international symposium on hardware-oriented security and trust—HOST 2011 (pp. 134–141). New York: IEEE.
2. Gassend, B., Clarke, D., van Dijk, M., & Devadas, S. (2002). Silicon physical random functions. In Proceedings of the computer and communications security conference.
3. Guajardo, J., Kumar, S. S., Schrijen, G. J., & Tuyls, P. (2007). FPGA intrinsic PUFs and their use for IP protection. In Lecture notes in computer science (LNCS), Workshop on cryptographic hardware and embedded systems—CHES 2007 (Vol. 4727, pp. 63–80). Berlin: Springer.
4. Krishna, A., Narasimhan, S., Wang, X., & Bhunia, S. (2011). MECCA: a robust low overhead PUF using embedded memory array. In Lecture notes in computer science (LNCS), Workshop on cryptographic hardware and embedded systems—CHES 2011 (Vol. 6917, pp. 407–420). Berlin: Springer.
5. Lao, Y., & Parhi, K. (2011). Reconfigurable architectures for silicon physical unclonable
functions. In IEEE international conference on electro/information technology—EIT 2011 (pp.
1–7). New York: IEEE.
6. Maes, R. (2013). Physically unclonable functions. New York: Springer.

## Slide 35: References
7. Majzoobi, M., Koushanfar, F., & Potkonjak, M. (2009). Techniques for design and implementation of secure reconfigurable PUFs. ACM Transactions on Reconfigurable Technology and Systems, 2(1), 1–33.
8. Pappu, R. S. (2001). Physical one-way functions. Ph.D. thesis, Massachusetts Institute of
Technology (MIT), Cambridge, MA.
9. Rührmair, U., Jaeger, C., Hilgers, C., Algasinger, M., Csaba, G., & Stutzmann, M. (2010b).
Security applications of diodes with unique current-voltage characteristics. In Lecture notes
in computer science (LNCS), International conference on financial cryptography and data
security—FC 2010 (Vol. 6052, pp. 328–335). Berlin: Springer.
10. Rührmair, U., Sehnke, F., Sölter, J., Dror, G., Devadas, S., & Schmidhuber, J. (2010a).
Modeling attacks on physical unclonable functions. In ACM conference on computer and
communications security—CCS 2010 (pp. 237–249). New York: ACM.
11. Rührmair, U., & van Dijk, M. (2013, May 19–22). PUFs in security protocols: attack models and security evaluations. In 2013 IEEE symposium on security and privacy, San Francisco, CA.
12. Schrijen, G.-J., & van der Leest, V. (2012). Comparative analysis of SRAM memories used as PUF primitives. In Design, automation and test in Europe—DATE 2012 (pp. 1319–1324). New York: IEEE

## Slide 36: References
13. Sklavos, N. (2011, April 6–8). Cryptographic algorithms on a chip: Architectures, designs
and implementation platforms. In Proceedings of the 6th design and technology of integrated
systems in nano era (DTIS’11), Greece.
14. Sklavos, N. (2013, October 22–23). Securing communication devices via physical unclonable functions (PUFs). In Information security solutions Europe (isse’13) (pp. 253–261). Brussels: Springer.
15. Sklavos, N., Chaves, R., Di Natale, G., & Regazzoni, F. (2017). Hardware security and trust.
Cham: Springer.
16. Sklavos, N., & Souras, P. (2006). Economic models and approaches in information security for computer networks. International Journal of Network Security (IJNS), Science Publications, 2(1), 14–20.
17. Suh, G. E., & Devadas, S. (2007). Physical unclonable functions for device authentication and secret key generation. In Design automation conference—DAC 2007 (pp. 9–14). New York: ACM.