## Slide 1: Chapter 30: A Comparative Study of Neural Network Training Algorithms for the Intelligent Security Monitoring of Industrial Control Systems
Jaedeok Kim and Guillermo Francia

## Slide 2
In 2011 a publication, NIST SP 800-137, released by NIST to provide guidelines for continuous monitoring of information security on federal information systems and organizations.
In 2015 U.S. Department of Energy’s Office of Electricity Delivery and Energy Reliability published a document, Energy Sector Cyber Security Framework Implementation Guidance, in response to NIST’s framework.
These guidelines and standards underscore the importance of protecting our critical infrastructures that are operating through automated controlled systems.
1. Introduction

## Slide 3
In response to this national need, we embark of a research study on continuous security monitoring of industrial control systems using artificial intelligent neural systems.
This chapter presents some preliminary work towards developing a complex neural system that classifies, in real time, industrial control system.
1. Introduction

## Slide 4
In May 2010, The National Science Foundation (NSF) funded the Critical Infrastructure Security and Assessment Laboratory (CISAL) project at JSU.
CISAL SYSTEM ARCHITECTURE
2. Facilities and Resources

## Slide 5
CISAL is designed to simulate the operations of a typical SCADA system serving a small community.
Current CISAL project outcomes include the design and implementation of the control systems laboratory that mimics a water distribution system and a nuclear power generation facility, the development of various curriculum modules for a critical infrastructure protection course, and the investigation of various wireless technology applications on control systems.
2. Facilities and Resources

## Slide 6
A neural network (NN) is an information processing system that is inspired by the human brain’s nervous system.
It consists of a large number of highly interconnected processing components called neurons.
It can be used to solve problems in a wide range of applications such as function approximations, linear and nonlinear regressions, pattern recognitions, and data classifications.
Two major steps in running a neural network are setting up an error function (or a performance index) and choosing a training algorithm that minimizes the error function.
3. Neural Networks

## Slide 7
Two commonly used error functions are the Mean Square Error (MSE) and the Cross-Entropy (CE).
MSE measures the expected value of squares of difference between network output vectors and target vectors.
CE is constructed by providing probabilistic views to the network outputs. CE measures the negative log likelihood.
3. Neural Networks
Two Error Functions

## Slide 8
The following NN training functions (or training algorithms) available in Matlab® Neural Network Toolbox that have been adopted and tested for data training.
Scaled Conjugate Gradient (trainscg)
Levenberg-Marquardt (trainlm)
BFGS Quasi-Newton (trainbf)
Resilient Backpropagation (trainrp)
Gradient Descent with Momentum (traingdm)
Gradient Descent with Momentum and Adaptive Learning Rate (traingdx)
4. NN Training Functions

## Slide 9
The research study involves the monitoring of a subset of a collection of complex operational data from a power generating system.
We monitor the operation of three pumps, the tank water level, and the operational status of water-cooled equipment such as a reactor or a generator.
We also test a different set of operational data by including the water temperature as an additional input data element.
The operational and pump statuses are binary values (0-OFF, 1-ON).
5. Comparative Analysis
Preamble

## Slide 10
The water temperatures are real numbers ranging from 0 Co to 400 Co.
The tank level is either continuous or discrete.
The continuous values range from 0.0 to 99.99 reflecting the fill percentage of the tank.
The 5 discrete values are indicative of the following level statuses: 1 (critically low), 2 (low), 3(normal), 4(high), and 5 (critically high)
For statistical stability of results of network training, we run each algorithm 5 times on the same set of input data for both continuous format and discrete format.
5. Comparative Analysis
Preamble

## Slide 11
We make comparisons of five different training algorithms (traincgf, trainlm, trainbfg, traingdx, trainrp) on four neural network system metrics: Network Error Function, Success Rate, Run Time, and Epochs
We also run comparative analysis investigating the statistical differences using the following different pairings:
  Continuous (tank level) without Water Temperature vs Discrete without Water Temperature
  Continuous with Water Temperature vs Discrete with Water Temperature
  Without Water Temperature vs With Water Temperature
5. Comparative Analysis
Preamble

## Slide 12
Training Parameters
Parameter | Value
Number of Input Attributes | 5
Number of Input Records | 30,000
Number of Output Attributes | 2
Number of Output Records | 30,000
Number of Neural Network Hidden Layers | 10
Allocation of Data for Training | 70%
Allocation of Data for Validation | 15%
Allocation of Data for Initial Testing | 15%
Maximum number of Training Epochs | 5,000
Performance index (Cross Entropy (CE) or Mean Square Error(MSE) | MSE or CE
The following table summarizes parameters for neural network training.
5. Comparative Analysis

## Slide 13
5. Comparative Analysis
Network Error Function
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
 | 0.0271 | 0.138 | 0.0325 | 0.0402 | 0.0328
 | 0.0323 | 0.138 | 0.032 | 0.0204 | 0.0153
 | 0.0329 | 0.139 | 0.0327 | 0.0395 | 0.0328
 | 0.0102 | 0.149 | 0.0329 | 0.0587 | 0.0177
 | 0.0164 | 0.148 | 0.0304 | 0.0288 | 0.0324
Figure 1. Performance with Continuous Tank Level w/o Temperature

## Slide 14
5. Comparative Analysis
Network Error Function
Figure 2. Performance with Discrete Tank Level w/o Temperature
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
 | 0.0446 | 0.137 | 0.0185 | 0.0166 | 0.0156
 | 0.0251 | 0.134 | 0.0188 | 0.0347 | 0.0388
 | 0.0161 | 0.138 | 0.0411 | 0.00849 | 0.0085
 | 0.0156 | 0.137 | 0.0323 | 0.0169 | 0.00835
 | 0.0607 | 0.138 | 0.0315 | 0.0164 | 0.00857

## Slide 15
5. Comparative Analysis
Network Error Function
Figure 3. Performance with Continuous Tank Level w/ Temperature
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
 | 0.00648 | 0.127 | 0.0184 | 0.0301 | 0.0102
 | 0.00451 | 0.133 | 0.029 | 0.0227 | 0.0171
 | 0.00741 | 0.129 | 0.0255 | 0.0168 | 0.00688
 | 0.00855 | 0.131 | 0.0202 | 0.0422 | 0.0102
 | 0.00867 | 0.131 | 0.0158 | 0.0281 | 0.0243

## Slide 16
5. Comparative Analysis
Network Error Function
Figure 4. Performance with Discrete Tank Level w/ Temperature
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
 | 0.000478 | 0.127 | 0.0197 | 0.0051 | 0.00384
 | 0.000808 | 0.127 | 0.0187 | 0.0215 | 0.00137
 | 0.00252 | 0.126 | 0.0124 | 0.0258 | 0.00365
 | 0.000567 | 0.126 | 0.029 | 0.0217 | 0.00653
 | 0.00129 | 0.131 | 0.00341 | 0.00862 | 0.00159

## Slide 17
5. Comparative Analysis
Network Error Function
Figure 5. Continuous vs Discrete (Performance w/o Temperature)
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
Continuous | 0.02378 | 0.1424 | 0.0321 | 0.03752 | 0.0262
Discrete | 0.03242 | 0.1368 | 0.02844 | 0.018618 | 0.015964

## Slide 18
5. Comparative Analysis
Network Error Function
Figure 6. Continuous vs Discrete (Performance w/ Temperature)
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
Continuous | 0.007124 | 0.1302 | 0.02178 | 0.02798 | 0.013736
Discrete | 0.0011326 | 0.1274 | 0.016642 | 0.016544 | 0.003396

## Slide 19
5. Comparative Analysis
Network Error Function
Figure 7. Without Temperature vs With Temperature in Performance
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
Without Temp | 0.02378 | 0.1424 | 0.0321 | 0.03752 | 0.0262
With Temp | 0.007124 | 0.1302 | 0.02178 | 0.02798 | 0.013736

## Slide 20
5. Comparative Analysis
Success Rate
Figure 8. Percentage of Success Rate w/o Temperature
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
Continous | 93.38 | 96.62 | 90.82 | 90.06 | 92.7
Discrete | 90.64 | 97.64 | 91.8 | 94.72 | 95.38

## Slide 21
5. Comparative Analysis
Success Rate
Figure 9. Percentage of Success Rate w/ Temperature
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
Continous | 98.26 | 99.14 | 93.86 | 93.48 | 96.36
Discrete | 99.78 | 99.66 | 95.2 | 96.66 | 99.42

## Slide 22
5. Comparative Analysis
Success Rate
Figure 10. Without Temperature vs With Temperature (in Percent)
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
Without Temp | 90.64 | 97.64 | 91.8 | 94.72 | 95.38
With Temp | 99.78 | 99.66 | 95.2 | 96.66 | 99.42

## Slide 23
5. Comparative Analysis
Run Time
Figure 11. Run Time (in seconds) Continuous w/o Temp
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
 | 5 | 14 | 9 | 1 | 2
 | 3 | 7 | 12 | 1 | 5
 | 1 | 21 | 10 | 1 | 1
 | 2 | 6 | 5 | 1 | 11
 | 5 | 12 | 10 | 1 | 9
 | 3.2 | 12 | 9.2 | 1 | 5.6

## Slide 24
5. Comparative Analysis
Run Time
Figure 12. Run Time (in seconds) Discrete w/ Temp
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
 | 4 | 17 | 5 | 3 | 4
 | 3 | 10 | 7 | 1 | 6
 | 5 | 18 | 8 | 1 | 4
 | 4 | 16 | 5 | 1 | 4
 | 5 | 18 | 12 | 11 | 8
 | 4.2 | 15.8 | 7.4 | 3.4 | 5.2

## Slide 25
5. Comparative Analysis
Run Time
Figure 13. Run Time (in seconds) w/o Temp (Continuous vs Discrete)
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
Continous | 3.2 | 12 | 9.2 | 1 | 5.6
Discrete | 1.8 | 30.8 | 9.6 | 1.8 | 1

## Slide 26
5. Comparative Analysis
Run Time
Figure 14. Run Time (in seconds) w/ Temp (Continuous vs Discrete)
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
Continous | 3.2 | 12 | 9.2 | 1 | 5.6
Discrete | 1.8 | 30.8 | 9.6 | 1.8 | 1

## Slide 27
5. Comparative Analysis
Run Time
Figure 15. Number of Epochs Needed
Chart: 
| trainscg | trainlm | trainbfg | traingdx | trainrp
Continuous | 134.6 | 139.6 | 115.2 | 100.6 | 247
Discrete | 166.6 | 183.8 | 132.6 | 154.8 | 370.4

## Slide 28
5. Comparative Analysis
Confusion Matrix
Figure 16. Confusion Matrix on the Resilient Backpropagation Training

## Slide 29: Conclusion
Except for the Gradient Descent with Momentum (traingdm) training algorithm, the other algorithms perform at a reasonable success rate of 90% and over.
The discrete dataset provides improved success rates in most runs than the continuous cases.
The addition of temperature variable to the input dataset increases the success rate considerably.
The run time and the number of iterations (epochs) displayed by the Resilient Backpropagation (trainrp) and Gradient Descent with Momentum and Adaptive Learning Rate (traingdx) training algorithms are generally better than the other algorithms.

## Slide 30: Future Work
The utilization of artificial intelligence approaches such as Clustering, Principal Component Analysis (PCA), Genetic Algorithms, Deep Learning, Support Vector Machine (SVM), etc. to enhance the performance of the machine learning classification system.
The investigation of using the Mean Square Error (MSE) function to further enhanced a classification system that was trained with the Cross Entropy criterion.