## Slide 1: Real-Time Process Control Systems (Real-Time Controller ASM for the Railroad Crossing Case Study)
Egon Börger
Dipartimento di Informatica, Universita di Pisa
http://www.di.unipi.it/~boerger

## Slide 2
E. Börger, R. Stärk
Abstract State Machines
A Method for High-Level System Design and Analysis
Springer-Verlag 2003
For update info see AsmBook web page:
http://www.di.unipi.it/AsmBook
For details see Chapter 5 (Synchronous Multi-Agent ASMs) of:

## Slide 3
Process Control Systems
Real-Time Controller ASMs (with atomic actions)
Railroad Crossing Controller ASM
Analysis of the Railroad Crossing Controller ASM (Safety & Liveness Proof)
Exercises and References

## Slide 4: Four-Variable Model for Process Control Systems
IN transforms continuous physical quantities, measured by e.g. sensors, into discrete software INPUT
OUT transforms discrete sw OUTPUT into values for actuators that manipulate the continuous physical process
INput
Device
OUTput
Device
DiscreteSw
INPUT
DiscreteSw
OUTPUT
SOFT
Controller
MONitored
PhysVars
CONtrolled
PhysVars
PhysProcessREQ
Goal: define SOFT to
correctly implement
REQ

## Slide 5: Sampling & Synchronization Problem for Process Control
Sampling Problem : approximate continuous flow of physical process data by (a finite number of) discrete samples taken at real-time moments that form an increasing discrete sequence
Synchronization Problem : synchronize the SOFT controller with the IN/OUT devices to guarantee a correct reactive behavior of the entire software system wrt the env, with stable states for
  reading INPUT
  internal controller steps
  sending OUTPUT

## Slide 6: Env-Controller Separation Principle for Process Control Systems
Environment-Controller Separation Principle At each moment, the software controller
  either through its input device takes INPUT from the environment, without involving any further internal computation step
  or makes an internal computation step (including the preparation of OUTPUT to be sent to the output device), without involving any further INPUT reading
This principle is applied by many process control systems. Its appropriateness for a physical system to be controlled depends on
  correctness of sampling mechanism
  sufficient hw speed (for the internal controller steps) wrt sampling

## Slide 7: Env-Controller Separation Principle in Neural Nets
A Neural Net is usually seen as a black-box yielding output to the env, as result of an internal computation which is triggered by an input taken from the env. The internal computation consists of a finite sequence of atomic actions performed by the basic computing elements (nodes of a directed data-flow graph)
  In forward propagation mode, the network input is transmitted by the input units to the internal units which propagate their results through the graph until the output units are reached
input
new input to be consumed
activate
Neural Kernel
compute
more units to be computed
NK step
NO
YES
clearState
  env recognizes whether NK has
  terminated its internal computation
  env signals
  presence of
  new input
  NK consumes
  input

## Slide 8: Env-Controller Separation Principle in Circuits
Circuit Synchronization by a clock which alternates between low and high pulse
circuit viewed as
  black box
  input lines (representing the environment)
  output lines
When clock pulse is low
  box and output idle, input may change
When clock pulse is high
  box and output may change, input is idle

## Slide 9
Control Systems
Real-Time Controller ASMs (with atomic actions)
Railroad Crossing Controller ASM
Analysis of the Railroad Crossing Controller ASM (Safety & Liveness Proof)
Exercises and References

## Slide 10: Goals of Real-Time Controller ASMs (with Atomic Actions)
atomic actions
  controller executes instantaneously
  environment changes take place instantaneously
at each real-time moment, there is a well defined state
runs which satisfy the environment-controller separation principle
In the definition below, we will allow that the controller is constituted by multiple agents, each of which executes a basic ASM. Atomicity of actions constitutes an idealization, to be refined by durative actions.

## Slide 11: Recalling Basic ASMs
A Basic ASM is a finite set of rules, executed by a single agent self, and having the form
  If Condition Then Updates
  with Updates a finite set of f (t1,…,tn):=t with arbitrary functions,
  Condition a Boolean valued expression (1st order formula)
In the current state (structure) S:
  determine all the fireable rules in S (s.t. Cond is true in S)
  compute all exprs ti,t occuring in updates f(t1,…,tn):=t
  execute simultaneously all these function updates
The updating yields the next state S’

## Slide 12: Runs of Real-Time Controller ASMs
Run of a Real-Time Controller ASM M given by
a discrete sequence 0 = t0 < t1 < t2,... of reals – consisting of (all & only) the computationally significant real-time “moments” of M - and associated states S(tn) where currtime = tn and
(tn+1) is obtained from (tn) ( = S(tn) minus currtime) by
  either Case 1: a computation step (of some agents) of M, without any change of monitored fcts between tn and tn+1
  or Case 2: a change of monitored fcts, without any M-comp step between tn and tn+1
standard extension to states S(t) for tn < t < tn+1

## Slide 13: Standard Extension of Runs of Real-Time Controller ASMs
A run ( tn,S(tn))n N of a real-time controller ASM M is naturally extended to states S(t) of arbitrary real-time moments tn < t < tn+1 as follows:
  currtime = t in S(t)
  (t) = (tn+1) in Case 1 (result of the instantaneous M-step executed at time tn)
  (t) = (tn) in Case 2 (unchanged M-state, since between tn and tn+1 no M-step takes place, & the instantaneous change of monitored fcts becomes effective at tn+1 )
Lemma.tn < t <t’< tn+1 : (t) = (t’)
NB. ( tn)n N is discrete iff t  only finitely many tn < t. This condition excludes so-called Zeno runs.

## Slide 14
Control Systems
Real-Time Controller ASMs (with atomic actions)
Railroad Crossing Controller ASM
Analysis of the Railroad Crossing Controller ASM (Safety & Liveness Proof)
Exercises and References

## Slide 15: Problem Description of Railroad Crossing Case Study
The system to be developed operates a gate at a railroad crossing. A set of trains travel on multiple tracks in both directions. Each track has four sensors, detecting when a train enters resp. exits the crossing: L1, L2 for trains coming from the left, R1, R2 for trains coming from the right. Based on these sensor signals, a controller should signal the gate to open/close.
Prove the following two properties for the system:
  Safety: When a train is in the crossing, the gate is closed.
  Liveness:The gate is open when no train is in the crossing.

## Slide 16: Train Motion Assumptions of Railroad Crossing
Train Motion: For every track, there is a train motion sequence t0 < t1 < t2,... of reals with the following properties:
  Initial State: at the initial moment t0, the observed track segment [L1,R1] is empty.
  Train Pattern: If t3i+1 appears in the sequence, then t3i+2 and t3i+3 appear in the sequence, and
    at t3i+1, an incoming train is detected at either L1 or R1
    at t3i+2 this train reaches the crossing
    at t3i+3 this train is detected to have left the crossing at L2 resp. R2
  Completeness : The sequence t0 < t1 < t2,... covers all the (and only) trains that appear on this track.

## Slide 17: Train & Gate Assumptions of Railroad Crossing
Train Approaching Time: dmin  dmax are the minimal/maximal time for a train to reach the crossing after having been detected at L1/R1:
  t3i+2 - t3i+1  [dmin, dmax] for all i in a train motion sequence
Gate Closure/Opening Time: during no interval [t, t+dclose] resp. [t, t+dopen] is a signal to close/open in force without at some moment in this interval the gate being closed/opened.
Gate versus Train Time: dclose < dmin
NB. Gate may react to closure/opening commands with some (bounded) delay, whereas wlog we will assume the controller to react immediately, i.e. at the instant when it is enabled.

## Slide 18: Signature of Railroad Crossing ASM
currtime: REAL is the central monitored time function
TRACK : static domain with
  monitored fct TrackStatus : TRACK  {empty, coming, inCrossing}
  controlled fct Deadline : TRACK  REAL  {} to measure the allowable WaitingTime bw the train appearance and the latest possible moment to start the gate closing (for the gate to be closed in time)
two dynamic fcts for gate moving directions and final gate positions:
  Dir  {open, close} controlled by the controller
  GateStatus  {opened, closed} controlled by the gate

## Slide 19: Controller ASM for Railroad Crossing
Controller  forall x  TRACK
SetDeadline(x)
SignalClose(x)
ClearDeadline(x)
SignalOpen
SetDeadline(x)  If TrackStatus (x) = coming & Deadline (x) =  then Deadline (x) := currtime + dmin – dclose (WaitTime)
SignalClose(x)  If currtime = Deadline (x) then Dir := close
ClearDeadline (x)  If TrackStatus (x) = empty & Deadline (x) <  then Deadline (x) := 
SignalOpen  If Dir = close & SafeToOpen then Dir:=open
where SafeToOpen  xTRACK: TrackStatus (x) = empty or
enough time to open before next closure currtime + dopen < Deadline (x)

## Slide 20: Gate ASM: an instance of a Flip Flop
Gate  OpenGate
CloseGate
where OpenGate  If Dir = open then GateStatus := opened
CloseGate  If Dir = close then GateStatus := closed
Initialization
  GateStatus = opened Dir = open
  for all xTRACK
  TrackStatus (x) = empty Deadline(x) = 
NB. Sharpening the guards in
  Gate rules by GateStatus = closed/opened
  SignalClose (x) by Dir = open
  yields a machine where each step changes the state. We disregard this optimization, since the definition of runs of a real-time controller ASM is not restricted to machine steps which change the state.

## Slide 21: The Agents of the Railroad Crossing ASM
The Railroad Crossing Controller ASM has three agents
  Controller, Gate
  Env, represented by the monitored fct TrackStatus
A representation of Env as agent has to internalize the timing conditions of train motion sequences, e.g. by a timed automaton ASM, consisting of one machine for each track x, each able to fire independently & simultaneously.
NB. The notion of real-time controller ASM run has to be adapted to treating env as a special team of agents
empty
inCrossing
coming
clock(x)
:= 0
dmin  clock(x)
 dmax

## Slide 22: A Run of the Railroad Crossing ASM is …
… a real-time controller ASM run. These runs reflect the train motion condition through the moments of change of the monitored function TrackStatus:
among the computationally significant moments of the run, every track x has a subsequence 0 = t0 < t1 < t2,… of significant moments of x such that TrackStatus(x) =
    empty over every interval [t3i, t3i+1 )
    coming over ... [t3i+1, t3i+2 ) & dmin  t3i+2 - t3i+1  dmax
    inCrossing over ... [t3i+2, t3i+3 )
    empty over [tk, ) if tkis the final significant moment of track x, in which case 3|k
NB. In those runs, the Controller is assumed to react immediately, the reaction time of Gate to be bounded in the sense of the Gate Closure/Opening Time property.

## Slide 23
Control Systems
Real-Time Controller ASMs (with atomic actions)
Railcroad Crossing Controller ASM
Analysis of the Railroad Crossing Controller ASM (Safety & Liveness Proof)
Exercises and References

## Slide 24: Safety & Liveness for Railroad Crossing ASM
For arbitrary runs of the Railroad Crossing ASM, the following two properties hold:
Safety Theorem. At any moment when a train is in the crossing (Gate Status (x) = inCrossing for some track x), the gate is closed (GateStatus = closed).
Liveness Theorem. Whenever the crossing is empty (i.e.TrackStatus(x)  inCrossing for every x) in an open real-time interval (,) with + dopen < - Dclose, the gate is open in the closed interval [+dopen,  - Dclose] where Dclose = dmax– WaitTime = dclose + (dmax – dmin)
NB. It can be shown that the Liveness Thm fails if dopen or Dclose are replaced with smaller values.
NB.One can also prove that the closing of the gate is never interrupted; under appropriate assumptions the same holds for opening.

## Slide 25: Proving Safety for the Railroad Crossing ASM
For some track x, let TrackStatus(x) = inCrossing over an interval [t3i+2,t3i+3). We show: GateStatus = closed over [t3i+1 + dmin,t3i+3]  [t3i+2,t3i+3].
Proof.
  SetDeadline (x) fires at t3i+1 (Controller is immediate) setting Deadline(x) to  = t3i+1 + WaitTime
  TrackStatus(x)  empty over I = (, t3i+3)
Hence over I, x makes SafeToOpen false, hence SignalOpen disabled.
Then also OpenGate is disabled over I
  because SignalClose(x) fires at  so that immediately after , Dir=close holds (& remains unchanged over I)
Dir=close immediately after  implies that
  GateStatus = closed for some <t<+dclose=t3i+1+dmin
  & remains so as long as SignalOpen is disabled, i.e. over (, t3i+3) and therefore over [t3i+1 + dmin,t3i+3]
    since only OpenGate, fireable only after SignalOpen, can change it to opened

## Slide 26: Proving Liveness for the Railroad Crossing ASM
By the Deadline Lemma (see below), for every track x holds:
Deadline(x) -Dclose >  + dopen over (,)
  Therefore SafeToOpen holds at currtime = 
  Thus Dir=open holds immediately after  (possibly through firing of SignalOpen)
Deadline(x) -Dclose > currtime over (,-Dclose)
  Hence over (,-Dclose): every SignalClose(x) is disabled, so that Dir remains open and CloseGate is disabled
Dir = open over (,-Dclose) and dopen time assumption imply that
  GateStatus = opened for some  < t < +dopen
  & remains so as long as CloseGate is disabled, namely over (,-Dclose)
  Therefore GateStatus = opened over [ + dopen, -Dclose ]
    since only CloseGate, fireable only after some SignalClose(x), can change it to closed

## Slide 27: Deadline Lemma for Railroad Crossing ASM
Deadline Lemma. In a run of the Railroad Crossing ASM, let x be a track with significant moments 0 = t0 < t1 < t2,….
  Deadline(x) =
     over (t3i,t3i+1 ]
    t3i+1+ WaitTime over (t3i+1,t3i+3 ]
  If TrackStatus(x)  inCrossing over an interval (,), then over this interval Deadline(x)   - Dclose where Dclose = dclose + (dmax - dmin ) = dmax - WaitTime
Prove (a) by induction on i
For (b) assume Deadline(x)< + WaitTime - dmax at some t (,).
Then Deadline(x) = t3i+1+ WaitTime at t for some t3i+1<tt3i+3 .
Then t3i+1<t<  t3i+2 since by hypothesis, (,) and the inCrossing interval [t3i+2,t3i+3) are disjoint.
Therefore - t3i+1 t3i+2 -t3i+1  dmax and - dmax t3i+1 so that
- Dclose =  - dmax +WaitTime  t3i+1 +WaitTime = Deadline(x) (at t) < - Dclose (by assumption): a contradiction

## Slide 28
Control Systems
Real-Time Controller ASMs (with atomic actions)
Railcroad Crossing Controller ASM
Analysis of the Railroad Crossing Controller ASM (Safety & Liveness Proof)
Exercises and References

## Slide 29: Railroad Crossing Case Study : Refinement Exercise
Refine the Railroad Crossing ASM by introducing gate positions between Closed = 0o and Opened = 90o. Clarify the real-world timing assumptions which allow that Dir=close/open only when GateStatus=opened/closed.
Hint. Consider the following timed automaton ASM, with additional GateStatus values closing, opening, and refined rules OpenGate, CloseGate.
closing
clock := 0
opening
Dir=close
clock < dclose
clock := 0
Dir=open
clock < dopen
opened
closed
OpenGate
CloseGate

## Slide 30: Exercises for the Railroad Crossing ASM
Show the following properties for runs of the Railroad Crossing ASM with significant moments 0 = t0 < t1 < t2,… for a track x:
  SetDeadline(x) fires exactly at t3i+1 (when TrackStatus(x) has become coming)
  SignalClose(x) fires exactly at t3i+1+ WaitTime
  ClearDeadline (x) fires exactly at t3i if i>0 (when TrackStatus(x) has become empty)
  Let s(x) be the local SafeToOpen(x) condition, namely TrackStatus(x)=empty or currtime + dopen < Deadline (x). Show:
    If WaitTime > dopen, then s(x) holds over intervals [t3i , t3i+1 +WaitTime – dopen) and fails over intervals [t3i+1 +WaitTime – dopen, t3i+3)
    If WaitTime  dopen, then s(x) holds over intervals [t3i , t3i+1] and fails over intervals (t3i+1, t3i+3)
    s(x) changes from false to true at moments t3i with i>0 (when TrackStatus(x) has become empty)
  SignalOpen fires exactly when SafeToOpen becomes true. If SafeToOpen becomes true at t, then some TrackStatus(x) has become empty at t.

## Slide 31: Railroad Crossing ASM : Exercises (Cont’d)
Show that the Liveness Theorem fails if dopen or Dclose are replaced with smaller values.
Prove that the closing of the gate is never interrupted, i.e. if Dir is set to close at some moment t, then Dir = close holds over the interval (t , t+dclose).
Prove that if WaitTime  dopen, then the opening of the gate is never interrupted, i.e. if Dir is set to open at some moment t, then Dir = open holds over the interval (t, t+dopen).
Show that the Railroad Crossing ASM, viewed as consisting of three agents for Controller, Gate, and the Environment (representing a team that updates the monitored functions), in a natural way satisfies the axioms for an async ASM.
Adapt the definition of real-time controller ASMs to the case where the changes of monitored functions are treated as resulting from updates of a team env of agents.

## Slide 32: References
C. Heitmeyer and D. Mandrioli (Eds.) : Formal Methods for Real-Time Computin. John Wiley & Sons, Chichester 1996
Y. Gurevich and J. K. Huggins: The Railroad Crossing Problem: An Experiment with Instantaneous Actions and Immediate Reactions
    In: Computer Science Logic. Selected Papers from CSL’95 (Ed. H. Kleine Büning). Springer LNCS 1092, 1996, 266-290
D. Beauquier, T. Colard, A. Slissenko: A Predicate Logic Framework for Mechanical Verification of Real-Time Gurevich Abstract State Machines: A Case Study with PVS
    TR 00-25, University Paris 12, CS Dept, 2000. See http://www.univ-paris12.fr/lacl/

## Slide 33: References
E. Börger, R. Stärk: Abstract State Machines. A Method for High-Level System Design and Analysis Springer-Verlag 2003, see http://www.di.unipi.it/AsmBook
D. L. Parnas and J. Madey: Functional Documentation for Computer Systems Engineering (Vol.2).
    Mc Master University TR CRL 237, Hamilton, Ontario, Sept.1991
D.L. Parnas and J. Madey: Functional documents for computer systems. In: Science of Computer Programming 25 (1995), 41-62.