## Slide 1: Pipelining a RISC Architecture Stepwise Verification of DLX
Egon Börger
Dipartimento di Informatica, Universita di Pisa
http://www.di.unipi.it/~boerger

## Slide 2
E. Börger, R. Stärk
Abstract State Machines
A Method for High-Level System Design and Analysis
Springer-Verlag 2003
For update info see AsmBook web page:
http://www.di.unipi.it/AsmBook
For details see Chapter 3.3 (Microprocessor Design Case Study) of:

## Slide 3: The Problem
Prove the pipelined version of a sequential architecture to be semantically correct
  i.e. show for every program that its execution under the pipelining discipline is equivalent to its step-by-step (so-called sequential) execution
Tasks:
  model the two architectures
  define the equivalence notion
  state the assumptions on the environment (compiler, hardware, etc.)
  prove the correctness

## Slide 4: The Case Study
RISC microprocessor architecture DLX (Hennessy/Patterson 1990,1996)
  typical instruction set architecture comprising instructions for arithmetical and set operations, jumps, interrupts, memory access
Pipelining techniques resolving structural, data and control hazards:
  instruction scheduling, forwarding, new hardware links with additional control logic, stalling
Design and verification technique:
  A model for datapath and sequential control of DLX is stepwise refined to its pipelined version which is proven to be correct
    using incremental design and modular proof techniques (based upon locality principle)

## Slide 5: Modeling and Verification Steps
Ground model DLXseq for sequential DLX providing one-instruction-at-a-time RISC processor view
  correct wrt control graph definition by Hennessy/Patterson 1996
Three application domain driven refinement steps (concentrated on control aspects)
  parallelization to DLXpar resolving structural hazards
  resolving data hazards in DLXdata
  resolving control hazards in DLXpipe
Each refined model proven to be correct wrt the preceding model
  using inductions and case distinctions which correspond to the pipelining conflict types and standard methods to solve them

## Slide 6: Main Theorem
For each DLX program P, the result of its sequential (one-instruction-at-a-time) execution on DLXseq is the same as the result of its pipelined (up to five instructions at-a-time) execution on DLXpipe .
Main contribution of the proof:
  from segments of parallel DLXpipe runs, which perform at each step multiple operations for multiple instructions, extracting for each analyzed instruction an equivalent sequential DLXseq subcomputation, which together form an equivalent DLXseq run
  defining the appropriate notions of
    data dependency and control dependency of instructions
    instruction cycle, result locations, relevant locations (per instruction, supporting instructionwise proofs)

## Slide 7: Ground Model DLXseq
Each instruction is executed by 5 successive steps
  IF: fetching instr from memory to datapath register IR
  ID: decoding instr, including extracting its operands from register file registers fstop,scdop into ALU input ports A,B
  EX: execution proper, computing via ALU
    ALU operations: value of ALU output port C for given input A,B
    data memory or branch address:
      update memory address register MAR using A
      update memory data register MDR with B
      update jump address PC
      update by A or transfer to C interrupt address register IAR
  MEM: loading from or storing to mem at MAR via MDR
  WB: writing back C to the destination register
Phases reflected in ground model by control states

## Slide 8: Uniformity of ground model to architectural features
size of register file using abstract content fct reg
  width of datapath using abstract registers PC,IR,A,B,C, MAR,MDR,IAR
  instruction set (in immediate or not immediate form)
    Alu  Set
    Jump  Branch Denote JumpLink = Jump - {TRAP}
      Jump consists of absolute jump instructions of three types
        TRAP: system jump (save PC in IAR and update PC)
        Link: a set of jump links (save PC in C, to be stored in reg file). The destination register of LINK instructions is assumed to be fixed (in Hennessy/Patterson R31).
        a set of other (so-called plain) jumps
    Mem = Load  Store
    Interrupt = { MOVS2I, MOVI2S } manipulating IAR
  instruction format: using abstract parameter functions opcode, fstop, scdop, dest, iop, ival (arg IR suppressed)
  memory access (bandwith) using abstract function mem

## Slide 9
FETCH
Operand
Fetch
Mem
Addr
Jump
Branch
Alu
Jumps
IAR
I2S
IAR
S2I
OPERAND
Alu
Set
IAR
S2I
Load
Store
IAR
I2S
WRITEBACK
ALU
Write
Back
CIAR
IF
ID
EX
MEM
WB
Pipelining Stages
DLXseq
IARA
Jump
Link
Trap
Branch
JUMP
LINK
Link
CPC
BRANCH
TRAP
no
Store
STORE
LOAD
Subword
SUB
WORD
yes
Store
MEMADDR
MDRB
PassBtoMDR
Mem
Acc
no

## Slide 10: Ground Model DLXseq Macros
IF: FETCH = IR  mem(PC), PC  next(PC)
ID: OPERAND = A  fstop, B  scdop
    JumpBranch = opcode  Jump  Branch
    AluSet = opcode  Alu  Set
    LoadStore = opcode  Load  Store
    IARS2I/IARI2S = opcode  { MOVS2I, MOVI2S }
EX: ALU = if iop(opcode) then C opcode(A,ival)
else C opcode(A,B)
  MEMADDR = MAR  A + ival
  BRANCH = if reg(A) = 0 then PC  PC + ival
    TRAP = IAR  PC, PC  ival
    JUMPLINK = if iop(opcode) then PC  PC + ival
  else PC  A
MEM: LOAD = MDR  mem(MAR)
    STORE = mem(MAR)  MDR
    SUBWORD = C opcode(MDR)
WB: WRITEBACK = dest  C
R  S  reg(R): = reg(S)
standard instruction argument IR and reg notationally suppressed

## Slide 11
FETCH
IR  mem(PC)
PC  next(PC)
IR  meminstr(PC)
If not jumps then PC  next(PC)
OPERAND
A  fstop
B scdop
A  fstop
B  scdop
IF, ID macros
DLXseq
DLXpar
Pre
serve
Refining DLXseq to DLXpar
control states become guards of instruction phases in rules
latches for longer living values: IR1,IR2,IR3,PC1,C1 with preservation rules
resolving structural conflicts by doubling resources
    code memory meminst increasing mem bandwith for simultaneous access
    incrementing PC with function next, avoiding use of ALU
    separating load/store accesses by splitting MDR into LMDR, SMDR
Speeding up pipe stages by incorporating SUBWORD into WB
Update of PC1 for instruction scheduling reasons connected to jump instructions
IR1IR
PC1 next2(PC)
jumps = opcode(IR1) Jumps or (opcode(IR1) Branch, reg(A)=0)

## Slide 12
ALU
If iop(opcode)
then Copcode(A,ival)
else Copcode(A,B)
If opcode(IR1)  Alu  Set then
If iop(opcode(IR1))
then C  opcode(IR1)(A,ival(IR1))
else C  opcode(IR1)(A,B)
IR2

IR1
MEMADDR
MAR  A + ival
If opcode(IR1)Load  Store then
MAR  A + ival(IR1)
PassBto
MDR
MDR  B
If opcode(IR1)  Store then
SMDR  B
MOVS2I
C  IAR
If opcode(IR1) = MOVS2I then C  IAR
MOVI2S
IAR  A
If opcode(IR1) = MOVI2S then IAR  A
BRANCH
If reg(A)=0 then
PC  PC + ival
If opcode(IR1)  Branch then
If reg(A)=0 then PC  PC1 + ival(IR1)
TRAP
IAR  PC
PC  ival
If opcode(IR1) = Trap then
IARPC1, PC ival(IR1)
JUMPLINK
If iop(opcode)
then PC  PC + ival
else PC  A
If opcode(IR1)  JumpLink then
If iop(opcode(IR1)) then
PC PC1+ival(IR1) else PC A
LINK
C  PC
If opcode(IR1)  Link then CPC1
EX macros
DLXseq
DLXpar
Preserve
Refining EX stage
rules

## Slide 13
LOAD
MDR  mem(MAR)
If opcode(IR2)  Load then
LMDRmem(MAR)
IR3
IR2
C1C
STORE
mem(MAR)  MDR
If opcode(IR2)  Store then
mem(MAR) SMDR
SUBWORD
C  opcode(MDR)
WRITE
BACK
dest  C
If opcode(IR3)Alu  Set  Link  {MOVS2I}
then dest(IR3) C1
If opcode(IR3)Load then
dest(IR3)  opcode(IR3)(LMDR)
MEM, WB macros
DLXseq
DLXpar
Preserve
Refining DLXseq MEM, WB stage rules to DLXpar
Speeding up pipe stages
combining SUBWORD
with WRITEBACK
separate overlapping load/store accesses
splitting MDR into LMDR, SMDR

## Slide 14
FETCH
WRITEBACK
IF
ID
EX
MEM
WB
Pipelining Stages
DLXpar Rules
ALU
MOVI2S
MEMADDR
PassBtoMDR
JUMP
LINK
LINK
BRANCH
TRAP
Preserve1
MOVS2I
OPERAND
Preserve
STORE
LOAD
Preserve2
Ideally all rules fire simultaneously
  one per instruction in its successive stages
The problem: how to guarantee that no conflicts arise when an instruction exec uses data which have to be computed by a preceding instruction whose pipelined execution is not yet terminated

## Slide 15: DLXpar Correctness Theorem
Theorem: For each DLX program P, let Ppar be its transformation obtained by inserting two empty instructions after each occurrence of a jump or branch instruction ( “instruction scheduling” ). Let C be the DLXseq computation with input P and Cpar the corresponding DLXpar computation with input Ppar. Then C and Cpar have the same result if Cpar is data-hazard-free.
  Tasks to be accomplished:
    define “correspondence” of computation
    define “ computation result” and “sameness” for them
    define “data-hazard” and data-hazard-freeness
    prove the statement
    justify the assumption on transforming P to Ppar
  Instruction scheduling serves here to separate semantics preserving parallelization from hazard prevention

## Slide 16: Defining corresponding instruction cycles
instruction cycle for instr
  in DLXseq any subcomputation starting with control state FETCH with loading instr from the code memory until the next occurrence of control state FETCH
  in DLXseq any subcomputation starting with instr and ending with the first pipe stage of instr at the end of which the values of all result locations of instr are computed and recorded in the appropriate location as defined below
    this pipe stage is denoted EX(instr), MEM(instr), WB(instr) depending on instr (see table below)
corresponding instruction cycles in C and Cpar
  ever pair (Ii,Ii’) of instruction cycles I0 , I1, … in C and
  I0’ , I1’ ,…in Cpar where I0 , I’0 are corresponding initial states (with corresponding initialization)

## Slide 17: Defining result locations and result of an instr
In DLX every instr has only one result proper (different from <reg,PC>). It is written at the end of the execution of instr.
<reg,dest(instr)>
Alu Set  Load
 Link  { MOVS2I}
WB(instr)
<reg,IAR>
{ TRAP, MOVI2S}
EX(instr)
<reg,PC>
Jump  Branch
EX(instr)
Jump  Branch
IF(instr)
<mem,arg>
Store
MEM(instr)
where arg = value of reg(fstop(instr))+ival(instr) when fetching instr
Result Location
of instr
Updated by
instr of type
To be collected after
the end of pipe stage
result of instr (or instr cycle) =
values f(a) assigned to
the result locations <f,a> for instr
at the end of the execution of instr
result of a computation =
sequence of results
of its instruction cycles

## Slide 18: Defining used locations
<reg,nthop>
Alu Set  {MOVI2S}
Branch 
Jump - { TRAP}
EX(instr)
Load  Store
MEM(instr)
<reg,IAR>
{ MOVS2I}
EX(instr)
<reg,PC>
Jump  Branch
EX(instr)
Jump  Branch
IF(instr)
<mem,arg>
Load
MEM(instr)
where arg = value of reg(fstop(instr))+ival(instr) when fetching instr
Location
Used by instr of type
Critical use
in stage
what instr uses:
static info encoded in instr
PC
operands in register file
mem locations
interrupt address reg

## Slide 19: Defining data hazards
conflicts can arise in two cases:
    data hazard: I’ uses as one of its operands the content of the destination register of a preceding I in the pipe
    control hazard: I’ enters the pipe shortly after a jump or branch instruction
I <1,2,3 I’ iff instr cycle for I’ starts 1, 2, or 3 steps after an instr cycle for I
I’ data dependent on I iff I <1,2,3 I’ and one of the following two cases holds:
  dest(I)  {fstop(I’),scdop(I’)} and I’JumpBranch
  dest(I) = fstop(I’) and I’  JumpBranch
DLXpar computation data-hazard-free if it contains no occurrence of an I’ which is in the pipe together with an occurrence of an I on which it is data dependent

## Slide 20: Instruction Scheduling
Goal: separate analysis of control hazards from correctness proof for parallelization:
    Problem: when a jump or branch instr is fetched, the two immediately following instruction cycles generate results which could spoil the continuation of the computation after the jump
Solution: assume for the correctness proof that the compiler produces Ppar from P placing two empty instructions after each jump or branch instruction.
      We define empty instructions NOT to start an instruction cycle.
      We assume these new instructions to be linked by the extension of the next function of P in the obvious way, as formalized by the PC- preservation rule PC1  next(next(PC)).
  Assume the compiler to guarantee hazard-freeness
    Both assumptions will be discharged in separate refinement steps

## Slide 21: Proof of DLXpar Correctness Theorem
  To establish: C and Cpar have the same result (assuming Cpar is data-hazard-free)
  Proof by in induction on the given runs, decomposing computations in instruction cycles so that the proof can be done instructionwise with ‘local’ arguments. This needs a stronger induction hypothesis:
DLXpar Lemma. Let ICn,ICparn be the n-th instruction cycle in C, Cpar. The following holds:
a) Completeness: If Cpar is data-hazard-free, then ICn,ICparn are instruction cycles for the same instr and start with the same values for the “relevant locations” used by instr
b) Correctness: Any instr cycle pairs as in a) for any instr which is not data-dependent on any instruction in the pipe compute the same result
  The lemma implies the theorem.

## Slide 22: Defining relevant locations for DLXpar
A location l used by instr is a relevant location except in the following two cases:
  Irrelev 1. I = <reg,IAR> and instr = MOVS2I enters the pipe 1, 2 or 3 stages after an occurrence of MOVI2S or of TRAP
    NB. No conflict can arise from using <reg,IAR> because MOVS2I. the only instruction which uses IAR, can never be in conflict with any preceding instruction. If I writes into IAR, then I=TRAP or I=MOVI2S and I writes into IAR in its third pipe stage. Therefore if I <1,2,3 I’ , then I has already written into IAR when I’ uses it.
  Irrelev 2. I = <mem,arg> and instr is a Load instruction which enters the pipe 1, 2, or 3 steps after an occurrence of a Store instruction for the same arg (see justification below)

## Slide 23: Rational for Irrelev 2 for DLXpar
Irrelev 2. I = <mem,arg> and instr is a Load instruction which enters the pipe 1, 2, or 3 steps after an occurrence of a Store instruction for the same arg
  No conflict can arise from using a mem location because load instructions---the only ones which use memory locations---can never be in conflict with preceding store instructions---the only ones which write into mem locations.
    If I Store and I' Load, then I updates its result location < mem, reg (fstop(I)) + ival (I)> in its fourth pipe stage and I' reads the value of the location < mem, reg (fstop (I)) + ival (I)> in its fourth pipe stage too. Therefore if I <1,2,3 I’ and I' loads the value of the result location of I as updated by I, then I has already updated this result location when I' loads from there.
    NB. DLX does not support self-modifying code

## Slide 24: Proof of DLXpar Lemma (a)
ad completeness: ICn,ICparn are instruction cycles for the same instr and start with the same values for the “relevant locations” used by instr
  n=0: by correspondence of runs and initialization
  n+1: by inductive hypothesis, for each i  n, ICpar’ starts with the same values for the relevant locations as does ICi and they both compute the same result. Therefore ICn+1,ICparn+1 are instruction cycles for the same instruction, say instr, and start with the same values for the relevant locations to be used by that instruction.

## Slide 25: Proof of DLXpar Lemma (b)
ad correctness: any instr cycle pair ICn,ICparn as in a) where instr is not data-dependent on any instruction in the pipe compute the same result
  Due to the absence of stalls, the n+1-th instruction cycle in Cpar starts
    after the first step of ICparn in case instrn is neither a branch instruction with true branching condition nor a jump
    otherwise the n+1-th instruction cycle in Cpar starts after the third step of ICparn due to the following Jump Lemma
Jump Lemma. If a jump or branch instruction I is fetched in a DLXpar-computation, then the following two fetched instructions are empty and at stage ID(I) the register PC1 is updated by the correct value to be used for the computation of the possible new PC-value in stage EX(I).
  By a case distinction following the instruction type it then follows from the definition of the rule macros that corresponding updates in C and Cpar provide the same values for corresponding result locations.

## Slide 26: Proof of Jump Lemma
Jump Lemma. If a jump or branch instruction I is fetched in a DLXpar-computation, then the following two fetched instructions are empty and at stage ID(I) the register PC1 is updated by the correct value to be used for the computation of the possible new PC-value in stage EX(I).
Proof: follows by an induction on the number of jump instructions which are fetched during a run, using the transformation of P to Ppar.

## Slide 27: Resolving data hazards for linear code execution
Goal: refine DLXpar to DLXdata where data hazards are resolved for non-jump/branch instructions so that the compiler assumption of hazard-freeness can be restricted to jump/branch instructions.
  I.e. we have to define DLXdata and to prove the following:
Theorem. Let C, Cdata be the computations of DLXseq , DLXdata started with program P, Ppar . Assume that in Cdata no occurrence of a jump or branch instruction is in the pipe together with an occurrence of an instruction on which it is data dependent. Then C and Cdata compute the same result.

## Slide 28: Data hazards for linear code execution
Data dependence condition DataDep(I,I’):
    I’  Jump Branch and
    I <1,2,3 I’ and dest(I)  {fstop(I’), scdop(I’) }
  NB. no write-after-write hazard can occur in DLX
    writing only in stage WB, but together with any stalled instruction every later instruction in the pipe is also stalled
  NB. no write-after-read hazard can occur in DLX
    read stage ID precedes the write stage WB
Hazard Resolution Method: standard techniques for hazard resolution incorporated into DLXpar macros
  forwarding via
    new dataflow connections (hardware links)
    additional decoder logic (multiplexing)
  stalling

## Slide 29: Conservative refinement of DLXpar macros to resolve data hazards for linear code execution
Idea:
  refine macros only for case DataDep(I,I’):
    if DataDep(I,I’), then the DLXdata macro refinement guarantees that correct arguments are taken to compute the result of instr, namely during EX(instr)-phase
    otherwise the DLXpar macro is executed
  weakening the compiler hazard-freeness assumption
    by refining the notion of relevant locations, taking out the hazardous locations since they are taken care of by the refined architecture
NB. This idea realizes an abstract form of the typical implementation using a scoreboard to keep track of data dependencies

## Slide 30: Proof of DLXdata Correctness Theorem
  Proof follows from the following lemma:
DLXdata Lemma. Let ICn,ICparn,ICndata be the n-th instruction cycle in C, Cpar, Cdata. Then:
Completeness: If Cdata is free of data hazards for jump/branch instructions, then ICn,ICparn,ICndata are instruction cycles for the same instruction I’ and start with the same values for the relevant locations used by I’.
For any I’-cycles IC, ICpar,ICdata as in a):
  Conservativity: if I’ is not data-dependent on any I in the pipe, then ICpar,ICdata compute the same result
  Refinement: if I’  Jump Branch is data-dependent on an I <1,2,3 I’ in the pipe, then IC,ICdata compute the same result

## Slide 31: Proof of DLXdata Lemma (1)
By induction on number n of instr cycles:
ad completeness: ICn,ICndata are cycles for the same instr and start with the same values of relevant locs
  n=0: by correspondence of computations
  n+1: follows from Jump Lemma as for DLXpar
ad conservativity: to show: if I’ is not data-dependent on any I in the pipe, then ICpar,ICdata compute the same result
  in case of no data dependence, in every pipe stage rule applied to I’, the DLXpar-macro is executed. Since by assumption ICpar and ICdata start with the same values for the relevant locations used by I', the effect of the rule applications to I' is the same in ICpar and ICdata, including the result locations of I‘. Then by the DLXpar lemma the result loc values of I’ are the same in IC and ICdata

## Slide 32: Proof of DLXdata Lemma (2)
ad Refinement: Let I’Jump  Branch be data-dependent on an I <1,2,3 I’ in the pipe. To show: IC,ICdata compute the same I’-result.
By definition of dest and assumption on I’:
  I  AluSet Load  Link { MOVS2I}
  I’  AluSet Load Store { MOVI2S} since I’  {MOVS2I}  Jump Branch
fstop(instr)
 Alu Set  Mem  JumpLink  Branch { MOVI2S}
sndop(instr)
Alu Set Store
function
defined for instr
dest(instr)
 Alu Set  Load  Link  {MOVS2I}

## Slide 33: Proof of DLXdata Lemma: Case I  Mem
Then
  I  AluSet Link { MOVS2I}, dest(I) is updated to the value used by I’ in WB(I), namely to the value of C1, which is copied in MEM(I) from C as
    computed in EX(I) by an ALU  SET operation
    or as content of PC1 (Link) or IAR (MOVS2I)
  Case I <2,3 I’: ID(I‘) overlaps with WB(I) or MEM(I) with the expected operand value in C1 or C
  Case I <1 I’: expected operand value computed during ID(I‘) and available not before EX(I‘)

## Slide 34: DLXdata Lemma: Case I  Mem , I <2,3 I’
Case I <2,3 I’: Refinement of OPERAND
  Since ID(I‘) overlaps with WB(I) or MEM(I) with the expected operand value in C1 or C, nthReg=A,B (nth=fst,scd) can be updated with C1 or C (called below C’)
  if nthop(IR) {dest(IR3),dest(IR2)} refinement case
  then nthReg  C’
  else nthReg  nthop(IR) conservative case
  where C’ = if nthop(IR) = dest(IR3)  dest(IR2) then C1
  if nthop(IR) = dest(IR2) then C last update counts
  Irrelev 3. I = <reg,nthop(I’)> where I’Jump  Branch for some I <2,3 I’ such that I  Mem, nthop(I’) =dest(I)
  Hw Cost: direct link bw register file exits A,B and C,C1

## Slide 35: DLXdata Lemma: Case I  Mem , I <1 I’
Case I <1 I’: Refining EX-macros by forwarding
  expected operand value computed during ID(I‘) is available at the end of EX(I) in C, to be forwarded directly to ALU for EX(I’), shortcutting transfer from C to register file to A,B
Refine EX-rules for I’  Alu  Set Load Store { MOVI2S}
  Method: adding to macros a clause which in the data hazard case provides the argument C instead of A,B
  Hw Cost: direct link between C and
    both ALU ports for I’  Alu  Set
    IAR for I' = MOVI2S
    MAR and SMDR for I’  MEM
  together with additional control logic (multiplexers) to select as ALU input the forwarded value rather than the value from the register file
  Irrelev 4. <reg,nthop(I’)> for possible combinations for I’

## Slide 36: DLXdata Lemma: Case I  Mem , I <1 I’ : Irrelev locs
Irrelev 4. <reg,nthop(I’)> such that for some I <1 I’ with I  Mem one of the following holds:
  opcode (I')  Alu  Set, iop (opcode (I')), dest (I) = fstop (I'), nth = fst
  opcode (I')  Alu  Set, not iop (opcode (I')), dest (I) = nthop (I')
  opcode (I')  Mem  {MOVI2S}, nth = fst, dest (I) = fstop (I')
  opcode (I')  Store, nth = scd, dest (I) = scdop (I')

## Slide 37: DLXdata Lemma: Case I  Mem , I <1 I’ : refined rules
If opcode(IR1)Load  Store then MEMADDR
if fstop(IR1) = dest(IR2) refinement case
then MAR  valfst + ival(IR1)
else MAR  A + ival(IR1) conservative case
where valnth = C if nothop (IR1) = dest(IR2)
= nthReg otherwise with fstReg=A,scdReg=B
If opcode(IR1)Store then PassBtoMDR
if scdop(IR1) = dest(IR2) refinement case
then SMDR  valscd
else SMDR  B conservative case
Analogously for ALU and MOVI2S rules

## Slide 38: Proof of DLXdata Lemma: Case I  Mem and I’  Mem
Then ILoad, I’ AluSet Link{ MOVI2S}
  expected value, loaded by I, available in LMDR at the end of MEM(I)
  Case I <2,3 I’: expected operand value available in EX or ID stage in LMDR
    refining ID-rule OPERAND and EX-rules ALU,MOVI2S
  Case I <1 I’: stall pipeline 1 clock cycle, at the latest before EX(I’), to let only MEM and WB stages progress
    NB. During a pipeline stall a just loaded value in LMDR may be written back; since in the next step it may serve as operand of a stalled instruction, we preserve LMDR

## Slide 39: DLXdata Lemma: Case I  Mem, I’  Mem, I <2,3 I’: refined C’
Case I <2,3 I’: refining
  C’ in OPERAND by LMDR and
  valnnth in ALU, MOVI2S by LMDR1
    using new WB-stage preservation rule LMDR1  LMDR
C’ =
LMDR last update in ante-ante-preceding load instr
if nthop(IR) = dest(IR3)  dest(IR2), opcode(IR3)  LOAD
  where LMDR = opcode(IR3) (LMDR)
  C1 previous case
  if nthop(IR) =dest(IR3)  dest(IR2), opcode(IR3)  LOAD
  C if nthop(IR) = dest(IR2) previous case

## Slide 40: DLXdata Lemma:I  Mem, I’  Mem, I <2,3 I’: refine valnth
Case I <2,3 I’: refining
  valnnth in ALU, MOVI2S by LMDR1
    new WB-stage preservation rules LMDR1  LMDR, IR4  IR3 in case an LMDR-value, written back during a pipeline stall, in the next step serves as operand of an instruction stalled after ID
valnnth =
C if nthop(IR) = dest(IR2) previous case
LMDR if nthop(IR1) = dest(IR3)  dest(IR2), opcode(IR3)  LOAD, opcode(IR4)  LOAD
case of no two successive load instructions
LMDR1 if nthop(IR1) = dest(IR4)  dest(IR2), dest(IR3), opcode(IR3), opcode(IR4)  LOAD
nthReg otherwise DLXpar case

## Slide 41: DLXdata Lemma:I  Mem, I’  Mem, I <2,3 I’: refined rules
If opcode(IR1) Alu  Set then ALU macro
if iop(opcode) then
if fstop(IR1) = dest(IR2) or for some m  {3, 4}
fstop(IR1) = dest(IRm) and opcode(IRm)  LOAD
then C  opcode(IR1) (valfst , ival(IR1))
else C  opcode(IR1) (A, ival(IR1))
else if dest(IR2)  {fstop(IR1), scdop(IR1) } or
for some m  {3, 4} opcode(IRm)  LOAD and
dest(IRm)  {fstop(IR1), scdop(IR1)}
then C  opcode(IR1) (valfst , valscd )
else C  opcode(IR1) (A, B)
Analogously for MOVI2S, MEMADDR, PassBtoMDR

## Slide 42: DLXdata Lemma:I  Mem, I’  Mem, I <2,3 I’: Irrelev locs
Irrelev 5. <reg,nthop(I’)> with I’MemBranchJump such that for some ILoad with dest (I) = nth op (I'), one of the following holds:
  I <3 I’
  I <2 I’ , iop (opcode (I')), nth = fst
  I <2 I’ , not iop (opcode (I‘))

## Slide 43: DLXdata Lemma: Case I  Mem, I’  Mem, I <1 I’
Case I <1 I’: stop EX(I’) together with IF,ID of later instructions for 1 clock cycle, letting only MEM and WB stages progress, to make value loaded by I available to I’
loadRisk = opcode (IR2)  LOAD and
reg (IR1)  Mem  Jump  Branch and
dest (IR2)  {fstop (IR1) , scdop (IR1)}
adding guard not loadRisk to EX,ID,IF stage rules
adding IF stage rule if loadRisk then IR2  undef
  whose execution makes loadRisk false so that the full pipelining will be resumed and this case can be handled as the previous one and is resolved by the refined EX-rules
Irrelev 6. <reg,nthop(I’)> for I’MemBranchJump and some ILoad: I <1 I’, dest (I) = nth op (I')

## Slide 44: Proof of DLXdata Lemma: Case I,I’  Mem
Case I <2,3 I’: expected operand value available in EX or ID stage
    forwarding solution by ID-rule OPERAND and refined EX-rules ALU,MOVI2S
    hw price: direct links bw LMDR and MAR, SMDR, new LMDR1
Case I <1 I’:
  Subcase 1. I’ uses the loaded val as datum to be stored: dest(I)=scdop(I’)
    forwarding solution
  Subcase 2. I’ uses the loaded val as address for Mem opn: dest(I)=fstop(I’)
    stalling-pipeline solution

## Slide 45: DLXdata Lemma: Case I,I’  Mem, I <2,3 I’
Subcase I <3 I’: resolved by ID-rule OPERAND
Subcase I <2 I’: resolved by refining MEMADDR and PassBtoMDR as shown above for ALU
Irrelev 7.
  <reg,nthop(I’)> for I’  Mem such that for some ILoad: I <3 I’, dest (I) = nthop (I')
  <reg,fstop(I’)> for I’  Mem such that for some ILoad: I <2 I’, dest (I) = fstop (I')
  <reg,scdop(I’)> for I’  Store such that for some ILoad: I <2 I’, dest (I) = scdop (I')

## Slide 46: DLXdata Lemma: Case I,I’  Mem, I <1 I’
Subcase 1: dest(I)=scdop(I’), i.e.I’ uses the loaded val as datum to be stored
  Then I’  Store, val loaded by I needed in MEM(I’) where available in LMDR
    forwarding solution by refining STORE
    hw price: link bw LMDR and memory input port
  Irrelev 8. <reg,scdop(I’)> for I’  Store such that for some ILoad: I <1 I’, dest (I) = scdop (I')
Subcase 2: dest(I)=fstop(I’), i.e. I’ uses the loaded val as address for Mem opn
  stalling pipeline: refine loadRisk by clause
  or dest(IR2) = fstop(IR1), IR1  Mem
  Irrelev 9. <reg,fstop(I’)> for I’  Mem such that for some ILoad: I <1 I’, dest (I) = fstop (I')

## Slide 47: Exercises
Resolve the conflict in case IMem, I’ Mem above without preserving LMDR.
  Hint. Anticipate the stalling from the EX phase to the ID phase, recognizing loadRisk already in phase ID. See Hinrichsen 1998.
Refine DLXdata to DLXpipe and prove it to correctly solve also control hazards (those triggered by jump or branch instructions).
  Hint. See Section 5 in Börger and Mazzanti 1997 (LNCS 1212)

## Slide 48: References
J.L.Hennessy and D.A.Patterson: Computer Architecture: A Quantitative Approach
  Morgan Kaufmann 1990,1996
E. Börger and S. Mazzanti: A practical method for rigorously controllable hardware design
  Springer LNCS 1212 (1997) 151-187
H. Hinrichsen: Formally correct construction of a pipelined DLX architecture.
  TR 98-5-1, May 1998, Darmstadt University of Technology, Dept. of Electrical and Computer Engineering
S.Tahar.Eine Methode zur formalen Verifikation von RISC-Prozessoren.
  Fortschrittberichte VDI, Reihe 10:Informatik/Kommunikationstechnik Nr. 350, VDI-Verlag, Duesseldorf 1995, pp.XIV+162.
E. Börger, R. Stärk: Abstract State Machines. A Method for High-Level System Design and Analysis Springer-Verlag 2003, see http://www.di.unipi.it/AsmBook