## Slide 1: Production Cell Case Study An ASM Solution
Egon Börger
Dipartimento di Informatica, Universita di Pisa
http://www.di.unipi.it/~boerger

## Slide 2: Production Cell Case Study Goals
Ground Model construction for inspection by application domain expert
Stepwise Refinement to executable code whose module structure reflects the decomposition of the ground model into components
Verification of required controller properties
Validation of code by experimentation with the FZI production cell simulator
Documentation of the design at each level

## Slide 3
E. Börger, R. Stärk
Abstract State Machines
A Method for High-Level System Design and Analysis
Springer-Verlag 2003
For update info see AsmBook web page:
http://www.di.unipi.it/AsmBook
For details see Chapter 5 (Synchronous Multi-Agent ASMs) of:

## Slide 4: Reflecting the Component Structure
…the production cell is composed of two conveyor belts, a positioning table, a two-armed robot, a press, and a travelling crane. Metal plates inserted in the cell via the feed belt are moved to the press. There, they are forged and then brought out of the cell via the other belt and the crane
Therefore one basic ASM is defined for each device
  with precise interfaces for device interaction and explicitly stated physical assumptions
Wlog the entire system is viewed as synch ASM
  given that each device interacts in a sequential manner with exactly one predecessor and one successor device

## Slide 6: Feed Belt Description
…The task of the feed belt consists in transporting metal blanks to the elevating rotary table. The belt is powered by an electric motor, which can be started up or stopped by the control program. A photoelectric cell is installed at the end of the belt; it indicates whether a blank has entered or left the final part of the belt. ... the photoelectric cells switch on when a plate intercepts the light ray. Just after the plate has completely passed through it, the light barrier switches off. At this precise moment, the plate ... has just left the belt to land on the elevating rotary table---provided of course that the latter machine is correctly positioned ... the feed belt may only convey a blank through its light barrier, if the table is in loading position ... do not put blanks on the table, if it is already loaded ...

## Slide 7: Deposit Belt Description
… The task of the deposit belt is to transport the work pieces unloaded by the second robot arm to the traveling crane. A photoelectric cell is installed at the end of the belt; it reports when a work piece reaches the end section of the belt. The control program then has to stop the belt. The belt can restart as soon as the traveling crane has picked up the work piece. ... photoelectric cells switch on when a plate intercepts the light ray. Just after the plate has completely passed through it, the light barrier switches off. At this precise moment, the plate is in the correct position to be picked up by the traveling crane ...

## Slide 8: Modelling Transport Belts for Reuse
Abstracting from motors and peculiar timing of reaction to sensor changes
PieceAtLightBarrier  PhotoelectricCell=on
PieceDeliverable  TableReadyForLoading
DeliverPiece 
For DepBelt: when light barrier switches off
FeedBeltFree:=true
TableLoaded:=true
Not PieceAt
Light Barrier
Critical
Run
For DepBelt: DepBeltLoadable:=true
Run
DeliverPiece
PieceAt
Light Barrier
Stop
Piece
Deliverable
yes
no

## Slide 9: Elevating Rotary Table Description
…The task of the elevating rotary table is to rotate the blanks by about 45 degrees and to lift them to a level where they can be picked up by the first robot arm. The vertical movement is necessary because the robot arm is located at a different level than the feed belt and because it cannot perform vertical translations. The rotation of the table is also required, because the arm's gripper is not rotary and is therefore unable to place the metal plates into the press in a straight position by itself.

## Slide 10: Modelling Elevating Rotary Table
Abstracting from motors, rotation and lifting
StoppedIn
LoadPos
MoveTo
Unload Pos
Table
Loaded
StoppedIn
UnloadPos
not Table
Loaded
MoveTo
Load Pos
Making Movement durative:
MoveToActionPos 
ActionPos
Reached
MovingTo
ActionPos

## Slide 11: Robot Description
…The robot comprises two orthogonal arms. For technical reasons, the arms are set at two different levels. Each arm can retract or extend horizontally. Both arms rotate jointly. Mobility on the horizontal plane is necessary, since elevating rotary table, press, and deposit belt are all placed at different distances from the robot's turning center. The end of each robot arm is fitted with an electromagnet that allows the arm to pick up metal plates. The robot's task consists in: taking metal blanks from the elevating rotary table to the press; transporting forged plates from the press to the deposit belt.

## Slide 12: Modelling Robot: Device Action Rules
Abstracting from motors, movement details, magnet
Waiting
For
DevAction
Yield
(DevAction)
DevReady
ForAction
DevAction
MovingTo
Next(DevAction)
Completed
DevAction
ReachedPosFor
Next(DevAction)
WaitingFor
Next(DevAction)
Defining DevAction  Next(DevAction) (the suggested order):
TableUnload  PressUnload  DepBeltLoad  PressLoad
Yield : TableLoaded:=false PressLoaded:=false
DepBeltLoadable:= false PressLoaded := true

## Slide 13: Robot Action Macros
DevAction
Next (DevAction)
Yield (DevAction)
TableUnload
PressUnload
TableLoaded:=false
PressUnload
DepBeltLoad
PressLoaded:=false
DepBeltLoad
PressLoad
DepBeltLoadable:=false
PressLoad
TableUnload
PressLoaded:=true

## Slide 14: Robot Interface Predicates
DevReadyForUnload  for Dev =Table, Press
  DevInUnloadPos and DevLoaded
    TableInUnloadPos  ERT.ctl_state = StoppedInUnloadPos
    PressInUnloadPos  Press.ctl_state = OpenForUnload
PressReadyForLoad 
  PressInLoadPos and not PressLoaded
    TableInUnloadPos  ERT.ctl_state = StoppedInUnloadPos
    PressInLoadPos  Press.ctl_state = OpenForLoad
DepBeltReadyForLoad = (DepBeltLoadable= true)

## Slide 15: Press Description
…The task for the press is to forge metal blanks. The press consists of two horizontal plates, with the lower plate being movable along a vertical axis. The press operates by pressing the lower plate against the upper plate. Because the robot arms are placed on different horizontal planes, the press has three positions. In the lower position, the press is unloaded by arm 2, while in the middle position it is loaded by arm 1. The operation of the press is coordinated with the robot arms as follows: 1. Open the press in its lower position and wait until arm 2 has retrieved the metal plate and left the press, 2. Move the lower plate to the middle position and wait until arm 1 has loaded and left the press, 3. Close the press, i.e. forge the metal plate. This processing sequence is carried out cyclically.

## Slide 16: Modelling Press
Abstracting from movement details
MoveTo
TopPos
Forging
Completed
ClosedFor
Forging
MoveTo
BottomPos
OpenFor
Unload
MoveTo
MiddlePos
not Press
Loaded
OpenFor
Load
Press
Loaded
Making movement durative:
MoveToAnyPos 
AnyPos
Reached
MovingTo
AnyPos

## Slide 17: Verification of Ground Model Properties
Safety Properties proved from assumptions on device placements, movements, actions
  no movement outside its bounds, no crash between devices, no action unless safe, etc.
Liveness proved: every blank put on the FeedBelt will eventually be forged and picked up by the crane at the end of the DepBelt
  exploiting the sequential order of travel of blanks
Maximal Performance (maximal throughput in minimal time) proved from assumptions on the time of device actions, movements and insertion of blanks to the FeedBelt

## Slide 18: Data Refinement of Feed Belt Movement as Motor Driven
Definition:
  ctl_state = Run  FeedBeltMot = on & not Delivering
  ctl_state = CriticalRun  FeedBeltMot = on & Delivering
  ctl_state = Stop  FeedBeltMot = off
Correspondingly the ctl-state updates become (non-optimized):
  ctl_state := Run  FeedBeltMot := on & Delivering:=false
  ctl_state := CriticalRun  FeedBeltMot := on & Delivering := true
  ctl_state := Stop  FeedBeltMot := off

## Slide 19: (1,2) - Refinement of Elevating Rotary Table by Vertical and Horizontal, Motor Driven Movement
ctl_state = StoppedInLoadPos 
  BottomPosition & MinRotation & TableElevationMot = TableRotationMot = Idle
ctl_state = StoppedInUnloadPos 
  TopPosition & MaxRotation & TableElevationMot = TableRotationMot = Idle
ctl_state = MovingToLoadPos 
  TableElevationMot = Up or TableRotationMot = clockwise
ctl_state = MovingToUnloadPos 
  TableElevationMot = Down or TableRotationMot = counterClockwise

## Slide 20: Signature for Robot Refinement by Rotation & Extension/Retraction of Magnetic Arms
RobotRotationMot with Angle measuring rotation
  Angle values where rotation stops for arm movement:
    Arm1ToTable, Arm2ToPress, Arm2ToDepBelt, Arm1ToPress (in the suggested rotation order)
Arms which can be extended/retracted
  Arm1Mot to reach Table/Press with Arm1
  Arm2Mot to reach Press/DepBelt with Arm2
  sensor ArmiExt measuring extension of Armi (i =1,2) with 4 values where extension/retraction stops
    Arm1AtTable, Arm2AtPress, Arm2AtDepBelt, Arm1AtPress (in the suggested rotation order)
  Magnets ArmiMagnet { on,off } to pick up or release pieces (i =1,2)

## Slide 21: Refinement of Robot ctl states WaitingFor/MovingTo
RobotIdle  RobotRotationMot = Arm1Mot = Arm2Mot = idle
ArmsRetracted  Arm1Ext = Arm2Ext = retracted

## Slide 22: Data Refinement of Robot Waiting/Moving Rule
Waiting 
If WaitingForDevAction & DevReadyForAction
then Arm(DevAction)Mot:= extend
Moving 
If MovingToDevAction & ReachedPosForDevAction
then RobotRotationMot:= idle

## Slide 23: (1,3) - Refinement of Robot Actions: arm extension
Action.Extension 
If extending ArmToDev & ArmExt = ArmAtDev
Then ArmMot := idle
where
moving ArmToDev 
Angle = ArmToDev & ArmMot = mov
for mov = extend,retract
ArmToDev = Arm1ToTable, Arm2ToPress, Arm2ToDepBelt, Arm1ToPress
ArmAtDev = Arm1AtTable, Arm2AtPress, Arm2AtDepBelt, Arm1AtPress

## Slide 24: (1,3) - Refinement of Robot Actions: action proper
Action.Proper 
If extended ArmAtDev Then
ArmMagnet := on for ArmAtDev=Arm1AtTable, Arm2AtPress
off for ArmAtDev=Arm2AtDepBelt,Arm1AtPress
  ArmMot := retract
  Yield Act(ArmAtDev) NB. Corrects a mistake found by model checking (Plonka 2000)
where extended ArmAtDev 
Angle = ArmToDev & ArmExt = ArmAtDev
& ArmMot = idle
Act(ArmAtDev)  TableUnload,PressUnload,DepBeltLoad,PressLoad
for ArmAtDev = Arm1AtTable, Arm2AtPress, Arm2AtDepBelt, Arm1AtPress

## Slide 25: (1,3) - Refinement of Robot Actions: retraction
Action.Retraction 
If retracting ArmToDev & ArmExt =retracted Then
RobotRotationMot :=
clockwise if Arm=Arm1 & Dev=Press
counterClock else
  ArmMot := idle
for ArmToDev = Arm1ToTable, Arm2ToPress, Arm2ToDepBelt, Arm1ToPress

## Slide 26: Exercise: Press Data Refinement by Detailing Motor Driven Movement and Being Open/Closed
ctl_state = OpenForAction 
  PressMot = Idle & ActionPos
    where UnloadPos = BottomPos, LoadPos = MiddlePos
ctl_state = ClosedForForging 
  PressMot = Idle & TopPos
ctl_state = MovingToMiddlePos 
  PressMot = Up & not PressLoaded
ctl_state = MovingToTopPos 
  PressMot = Up & PressLoaded
ctl_state = MovingToBottomPos  PressMot = Down

## Slide 27: Implementation of the Refined Model
Structure Mapped from Machine To Code: One C++ module per submachine, plus a module for handling errors reported by the simulation
Sequentialization: decide upon the order in which the controller asks the simulation env for new status information and forwards it to the seven modules to execute them:
  since the component dependencies are completely described in the interfaces, wlog we can follow the order used by the simulator
    each machine module gets its updated sensor readings from the standard input, in the order specified by the status vector in the simulator

## Slide 28: Main C++ Program control.cc
#include "control.h"
cElist Errors;
cFeedBelt FeedBelt;
cElevRotTable ElevatingRotaryTable;
cRobot Robot;
cPress Press;
cDepositBelt DepositBelt;
cTravCrane TravelingCrane;
int main()
{ loop
{ AskNewStatus();
cin>> Press
>> Robot
>> ElevatingRotaryTable
>> TravelingCrane
>> FeedBelt
>> DepositBelt
>> Errors;
Oper();
};
}
control.h contains contains the defs of the classes and the modules AskNewStatus(), for the interface to env, and Oper(), for the piece inserting operator

## Slide 29: Code Validation
Correctness The code was extensively tested by Luca Mearelli, correctly controlling the simulator at FZI in Karlsruhe during night long experiments
Safety Properties All test runs worked conforming to all the safety requirements
  Maximal Performance: the maximum throughput of 7 pieces circulating in the system was achieved
Inspection The code was inspected at the Dagstuhl Seminar 9720 (12.5.-16.5.1997 ) on “Practical Methods for Code Documentation and Inspection” (See Report 178, edited by E. Börger, P. Joannou, D. Parnas)

## Slide 30: References
C. Lewerentz and T. Lindner (eds.), Formal Development of Reactive Systems.
  Case Study “Production Cell’’. Springer LNCS 891. 1995.
E. Börger and L. Mearelli,Integrating ASMs into the Software Development Life Cycle
  J.of Universal Computer Science 3(5) 1997, 603—665
L. Mearelli, Refining an ASM Specification of the Production Cell to C++ Code
  J.of Universal Computer Science 3(5) 1997, 666—688
FZI simulator for the production cell http://www.fzi.de/divisions/prost/projects/production_cell/ProductionCell.html
C++ code for Mearelli’s program which controls the FZI simulator http://www.fzi.de/prost/projects/production_cell/contributions/ASM.html

## Slide 31: References
E. Börger, R. Stärk: Abstract State Machines. A Method for High-Level System Design and Analysis Springer-Verlag 2003, see http://www.di.unipi.it/AsmBook
K. Winter, Model Checking for Abstract State Machines
  J.of Universal Computer Science 3(5) 1997, 689—701
C. Plonka, Model Checking for the Design with Abstract State Machines
  Diplomarbeit, University of Ulm, January 2000