## Slide 1: Using the IBIS Quality Checklist
Mike LaBonte, Cisco Systems
IBIS Open Forum Summit
4 October 2004
Appendix I_5
Used with permission of the IBIS Subcommittee on Quality

## Slide 2: IBIS Quality Subcommittee
IQ Purpose:
  Model Makers: produce IBIS files that users trust
  Model Users: receive IBIS file that work
IBIS Quality Specification
  http://www.sisoft.com/ibis-quality/docs/IQ_specification.txt
IBIS Quality Checklist
  http://www.sisoft.com/ibis-quality/docs/IQ_checklist.xls
  The specification is needed to understand checklist items.

## Slide 3: Overview of using the IQ Checklist
What you need:
  An IBIS file
  The IQ Checklist spreadsheet (copy)
  The IQ Specification
  Ibischk3 or ibischk4 program
  An IBIS file viewer that display I/V and V/T curves

## Slide 4: Start with a blank IQ Checklist spreadsheet

## Slide 5: Fill in basic information

## Slide 6: Run IBISCHK on the IBIS file
Use the latest IBISCHK
Change [IBIS ver] in the file to match the IBISCHK used

## Slide 7: Enter the ibischk results

## Slide 8: Use the IQ Specification as a reference

## Slide 9: Check each IBIS file header item

## Slide 10: IQ Checklist has multiple sheets
Sheet for each Component and Model
Copy and rename as needed

## Slide 11: Check the [Component]s
Fill in the name
Use N/A for irrelevant items

## Slide 12: Common errors
Example: [Pin] must not use the same Model for two pins if their electrical performance differs
Example: [Pin] must not have pin name “A02” if the datasheet has “A2”

## Slide 13: Check the [Model]s
Fill in the name
Use N/A for irrelevant items eg. Vinl and Vinh for an Output

## Slide 14: About IQ levels
PASSes LEVEL 0 check for reasonable C_comp
Correctness not checked by any means
Summary LEVEL is highest checked LEVEL
This is a LEVEL 0 model (at best)

## Slide 15: Summarize IQ level on each sheet
… and again on the Summary sheet
Determine overall IQ level

## Slide 16: Copy spreadsheet contents
Select all |IQ lines
Make sure every copied line has the |IQ
Use clipboard Copy
Missing |IQ !!!

## Slide 17: Paste into the IBIS file
After [Notes] is a good location
IBISCHK the file again, to guard against tabs and lines exceeding 80 characters

## Slide 18: Some checks require a curve viewer

## Slide 19: Some checks require combined I/V tables

## Slide 20: We need your feedback !
Get the IQ Checklist Kit and try it yourself:
  http://www.sisoft.com/ibis-quality/docs/IQ_checklist_kit.zip
Let us know what needs to change
Send checked IBIS files back to the vendor
How can we get a checker program written?
Ask your vendors to send you IBIS files with IQ!