## Slide 1: ROBOT GRIPPERS AND FEEDING DEVICES
T. Bajd and M. Mihelj

## Slide 2: Robot grippers
GRIPPERS
WITH
FINGERS
SPECIAL
GRIPPERS
GRIPPERS
WITH TWO
FINGERS
MULTIFINGERED
GRIPPERS
vacuum
magnetic
perforation
Multifingered grippers usually have three fingers, each having two or three segments. Such gripper has 6 or 9 DOFs which is the same or even more than robot manipulators.

## Slide 3: Robot gripper with two fingers
Pneumatic, hydraulic or electrical motors are used with two-fingered grippers. Usually they work in on-off regime. Distance or force between the fingers can be controlled.

## Slide 4: Kinematic presentations of two-fingered grippers
The robot grippers are often designed by the end-users of industrial robots. Simple kinematic presentations enable the choice of an appropriate gripper for the selected task.

## Slide 5: Twofold robot gripper
The robot with twofold gripper can simultaneously bring an unfinished part into the machine while taking a finished part out of it.

## Slide 6: Gripper with spring fingers
When grasping lightweight and fragile objects, grippers with spring fingers can be used.

## Slide 7: Form closure, force closure and combined grasp
A reliable grasp can be achieved either by form or force closure of the two fingers. Also possible is the combination of the two grasp modes.

## Slide 8: External, internal and intermediate grip
The grasping force can be applied only to the external or only to the internal surfaces of a work-piece. An intermediate grip is also possible.

## Slide 9: Vacuum gripper
Vacuum grippers are applied in cases when the surface of the grasped object is flat or evenly curved, smooth, dry and relatively clean. The advantages of these grippers are reliability, low cost and small weight.
Suction heads of various shapes are commercially available. Often we use several suction heads together.

## Slide 10: Grasping and releasing of an object with vacuum gripper
Releasing of very lightweight and sticky objects can be critical with vacuum grippers. In this case we release the objects with the help of positive pressure.

## Slide 11: Magnetic grippers
With magnetic grippers either permanent magnets (temperatures up to 500 ºC) or electromagnets (up to 100 ºC) are used. The surfaces of the objects must be even or clean.

## Slide 12: Special grippers
Perforation grippers are used for handling material such as textile or foam rubber. Adhesive grippers can be used when grasping very lightweight parts.

## Slide 13: Feeding devices
The task of the feeding devices is to bring parts to the robot in such a way that the robot knows their position and orientation without the use of robot vision.

## Slide 14
Feeding devices
The robot feeding devices must:
  not damage parts,
  operate reliably,
  position the parts accurately,
  work at sufficient speed,
  require minimal time for loading,
  contain sufficient number of parts.

## Slide 15: Pallets
The pallets store the parts, while determining their position and sometimes also orientation. We distinguish among three types of pallets: vacuum formed, injection molded and metal pallets.

## Slide 16: Simultaneous loading of a fixture table
The human operator takes a part from a container, where the parts are unsorted, and places it onto the fixture table.

## Slide 17: Loading of the pallets in advance
The pallets can be loaded in advance in some other place and afterwards brought into the robot cell. The pallet is positioned properly by the use of special pins in the working table.

## Slide 18: Rotating table
The rotating table enables loading of the pallets on one side, while the robot activities take place on the other side of the turntable. Improved speed and safety of the robot cell can be achieved.

## Slide 19: Part feeders
different types of parts can be used with the same part feeder (not in the same time)
large number of parts can be inserted
the parts can be filled disorderly

## Slide 20: Vibratory bowl feeder
The vibration of the bowl and the in-line feeder is produced by the use of an electromagnet. The vibrations cause the parts to travel out of the bowl. Specially formed spirally sloped fences force them into required orientation.

## Slide 21: Magazine feeder
A simple magazine feeder consists of a tube storing the parts and the sliding plate, which takes the parts one by one out of the magazine.

## Slide 22: Integrated circuits magazine feeder
The magazine feeders are excellent solutions for handling integrated circuits, as the integrated circuits are already shipped in tubes which can be used for feeding purposes.

## Slide 23: Sliding chain conveyor
Conveyors are used for transport of parts, assemblies or pallets between the robot cells. The simplest conveyor makes use of a plastic or metal chain which is pushing the pallets along a metal guide.

## Slide 24: Belt conveyor
With the belt-driven conveyor, the upper part of the belt is driving pallets or other objects or material.

## Slide 25: Conveyor with rollers
The advantage of the conveyors with rollers is in low collision forces occurring between the pallets or objects handled by the conveyor.