## Slide 1: SAFETY IN INDUSTRIAL ROBOTICS
R. Kamnik, T. Bajd and M. Mihelj

## Slide 2: Industrial robot
Definition: Industrial robot is position controlled, reprogrammable and multifunctional device capable of moving along several degrees of freedom in 3-D space.
Applications: Manipulation of material, workpieces and tools in performing various tasks and programmed moves.

## Slide 3: Robot configurations
SCARA
ANTHROPOMORPHIC
CARTEZIAN

## Slide 4: Different aspects of robots implementation
Increasing of safety Instead of human, robots perform dangerous and potentially harmful operations
Deterioration of safety Hazardous situations in robot operation (fast moves and fast change of configuration)

## Slide 5: Three basic hazards associated with robots
Hazard of impact
Hazard of trapping
Other hazards (application specific: electric shock, burns, radiation, …) while - programming a robot - servicing a robot - functioning a robot, when the human worker is inside the robot workspace

## Slide 6: Potential causes of hazards
Control errors (software errors, errors in data transfer, faults in electrical, pneumatic or hydraulic control modules)
Mechanical failures (tool tolerances, mechanical incompatibility, overloading, corrosion, fatigue, lack of maintenance)
Environmental sources (fumes, arc flash, flying particles, radiation, laser beam)
Dangerous peripheral devices (machine centers, conveyors, machine tools, presses)
Human errors (during programming, maintenance, teaching, servicing due to over familiarity or lack of knowledge.)
“Most of the accidents occurred when the robot started to operate without the victim’s knowledge, who had entered the danger area with little concern since the robot was idle.” from Robot Safety, Industrial Welfare Division, Wellington, 1987.

## Slide 7: Requirements of the machinery directives 98/37/EC and 2006/42/EC
A machine is considered to be the sum total of interlinked parts or devices, of which at least one part or device can move and correspondingly has a function.
Basic safety measure: prevention of physical access into danger zone (every potentially dangerous part securely fenced)

## Slide 8: Safety Requirements for Robots and Robot Systems
Large surrounding area can be potentially dangerous
(within the range of robot arm’s reach and wider)
A whole robot cell must be built according to directives for safety requirements of machinery

## Slide 9: Safety Requirements for Robots and Robot Systems - Standardization
Demand for a safety standard containing instructions for safe design:
Provision of hazard lists and measures to reduce risks
Definition of limits for allowed contact forces and impacts
Requirements for control system performance (safety level)
Definition of validation methods

## Slide 10: Safety Requirements for Robots and Robot Systems - Standards
ANSI/RIA R15.06-1999
Industrial Robots and Robot Systems –
Safety Requirements
Robotic Industries Association
ANSI/RIA/ISO 10218-1-2007
Robots for industrial environments –
Safety requirement
(programmable constrains in joints, cooperative robots, synchronous motion)
Practical guidelines for safety analysis and safety assurance

## Slide 11: Basic safety measures in normal operating mode
Prevention of manual or physical access to areas which are hazardous as a result of automatic movements of robot, tools and peripheral equipment
Protection from flying workpieces or release of energy from tools or periphery
Redundant and diverse layout of electro-mechanical control systems including test circuits (emergency stop switches)
Redundant and diverse set-up of microprocessor control systems

## Slide 12: Safety assurance at the level of hardware
Level 1: Physical guarding of workcell – prevention of physical access and prevention of any release of energy
Barrier with interlocked access gate
Barrier with rotary table

## Slide 13: Safety assurance at the level of hardware
Level 2: Sensing of human presence within the workcell (optical and electronic sensors)

## Slide 14: Safety assurance at the level of hardware
Level 3: protection of human in immediate proximity to the robot arm (optical sensors, force sensor, collision detection)
- > recognition of presence and switching to safe state

## Slide 15: Optical sensors with programmable areas of action
Stop motion range
Warning range
Measurement range
angle and distance
RS4- 4
Stop motion range
Measurement range
Warning range

## Slide 16: Safety measures in special operating modes (setting up, programming)
Only controllable and manageable movements are allowed:
  motion with reduced speed and only as long as instructed
  fail-safe state monitoring (emergency stop buttons)
  acknowledgeable controls (three state, i.e. dead-man switch)
  programmable limitations of robot workspace

## Slide 17: Safety assurance during programming and teaching of motion trajectory
Thoroughly trained operator.
Awareness of dangers and precautions.
Slow motion mode during teaching.
Immediate and easy access to an emergency stop button.
Operator should stand on position which is safe and allows good observation of operation.
An additional observer outside operation area.
Protective clothing and equipment (helmet).
Constant acknowledgement of motion via “dead man switch” at teach box.

## Slide 18: Good luck with working with robots!