## Slide 1: GEOMETRIC DESCRIPTION OF THE ROBOT MECHANISM
T. Bajd and M. Mihelj

## Slide 2: Robot mechanism with coordinate frames
The geometric description of the robot mechanism is based on the usage of translational and rotational homogenous transformation matrices. A coordinate frame is attached to the robot base and to each segment of the mechanism.
Vector expressed in one of the frames can be transformed into another frame by successive multiplication of intermediate transformation matrices.

## Slide 3: Vector parameters of kinematic pair
Vector parameters for geometric description of a robot mechanism.
Consider only mechanisms with parallel or perpendicular consecutive joint axes.
Segments i−1 and i connected by joint i including both translation and rotation.
Relative pose of the joint determined by the segment vector bi−1 and unit joint vector ei
Segment i can be
  translated along the vector ei for the distance di and
  rotated around ei for the angle ϑi.

## Slide 4: Geometric relations and relative displacement
ei – unit vector describing either the axis of rotation or direction of translation in the joint i and is expressed as one of the axes of the xi, yi, zi frame
bi−1 – segment vector describing the segment i−1 expressed in the xi−1, yi−1, zi−1 frame
ϑi – rotational variable representing the angle measured around the ei axis in the plane which is perpendicular to ei (the angle is zero when the kinematic pair is in the initial position);
di – translational variable representing the distance measured along the direction of ei (the distance equals zero when the kinematic pair is in the initial position).

## Slide 5: Rotational and translational joint
Rotational joint
  variable is angle ϑi,
  while di = 0
Translational joint
  variable is displacement di,
  while ϑi = 0
In initial pose
  joint angle equals zero, ϑi = 0
  joint displacement equals zero, di = 0
  and the coordinate frames xi, yi, zi and xi−1, yi−1, zi−1 are parallel.

## Slide 6: Joint transformation matrices
joint axis aligned with xi
joint axis aligned with yi
joint axis aligned with zi
without joint

## Slide 7: Vector parameters in four steps
STEP 1
  robot mechanism is placed into the desired initial (reference) pose;
  joint axes must be parallel to one of the axes of the reference coordinate frame x0, y0, z0;
  in the reference pose all values of joint variables equal zero, ϑi = 0 and di = 0, i = 1,2, ...,n;
STEP 2
  centers of the joints i=1,2, ...,n are selected;
  center of joint i can be anywhere along the corresponding joint axis;
  local coordinate frame xi, yi, zi is placed into the joint center in such a way that its axes are parallel to the axes of the reference frame x0, y0, z0;
  local coordinate frame xi, yi, zi is displaced together with the segment i;
STEP 3
  unit joint vector ei is allocated to each joint axis i = 1,2, ...,n;
  it is directed along one of the axes of the coordinate frame xi, yi, zi;
  in the direction of this vector the translational variable di is measured, while the rotational variable ϑi is assessed around the joint vector ei;
STEP 4
  segment vectors bi−1 are drawn between the origins of the xi, yi, zi frames, i = 1,2, ...,n;
  segment vector bn connects the origin of the xn, yn, zn frame with the robot end-point.

## Slide 8: Mechanism with four degrees of freedom
Reference pose

## Slide 9: Vector parameters and joint variables

## Slide 10: Vector parameters and joint variables

## Slide 11: Joint transformation matrices
Joint 1
Joint 2
Joint 3
Joint 4
Constant matrix

## Slide 12: SCARA robot mechanism
Reference pose
Vector parameters

## Slide 13: Vector parameters and joint variables

## Slide 14: Joint transformation matrices
Joint 1
Joint 2
Joint 3