## Slide 1: INVERSE GEOMETRY AND WORKSPACE OF ROBOT MECHANISMS
T. Bajd and M. Mihelj

## Slide 2: Triangle
Triangle plays an important role in Euclidean geometry.

## Slide 3: Triangle
Triangle plays an important role in geometry of robot mechanisms.

## Slide 4: Two-segment planar robot
When solving the inverse geometry of robot, we calculate the joint angles and from the known position of the robot end-point .

## Slide 5: Two-segment planar robot
The angle in the second joint of the two-segment robot is calculated by the use of the law of cosines.

## Slide 6: Two-segment planar robot
The angle in the first joint is calculated as the difference of the angles and .

## Slide 7: Two-segment planar robot
When calculating the joint angles we have two
configurations, „elbow-up“ and „elbow-down“.

## Slide 8: Three-segment planar robot
When solving the inverse geometry of robot, we calculate the internal coordinates from the known position and orientation of the end-effector.

## Slide 9: Three-segment planar robot
While defining the two solutions for the second joint angle are obtained by the law of cosines.

## Slide 10: Three-segment planar robot
The solutions for the angle in the first joint are obtained by law of cosines. They depend on the selected solution for the second joint angle

## Slide 11: Three-segment planar robot
Usually there exist two configurations. When the second joint is extended (), only single solution exists. When and , there is infinite number of configurations.

## Slide 12: Two-dimensional robot workspace
The workspace of a robot mechanism is the spatial volume which is reachable by its end-point.

## Slide 13: Two-dimensional robot workspace
The workspace of a robot mechanism depends on the number of degrees of freedom, their arrangement, the lengths of the segments and constraints in the motion of particular joint coordinates.

## Slide 14: Two-dimensional robot workspace
The reachable workspace of a planar mechanism with two rotational joints (2R) is determined with arc which is expanded around the first rotational axis along the arc .

## Slide 15: Workspace of 2R robot mechanism
The work space can be described by a mesh of two types of circles. The circles depending on the angle have their radii of equal length while their centers travel around the origin of the coordinate frame. The circles depending on angle have all their centers in the origin of the frame, while their radii depend on the lengths of both segments and the angle between them.

## Slide 16: Workspace of 2R robot mechanism
The shape of workspace is presented for
and
The area of the workspace can be replaced by the area of a corresponding sector of a ring.

## Slide 17: Workspace of 2R robot mechanism
Different values of the working areas are obtained for equal ranges of the angle and for .

## Slide 18: Workspace of 2R robot mechanism
The largest working area of the 2R mechanism occurs for equal lengths of both segments.

## Slide 19: Workspace of 3R planar robot mechanism
The reachable robot workspace represents all the points that can be reached by the robot end-point. The dexterous workspace comprises all the points that can be reached with an arbitrary orientation of the robot end-effector.

## Slide 20: Three-dimensional robot workspace
When adding translation to 2T mechanism, the Cartesian mechanism is obtained. When adding rotation to 2T mechanism, the cylindrical mechanism is obtained.

## Slide 21: Three-dimensional robot workspace
When adding translation to RT mechanism, the cylindrical mechanism is obtained. When adding rotation to RT mechanism, the spherical mechanism is obtained.

## Slide 22: Three-dimensional robot workspace
When adding translation to RR mechanism, the so called SCARA mechanism is obtained. When adding rotation to RR mechanism, the anthropomorphic mechanism is obtained.

## Slide 23: Robot workspace
The robot manufacturer is required to clearly show the maximal reachable workspace of an industrial robot in at least two planes.

## Slide 24: Robot workspace
Robot workspace plays an important role when selecting an industrial robot for an anticipated task.