## Slide 1: ROBOT ASSEMBLY
T. Bajd and M. Mihelj

## Slide 2: Robot assembly
The knowledge on robot assembly is important when planning an intelligent control of a robot assembly cell, usually comprising robot vision, force control and special gripper.
The knowledge can be usfully applied when designing a product which is not to be only functional and aesthetic, but also convenient for simple and economic assembly.

## Slide 3: Robot assembly
Mechanical assembly – stable composition of interconnected parts
Part – rigid body which does not change its shape during the assembly process
Stable mechanical assembly – connections between the parts are plane contacts
Subassembly – stable subset of interconnected parts
Functionality of subassembly – two parts can only be joined in a unique way
3 DOF
2 DOF
1 DOF
0 DOF

## Slide 4: Graph of connections
The parts belong to the nodes of the graph:
P = {p1, p2, … pN}
The connections correspond to the edges of the graph:
C = {c1, c2, … cL}
The connection c1 has 3 DOF,
c2 – 0 DOF, c3 – 2 DOF, c4 – 3 DOF and c5 – 0 DOF. The connection of the cup and bottom is not functional.

## Slide 5: Assembly sequence
First screw the cup to the receptacle
Second insert the stick into receptacle
Finally screw the bottom to the subassembly of the receptacle, stick, and cup

## Slide 6: Ordered list of assembly tasks
({{Cup}, {Receptacle}},
{{Cup, Receptacle}, {Stick}},
{{Cup, Receptacle, Stick}, {Bottom}})
Number of
elements N - 1
}

## Slide 7: Ordered list of binary vectors
([F, F, F, F, F],
[F, T, F, F, F],
[T, T, T, F, F],
[T, T, T, T, T])
Number of
elements N
}
T – connection is
established
F – connection is not
established
[c1, c2, c3, c4, c5],

## Slide 8: Ordered list of assembly states
({{Cup}, {Receptacle}, {Stick}, {Bottom}},
{{Cup, Receptacle}, {Stick}, {Bottom}},
{{Cup, Receptacle, Stick}, {Bottom}},
{{Cup, Receptacle, Stick, Bottom}})
Number of
elements N
}

## Slide 9: Ordered list of connections
({c2},
{c1, c3},
{c4, c5})
Number of elements N-1
}

## Slide 10: Directed graph of assembly sequences
The directed graph represents all the sequences for a mechanical assembly. The nodes are stable assembly states, while the edges belong to the connections.
Each path between
the initial and final state corresponds to a feasible assembly sequence.

## Slide 11: Car automatic transmission system
The mechanical assembly consists from 11 parts. The corresponding graph of connections has 18 possible connections or assembly tasks.

## Slide 12: Car automatic transmission system
The nodes of the graph are described by binary vectors. Different assembly costs can be assigned to the edges of the directed graph. The assemblies with a larger number of DOF are less stable and should be avoided, when searching for more advantageous assembly sequences.

## Slide 13: AND/OR graph
The AND/OR graph represents the set of all possible assembly sequences. The nodes represent the subassemblies. The arcs are feasible assembly tasks. The solutions of the AND/OR graph are feasible subassembly trees.

## Slide 14: AND/OR graph
The main advantage of the AND/OR graph is to show explicitely the possibility of simultaneous execution of assembly tasks.
Subassembly tree corresponding to first assembly sequence.
Subassembly tree corresponding to the sixth and seventh assembly sequence.

## Slide 15: Strongly and weakly connected mechanical assemblies
Strongly connected assembly – every part is connected to every other part
Weakly connected assembly – there are N – 1 connections between N parts
Mechanical assembly of 10 parts
Directed graph: 115975 nodes
AND/OR graph: 1023 nodes
Directed graph: 512 nodes
AND/OR graph: 55 nodes
Strongly connected assembly
Weakly connected assembly