## Slide 1: STANDARDS IN ROBOTICS
T. Bajd and M. Mihelj

## Slide 2: Coordinate frames of robot manipulator
World frame is defined by the user. The axis is in the opposite direction of gravity. Base frame is defined by manufacturer. Positive axis is pointing perpendicularly from the base. Mechanical interface frame is placed into robot palm connecting robot arm with the gripper. Positive axis points perpendicularly away from the interface.

## Slide 3: Testing of industrial robot manipulators
The tests are performed during the robot acceptance phase or in various periods of robot usage in order to check the accuracy and repeatability of robot motions. In point-to-point robot tasks the following performance parameters are assessed according to the ISO 9283 standards:
pose accuracy and repeatability
distance accuracy and repeatability
drift of the pose accuracy and repeatability
pose stabilization time
pose overshoot

## Slide 4: Measurements of accuracy and repeatability
The measurements must be performed in five points, located in a plane, which is placed diagonally inside a cube. The test must be executed with maximal load and maximal velocity. When testing accuracy and repeatability 30 cycles must be performed.

## Slide 5: Measurements of accuracy and repeatability
Contactless optical measuring methods are recommended.

## Slide 6: Measurements of accuracy and repeatability
The reasons for deviations between the command (desired) and attained (actual) pose are: errors caused by the control algorithm, coordinate transformation errors, differences between dimensions of robot and its model, mechanical faults (e.g. hysteresis or friction) and external influences (e.g. temperature).

## Slide 7: Measurements of accuracy and repeatability
The standard defines the course of measurements. The robot starts from point . Each point is always reached from the same direction.

## Slide 8: Position accuracy
Position accuracy is determined by the distance between the command position and the barymeter of the cluster of attained positions .

## Slide 9: Drift of position accuracy
The robot is cyclically displaced between points and for 8 hours.

## Slide 10: Orientation accuracy (about z axis)
The orientation accuracy is the difference between the commanded angular orientation and the average of the attained angular orientations .

## Slide 11: Position repeatability
The position repeatability is determined by radius of the sphere where the center is the cluster barycenter.

## Slide 12: Drift of position repeatability
The robot is cyclically displaced between points and for 8 hours.

## Slide 13: Orientation repeatability (about z axis)
The orientation repeatability expresses how dispersed are the 30 attained angles around their average for the same command angle.

## Slide 14: Distance accuracy and repeatability
Distance accuracy
Distance repeatability
pair of desired positions
pair of attained positions

## Slide 15: Position stabilization time
It is measured as the elapsed time from the instance of the initial crossing into the limit band until the instance when the robot remains within the limit band. The limit band is defined as the repeatability or a value stated by the manufacturer.

## Slide 16: Overshoot
It is measured as the maximum distance from the attained position after the instance of the initial crossing into the limit band and when the robot goes outside the limit band again.