## Slide 1: Magnetic and Acceleration Sensor for Detecting Direction/Motion
AMO SENSE
World Best, High Performance

## Slide 2: Contents
Sensor Application
Introduction of Company and Business Division
Structure of Sensor
Feature of Sensor
Influence on Magnetic field inside device
Product
Road-Map
Application Function
Summary for Phone Application
Current version to use
Important Point of Magnetic Sensor
Our Solution
Our Advantage
Comparison with Competitor

## Slide 3
Sensor Application
3D Device
Robot
RC
Sport
Phone
Automotive

## Slide 4: Introduction of Company and Business Division
Name: Amotech Co., Ltd
Founded: October 19th, 1994
Turnover: USD60 Million (2008)
Employee: 500 (in Korea)
2003 Listed on KOSDAQ
Main Product
EMI/ESD Components
Microwave Components
BLDC Motor
Direction/Motion Sensor
Power LED
Amorphous Core
Nano Filter/Ribbon Heater
Main Customer: Sensor Division
S-Corp. (Korea), P-Corp. (EU)
G-Corp. (USA), K-Corp. (Japan)
and so on
AmoSENSE Division
- 2002 : Started a magnetic sensor taking
over a company of Japan
- 2003 : Extended to convergence sensor
included accelerometer and
strengthened Software division
- 2005 : Application Program
 Constellation Searching
- 2006 : Facility for M/P (Capa: 300K/M)
- 2007 : Application Program
 Pedometer
- 2008 : Moved to New plant and
increased Capability (1KK/M)
- 2009 : Application Program
 Pointer/3D Remote Controller

## Slide 5: Structure of Sensor
Analog Circuit
for
Sensor Device
Control Logics
DAC
Sensing Element
Mag. X,Y,Z-axis
ADC
Package to be composed on 3-axis
magnetic element and ASIC
Operation all algorithm in Host CPU
Model : AMS0303H (3.2 x 3.2 x 1.1)
1
2
【 Embedded MCU ASIC Part 】
- Converts the values detected from geomagnetic
and acceleration elements into electric signal by
ADC/DAC
- Performs various functions by embedded special
algorithm in MCU
【 Geomagnetic Part 】
- Composed on X, Y and
Z-axis
【 Acceleration Part 】
- Composed on X, Y and
Z-axis
1
2
3
Analog Circuit
for
Sensor Device
Control Logics
DAC
ADC
1
3
Sensing Element
Accel. X,Y,Z-axis
2
embedded MCU
【 ASIC Part 】
- Converts the values detected from
geomagnetic and acceleration elements
into electric signal by ADC
- Performs order for exact calibration by
DAC
【 Geomagnetic Part 】
- Composed on X, Y and Z-axis
1
2
Package to be composed 3-axis magnetic,
acceleration elements, ASIC and MCU
Operation almost algorithm in built-in MCU
Model : iM-3502 (5.0 x 5.0 x 1.2)
3-axis Magnetic Field Sensor
6-axis Motion Sensor
Sensing Element
Mag. X,Y,Z-axis

## Slide 6: Feature of Sensor
3-axis accelerometer + 3-axis magnetic sensor + u-Processor
Package: 4.5x4.5x1.2mm, LGA, Lead Free, Halogen Free
Embedded micro-processor
- 16KB Flash, 20MIPS, 2KB SRAM, Watchdog
Built-in software: Calibration free
(1) iRAC (Intelligent Real time Automatic Calibration)
- Automatic Offset and Tilt (Roll/Pitch) Compensation
- Automatic Calibration for Magnetic field Disturbance
(2) User application software (if required)
Serial interface: I2C, SPI
Wide Magnetic Measurable Range: ± 10Gauss, appropriate for mobile phone
Minimum Measurable Magnetic field: 10nT (0.1mGuass)
Maximum sampling rate : 50Hz~200Hz
Azimuth & Roll/Pitch Resolution: 1o(degree)
Interface Voltage: 1.6Volt ∼ 5.0Volt
Low power: Adjustable by changing clock frequency & sampling rate
less than 6.5mA in active mode for 6axis, at 10MHz MCU clock
less than 25uA in all power down mode

## Slide 7
‘S’ Corp.’s GT-B2700
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21
1 | 0.104 | 0.02 | -0.088 | -0.232 | -0.292 | -0.166 | 0.05 | 0.248 | 0.326 | 0.32 | 0.308 | 0.284 | 0.8 | 1.2 | 1.5 | 1.3 | 1.7 | 1.3 | 0.248 | 0.26 | 0.242
2 | 0.056 | -0.088 | -0.352 | -0.754 | -0.994 | -0.628 | 0.104 | 0.536 | 0.53 | 0.434 | 0.356 | 3.5 | 3.5 | 2.8 | 3.1 | 2.5 | 2.7 | 3.3 | 1.2 | 0.188 | 0.176
3 | -0.046 | -0.25 | -0.772 | -1.636 | -1.408 | 0.866 | 2.048 | 2.024 | 1.19 | 1.2 | 2 | 5.5 | 5.6 | 5.1 | 5.5 | 5.2 | 5 | 5.4 | 3 | 0.182 | 0.17
4 | -0.076 | -0.328 | -0.898 | -2.536 | 2.612 | 20.426 | 17.834 | 6.398 | 2.51 | 0.728 | 3 | 3.7 | 4.8 | 3.5 | 6.4 | 6.2 | 6.6 | 5.6 | 4.1 | 0.248 | 0.254
5 | -0.022 | -0.238 | -0.76 | -1.516 | 2.732 | 22.7 | 22.244 | 10.112 | 2.552 | 0.914 | 2.1 | 0.53 | 6.1 | 5.1 | 6.3 | 6.2 | 6.4 | 6 | 3.5 | 0.218 | 0.2
6 | 0.002 | -0.136 | -0.346 | -0.16 | 3.686 | 10.94 | 11.6 | 4.976 | 1.676 | 1.01 | 2.6 | 2.1 | 2.6 | 2.5 | 5.7 | 4.9 | 3.6 | 3.4 | 2 | 0.23 | 0.23
7 | 0.062 | -0.01 | -0.01 | 0.29 | 1.43 | 3.386 | 3.41 | 2.15 | 1.232 | 0.836 | 0.59 | 0.41 | 0.272 | 0.188 | 4.5 | 4.2 | 2.3 | 1.5 | 0.218 | 0.194 | 0.2
8 | 0.122 | 0.11 | 0.152 | 0.296 | 0.656 | 1.112 | 1.202 | 0.986 | 0.746 | 0.608 | 0.458 | 0.338 | 0.248 | 0.206 | 1.8 | 1.3 | 0.8 | 0.4 | 0.23 | 0.218 | 0.212
9 | 0.164 | 0.158 | 0.182 | 0.272 | 0.422 | 0.56 | 0.608 | 0.56 | 0.482 | 0.416 | 0.332 | 0.242 | 0.182 | 0.182 | 0.206 | 0.212 | 0.23 | 0.248 | 0.236 | 0.164 | 0.194
Magnetic scan data inside mobile phone
Due to Magnetic parts like Speaker, Vibrator, Battery, Shielding material, etc.
(1) Magnetic field density at most of place inside a mobile phone:
about ± 6 Gauss (stationary field)  Our guarantee range is ±10 Gauss
(2) Very hard to find out the proper place for e-compass on mobile phone
 Magnetic Field Scan Service
Influence on Magnetic field inside device
Wide measurable range: ± 10 Gauss

## Slide 8
Product Specification
Item | 3-axis Geomagnetic Sensor |  | 6-axis Motion Sensor | 
Part No. | AMS0404H | AMS0303H | AMS0805WAH | iM-3502
Azimuth accuracy | ±5˚ | ±5˚ | ±5˚ | ±5˚
Resolution | Below 1˚ | Below 1˚ | Below 1˚ | Below 1˚
Measure range | ±1,000uT | ±1,000uT | ±1,000uT | ±1,000uT
Min. measurable Magnetic flex density | 20nT | 20nT | 20nT | 10nT
ADC/DAC | 10bit/10bit | 10bit/10bit | 10bit/10bit | 10bit/10bit
Response Time | 200Hz | 200Hz | 20Hz ~ 30Hz | 20Hz ~ 30Hz
Operating Volt. | 2.3V ~ 3.6V | 2.3V ~ 3.6V | 2.3V ~ 3.6V | 2.3V ~ 3.6V
Power Consumption | Full: 4.5mA Idle: below 5uA | Full: 4.5mA Idle: below 5uA | Full: 10mA Idle: below20uA | Full: 6.5mA Idle: below 5uA
Output format | I2C/SPI | I2C/SPI | I2C/SPI | I2C/SPI
Operating Temp. | - 30℃ ~ +85℃ | - 30℃ ~ +85℃ | - 20℃ ~ +85℃ | - 30℃ ~ +85℃
Tilt compensation Range | - | - | -89˚ ~ +89˚ | -89˚ ~ +89˚
Tilt resolution | - | - | Below 1˚ | Below 1˚
ESD(HBM) | 2,000V | 2,000V | 2,000V | 2,000V
Chip size(mm) | 4.0 x 4.0 x 1.0 | 3.0 x 3.0 x 1.1 | 7.0 x 9.0 x 1.2 | 5.0 x 5.0 x 1.2
Algorithm (iRAC) | Provide as Library | Provide as Library | Embedded | Embedded

## Slide 9
AMS0805H
Size: 5.0 x 5.0
Without MCU
AMS0303H
Size: 3.2 x 3.2
Without MCU
E-Compass
iM-3501/2
Size: 5.0 x 5.0
With MCU
iA-5351
Size: 3.5 x 3.5
(Acc.+Gyro)
aM-3300
Size: 2.5 x 2.5
With MCU
AMS0805WAH
Size: 7.0 x 9.0
With MCU
6-axis Motion
Sensor
iM-9551
(Acc+Mag+Gyro)
USB, RS232
iM-9351
Size: 4.5 x 4.5
(Mag + Acc + Gyro)
9-axis Motion
Sensor
Road-Map
Next
Inertial Motion
Sensor
iA-4351
Size: 3.5 x 3.5
(3-axis Gyro)
AMS0404H
Size: 4.0 x 4.0
Without MCU
aH-1200
Size: 2.0 x 2.0
Without MCU
Plan
Current / New
iM-3452
Size: 4.5 x 4.5
With MCU

## Slide 10: Application Function (I) : Geomagnetic Point
Implement exact direction under tilt condition as well as horizontal
▷ Phone, Radar Detector, Sport watch, Binocular …
Searches the position with the data from sensor with GPS signal
▷ Pedestrian Navigation Phone, PND …
Dead-Reckoning
Heading-Up
Auto-scroll the Map detecting direction
▷ Pedestrian Navigation Phone …
E-Compass

## Slide 11
Possible to control various function with special gesture to use motion or impact
- To transmit urgent message under
the emergency situation by impact
- To know the situation at nurse desk
when patient falls down in hospital
- To check the status of device whether
dropped or no
▷ Phone, Medical suppliers …
Managed the walking, running step and Calorie consumption with Program
▷ Phone, Pedometer, Running Shoes …
Health Management
Various UI
3-Dimension game like Gun, Car using the motion
(YAW/PITCH/ROLL)
▷ Phone, Hand-held Game Device, Joystick, Remote presenter …
3D Motion
Application Function (II) : Acceleration Point

## Slide 12
If you have the concept to use accelerometer and magnetic sensor ?
 Possible to perform 『constellation search』 without additional cost
E-Compass
Perform the compass function
to use azimuth of magnetic sensor
Heading
(Navigation Compass)
Constellation Search
Pedometer
Air Mouse / 3D Game
Application S/W
HOT
Working together acceleration sensor
Calibrate the tilt to utilize data
from accelerometer
Possible to perform for only
functions of accelerometer
regardless of magnetic sensor
Basic
Use to scroll the map toward
advance direction automatically
based on all moving
Summary for Phone Application
To differentiate from current version creating new functions
To increase of commodity value to add several functions with minimum cost

## Slide 13: Application S/W
S/W to utilize exercise for
「working and running」
 Increase the effect in case
of including management
program
Pedometer
Constellation Search
 Low consumption current
and Accuracy
 Patent and Accuracy
3D Motion
Moving of Up/Down
Moving of
Right/Left
Moving of horizontality
S/W of 3D Motion for Air
Mouse, 3D Game and so on
PITCH
YAW
ROLL
【 Display Items 】
- Exercise Time
- Calorie Consumption
- Moved distance and
velocity
- Walking/Running
step number
- Speed: Average velocity
for 5 seconds
- Pace: Time to go 1Km
with current speed
S/W to search the direction
and position with the device
 Support with game
development engineer
and Accuracy

## Slide 14
Convergence Package
(Magnetic + Acceleration)
Separate Package
(Magnetic + Acceleration)
Data output regardless of OS and Chipset
No relation to Computing Power of Host CPU
Possibility to control data output and power current
Excellent accuracy under general environment
 Performance of stable Application
Debugging number is a few  Keep development period
+ +
MCU
Current version’Type
Convergence Version
Discrete Version
1-Chip
Point

## Slide 15: Important points for Magnetic sensor
Disturbance by magnetic components like Speaker, Vibrator and Battery
* It comes out errors whenever over 0.6Gauss is detected around sensor
 It is important to interfere from circumference outside, but it is very serious
to affect from some devices in the mobile phone like Speaker, Vibrator and Battery
Disturbance by sudden current flow
* Sudden high current flow like LED ON of Keypad and call receiving affects the
performance of magnetic sensor
 Magnetic sensor has to put it in suitable place considering all power lines in dev
Operating to cover geo-magnetic absorption by Soft-iron
* Building inside made by H-beam and in the car
 It is not operated magnetic sensor
Error due to other factors
- Altered the sensitivity of each axis due to temperature change
- Alignment problem due to assembly tolerance : Mounted in NOT perfect alignment
- Error due to tilt motion

## Slide 16
iRAC (Intelligent Real time Automatic Calibration)
We developed special algorithm to solve several problems and it is built in the MCU of
sensor inside.
The algorithm is automatically operated the functions as follows:
Output the signal to display current status of magnetic field
We provide a convenience system to check current magnetic status of mobile phone.
Phone Consumers can check it with phone screen in person whether phone is calibrated or not.
Calculated and calibrated DATA is outputted
Our sensor is outputted the data calculated and calibrated by algorithm together.
Customers can be used for the data considering application functions
Automatic
Offset
Compensation
Automatic
Calibration for Magnetic
field disturbance
Automatic
Temp/Sensitivity/Tilt
Calibration
Our Solution

## Slide 17
Service application S/W, which competitors don’t provide
 It can increase commodity value of device to some applications under the same cost
* Proving the solutions to operate the applications regardless of OS
Excellent performance comparing with competitors
- Minimize the errors under area like inside and surrounding building
 It can get complain from users because the errors connect to display
Keep key patents
- Patent hold : Published(39), issued (20)
- 3-axis magnetic field sensor + 3-axis acceleration sensor
=> 6-axis motion sensor (No.: US 6,536,12)
- 6-axis motion sensor with Mobile Phone (No.: JPN 4034039)
- Calorie Counter (No.: KR10-0665730)
- Constellation Search (No.: PCT KR2005/003240)
Our Advantage
3-axis Magnetic Field Sensor
+ Constellation Search S/W
6-axis Motion Sensor
+ Pedometer S/W
6-axis Motion Sensor
+ 3D Motion S/W
6-axis Motion Sensor
+ Constellation Search S/W

## Slide 18
Item |  | Amotech’s AMS0303H | A-Company’s AK-8973X | Remark
Size |  | 3.2 x 3.2 x 1.1 | 2.5 x 2.5 x 0.5 | AKM is smaller than us about 1.6 times
Accuracy of Azimuth |  | ±5˚ | ±5˚ | AKM is appeared about 1o of error under earth magnetic field, but about over 5o of error under bad magnetic environment  It can get the complain from users if device’ engineer doesn’t reduce the error because basic environment is all area.
Resolution | 0.5 G (Earth magnetic field) | 0.23o | 1.17o | 
 | 0.4 G (Earth magnetic field) | 0.29 o | 1.47o | 
 | 0.2 G (Surrounding building) | 0.58 o | 3.01o | 
 | 0.1 G (Inside bridge) | 1.17 o | 6.34o | 
Magnetic measurement Range | Guarantee | ±1,000uT (10G) | ±800uT (8G) | AKM is designed 20G, but guarantee is 8G  The range is higher, stable data output
 | Minimum | 20nT (0.1mG) | 200nT (2mG) | 
Sensitivity (Under Normal magnetic field ) |  | 500 Count/Gauss | 100 Count/Gauss | We are better than AKM about 5 times  Sensitivity is better, stable data output
Output range under Earth magnetic field (30uT) |  | 60 count | 30 count | 
Response Time (including algorithm) |  | 30Hz~50Hz | 20Hz~40Hz | 
ADC/DAC |  | 10bit/10bit | 8bit/8bit | 
Power consumption current |  | 4.0mA | 6.8mA | We are lower than AKM about 1.5 times
Comparison with Competitor

## Slide 19
THANK YOU!